## Slide 1
SBG-1000 SRN for 1.0Au
ES R&D) iPECS LIK team
10 Apr 2012

## Slide 2
Version History
Version | Release Date | Base LIK | Description
A.0Am | 2011.04.25 | 5.5Cj | DECT S/W QE passed
A.0An | 2011.05.12 | E.5Da | DECT F/T QA passed
A.0Ao | 2011.06.17 | E.5De | PSTN 4 F/T QA trial
1.0As | 2011.08.16 | E.5Eb | PSTN 4 MP QA passed
1.0At | 2011.12.08 | E.5Gg | MP QA
A.0Au | 2012.03.02 | E.5Go | Temporary for F/T & IRs
1.0Au | 2012.04.10 | E.5Gp | MP QA

## Slide 3
SBG-1000 A.0Am
ES R&D) LIK team
25 Apr 2011

## Slide 4
Capacity
Capacity Lock Key is added
DECT | Lock Key | VoIP | Station
Disable |  | 3 | 12
 | Extended | 6 | 24
Enable |  | 3 | 12
 | Extended | 4 | 24
  Remove R1141 on the bottom side PCB near U17 CPLD
  Hardware Version will be shown as “05” not “01”.
  Contact to myoungsup.shin@lgericsson.com for the detail.
H/W ECO should be applied to the old H/W without DECT
from A.0Am

## Slide 5
Nation Code and DECT Usage
Nation Code can be modified in Web GUI
DECT Usage is added
Nation Code and DECT Usage can be modified
only right after Restore Factory Settings.
If Nation Code or DECT Usage is modified,
SBG will be restarted and all Voice DB will be initialized.
Nation Code and DECT Usage can be modified
only right after Restore Factory Settings.
If Nation Code or DECT Usage is modified,
SBG will be restarted and all Voice DB will be initialized.
from A.0Am

## Slide 6
Added Feature - I
Language Selection is added
Web Phone is added
Language Selection and Web Phone are added
from A.0Am

## Slide 7
Summary page is added
Added Feature - II
from A.0Am

## Slide 8
DECT Registration is added
Added Feature - III
from A.0Am

## Slide 9
CODEC Priority and Fail Over are added
Added Feature - IV
Default CODEC Priority when all “none”
g.711-u > g.711-a > g.723 > g.729 > g.729a
If
Fail Over Usage set to “ON”
No Response Time to Fail Over has 3 ~ 10 seconds
Fail Over CO Group Number has 1 ~ 5 CO Group
then SIP Call Fail Over to PSTN Backup CO Group
after No Response Time
directly when WAN link fault
from A.0Am

## Slide 10
Networking Admin is added
Added Feature - V
from A.0Am

## Slide 11
Mobile Extension is added
Added Feature - VI
from A.0Am

## Slide 12
IPCR is added
Added Feature - VII
Automatic Talk Recording Destination is added in Voice Config > Station Data > Common Attributes for IPCR
from A.0Am

## Slide 13
Network, EZ ATTD, CTI(TAPI), Web Phone, CAPACITY, IPCR Lock Keys are added
Lock Key added
from A.0Am

## Slide 14
SBG-1000 A.0An
ES R&D) LIK team
12 May 2011

## Slide 15
DB Incompatibility
Maximum CO increases from 8 to 10 in order to support PSTN 4 option boards (4 FXO / 2 BRI )
Restore Factory Settings SHOULD be applied by web admin or “Reset to defaults” button after upgrade
  If H/W with DECT, DECT PARK code SHOULD be memorized before upgrade and SHOULD be set after upgrade.
    Attendant LIP
      PGM+0+#+Flex4 : Display PARK code
      PGM+0+#+Flex6 : Set PARK code
    WBM
      Services > Voice Install > Station Registration > DECT Registration
  After re-program PARK code, Reboot to apply new PARK code.
from A.0An
 | ~ A.0Am | A.0An ~
Max. VOIP | 6 | 6
Max. PSTN | 2 | 4
Total Max. CO | 8 | 10

## Slide 16
SBG-1000 A.0Ao
ES R&D) LIK team
16 Jun 2011

## Slide 17
Support PSTN 4 option boards
PSTN 4 option boards are supported with new H/W
  Hardware Version XXE means “Enhanced” new H/W.
  Only new H/W can support PSTN 4 option boards
from A.0Ao
Option Board | Resources
CIU4 | FXO 4
BRIU2 | BRI 2

## Slide 18
Numbering Plan
Services > Voice Install > System > Identification
Two type of Numbering Plan
from A.0Ao
Normal | Networking
Networking Numbering Plan starts with * or # for the sake of convenient voice networking

## Slide 19
Authorization Code
Services > Voice Config > Station Data > Authorization Code & COS
Services > Voice Config > System Data > System Attributes
from A.0Ao
100 System Authorization codes can be programmed
If it has “ON”,
Forced Account Code is activated and User should enter the authorization codes for outgoing CO call.

## Slide 20
SBG-1000 1.0As
ES R&D) LIK team
12 Aug 2011

## Slide 21
Support LIP-8002E
LIP-8002E
  New Entry Level LIP based on IPKTS protocol
  Same H/W with LIP-8002 using SIP, but different button silk
from 1.0As
Dial By Name
Call Log
Message Wait LED
In OFF-HOOK state,
DND button is used as FWD button

## Slide 22
Station VM Attributes
Services > Voice Config > Station Data > Station VM Attributes
For Enhanced VM features as LIK 5.5
from 1.0As

## Slide 23
USB Upgrade
F/W (GS87MXXXX.rom) should be in the top directory of USB memory.
from 1.0As
[5] REC. VSF ANNCEMENT
[9] USB UPGRADE
Press PGM + 0 + 9 in Attendant
Press Number to View File
Browse with Vol▲▼ and Press Save
Selected file is copied from USB to Memory
F/W is burned onto NAND file system
Press Save to Restart
SBG will Reboot
ROM FILE NUM: TOTAL 8
PRESS 0-7 TO VIEW FILE
7 : GS87MX0Yz.rom
PRESS [SAVE] TO UPGRADE
7 : GS87MX0Yz.rom
COPY IN PROGRESS
7 : GS87MX0Yz.rom
BURNING IN PROGRESS
7 : GS87MX0Yz.rom
PRESS [SAVE] TO RESTART
7 : GS87MX0Yz.rom
RESTARTING......

## Slide 24
Added & Fixed
from 1.0As
Added
  Services > Voice Config > System Data > System Attributes
Fixed
  Internet Connectivity Test
    Under some ADSL routers which cannot support ping to the public site, this test always fails.
    If ping fails, TCP connection method is used for this test.
For the enhanced security,
if it has “ON”, # should be entered after System Auth Code.
If it has “ON”, Enhanced VM feature is available.
If it has “ON”, WAN Fault Alarm will not be notified on Attendant.

## Slide 25
SBG-1000 1.0At
ES R&D) LIK team
8 Dec 2011

## Slide 26
COS 1~7
COS expanded from 4 to 7
Allow/Deny C Toll Exception Table added
from 1.0At

## Slide 27
SIP & MSN 24 IDs
SIP User IDs and MSN IDs are increased to 24 IDs
from 1.0At
“UnRegister” added

## Slide 28
Added Features – I
CO GW Order is added for PSTN or ISDN user.
from 1.0At

## Slide 29
Added Features – II
Executive / Secretary is added
from 1.0At

## Slide 30
Fixed
Ez ATTD
  Ez ATTD interworking bug is fixed.
  Ez ATTD can support SBG-1000 from XC.7Ah version.
PPPoE
  Voice mute using PPPoE WAN interface is fixed.
DB Download
  Only compressed DB can be downloaded for security reason.
from 1.0At

## Slide 31
SBG-1000 A.0Au
ES R&D) iPECS LIK team
2 Mar 2012

## Slide 32
Added Features – I
Soft Switch Type & IP AUTH USAGE added
Emergency Call ATD Notify added
from A.0Au
Added in order to support Various Servers easily
For Security Enhancement
[NZ-AGT-12021]
If it is set to “DISABLE”,
ATD will not receive Emergency Call Alarm ring.
[NZ-AGT-12021]
SBG validated with BroadWorks

## Slide 33
Added Features – II
Data(Fax) Station Number added
from A.0Au
Auto FAX Detection [AU-ARI-11147]
- If it has Station Number,
Incoming call initiates FAX tone detection,
if detected, then specified station will ring to answer.

## Slide 34
Fixed IR
NZ-AGT-12021
  Destination in Call Routing by Auto Attendant was not able to change back to N/A
ZA-MAR-12052
  LWS-WK Flexible button LED did not work correctly
NZ-AGT-12030
  Demo Key includes Capacity expansion. After expired, system should be re-configuration.
   Capacity will NOT be expanded by Demo Key.
from A.0Au

## Slide 35
SBG-1000 1.0Au
ES R&D) iPECS LIK team
4 Apr 2012

## Slide 36
Added Features – I
from 1.0Au
Station Group Jump Buttons added

## Slide 37
Added Features – II
from 1.0Au
Paging Access of ALL stations in ONE screen

## Slide 38
Fixed IR
DE-NTP-12019
  Net Station Number type is added in Services > Voice Config > Station Data > Flex Button Assignment menu.
from 1.0Au