## Slide 1
<number>
WANU Overview
March 2011
Notes: <number>

## Slide 2
<number>
Why WANU?
1. Small Size Media Gateways: 6/8/24 channels
 Needs multiple IP addresses when two or more VOIM are installed
or
 Needs the Port Forwarding about Multiple Gateways at NAT Router
2. ALG (SIP/H.323) on NAT Router Does Not Know Where the Inbound Call Should Be Forwarded to System Gateway
1. System Connection with One IP Address at Internet
2. Port Forwarding about One IP Address at Router
3. IP Signal (SIP/H.323) Is Simply Forwarded to Just One System Gateway (WANU)
Simple Port Forwarding and Proprietary ALG Function
Notes: <number>

## Slide 3
<number>
<number>
Operation Diagram
All Remote Hosts Connect to System by Using One IP Address
WANU Operates As a Router Device in System Network
Internet
Web Admin & Telnet
Remote Phones
IP System
20.20.20.3
10.10.10.4
30.30.30.1
40.40.40.1
50.50.50.1
MFIM
VOIM
LIP
10.10.10.2
10.10.10.3
10.10.10.5
VOIMW
iPECS LIK
20.20.20.1
IP Signal
Media
Maintenance

## Slide 4
<number>
Implementation
Media Gateways (MFIM Built-in and VOIM) Side
* Default Port Ranges
- SIP In/Outgoing: UDP 5060
- H.323 Incoming: TCP 1720
- H.323 Outgoing: TCP/UDP 2048~3071
- RTP (built-in): UDP 7000~/7100~/7300~/9200~
- RTP (VOIM): UDP 6000~/8000~/9000~/9200~
- Web: TCP 80
- Maintenance: TCP 5003
* Reassign Port Range with Consequent Number per Type of Port
* Reassign Port Range without Overlap among the Gateways to be installed

## Slide 5
<number>
Implementation
WANU (VOIMW) Side
* Use reserved second Ethernet Port
* Use Linux Routing
* Use Linux Netfilter/Iptables for Port Forwarding Functions
 Netfilter/Iptables are commonly used to make a router device by using Linux system.
* Proprietary SIP/H.323 ALG Function
 There is no address translation to save the system performance
 Signal distribution is implemented by proxy server and channel number of each VOIM gateways
* Proprietary RTP Packet Forwarding Function to Save the System Performance
* Performance
 7 CPS (Calls Per Second) and 128 Concurrent SIP Calls (with MFIM V50)

## Slide 6
<number>
Internal Block Diagram
VOIM
VOIM
MFIM Port Ranges
Local Port Ranges
VSF Port Ranges
PC Port Ranges
Other Forwarding Port Ranges
Other Forwarding Port Ranges
SIP Port Ranges
H.323 Port Ranges
ALG
SIP
H.323
MFIM
VSF
PC
VOIM
Media Port Ranges
WAN
WANU
LAN
Port Information
Port Information of Each Board Are Stored to WANU

## Slide 7
<number>
Usage of Ethernet Ports
Label\Fun. | VOIM | VOIMW
WAN | LAN1 (to System/Router) | LAN1 (to System)
LAN | LAN2 (not used) | LAN2 (to Router)
Assignment of Ethernet Ports |  | 
* Current labels of each ports will be changed to LAN1 and LAN2 in next production (from January 2011). |  | 
Label Issue of Ethernet Ports

## Slide 8
<number>
System Program
Router IP Address of System Should Be Assigned with WANU Local’s
 PGM102/132
Firewall IP Address of System Should Be Assigned with WANU Public’s
 PGM102/132
Reassign Ports Ranges of Media Gateways without Overlap Among the Media Gateways
 Gateway’s Local Web or Maintenance, optional
Setting Up All Information about IP and Port Ranges to WANU

## Slide 9
<number>
System Program
Step 1. Register All VOIM Gateways to MFIM

## Slide 10
<number>
System Program
Step 2. Configure the Gateway and Firewall for MFIM – PGM102
 In this example, system is installed behind NAT router and its firewall IP is 150.150.150.61
WANU enabled VOIM in this example

## Slide 11
<number>
System Program
Step 3. Configure the Gateway and Firewall for VOIM – PGM132
 In this example, system is installed behind NAT router and its firewall IP is 150.150.150.61

## Slide 12
<number>
System Program
Step 4. Reassign Port Ranges at Each VOIM
 Needs rebooting after changing port ranges
 VOIM supports web I/F (System/Relay)
Setting Up the Web and Maintenance Ports at VOIM.  optional
Setting Up the H.323, RTP, Data Sharing Ports at VOIM and MFIM.
Data Sharing ports are not available in MFIM.

## Slide 13
<number>
System Program
Step 5. Setting Up Port Ranges of Each VOIM at WANU
CIDR notation: a suffix indicating the number of bits in the address
After saving, it is presented to subnet mask. Ex> 24  255.255.255.0

## Slide 14
<number>
System Program
Step 6. Verifying Port Ranges of Each VOIM at WANU
In these fields, two start and end numbers are significant
IP or domain name can be set according to MFIM program. It needs configuring the DNS server address at WANU menu if domain name is specified here.
Currently IP address is only acceptable. Here, 255.255.255.255 means proxy address is not specified.
Board level channels per each VOIM
Max. SIP channels according to PGM 140 “CO VOIP Mode”
Max. H.323 channels according to PGM 140 “CO VOIP Mode”
Forwarding order about incoming call. 0  highest, -1  not assigned
Call direction. Incoming call is not forwarded to board if it is set to Tx
Secondary IP or subnet mask. Here, 255.255.255.255 means single address.

## Slide 15
<number>
System Program
Step 6-1. Configuration Example with MFIM V55
 All of SIP signal are processed at MFIM V55
IP address of MFIM1200 V55
SIP ports are forwarded to MFIM V55. All SIP related ports are assigned to MFIM to forward SIP packets to MFIM.
Total and max number of MFIM SIP should be greater than system capacity. And max SIP number of VOIMs are set to zero.
No need to specify SIP proxy address. MFIM will process all SIP packets from the any proxies.
Ports information about H.323/RTP should be set to here if MFIM V55 have the built-in VOIP gateway.

## Slide 16
<number>
System Program
Step 7. Setting Up the WANU Configurations
Enable WANU function
Reply about ICMP ping packet from the WAN side
Accept web access toward VOIMW from the WAN side
Accept connection of maint. toward VOIMW from the WAN side
Reply about ICMP ping packet from the system side
Enable function of media gateway. This is applicable when WANU function is enabled.
Enable ALG of IP signal
Forwarding method. Round  load balancing, First  seize to max. channel
Keep alive timer. Incoming call is not forwarded to gateway does not respond
Not tested

## Slide 17
<number>
System Program
Step 8. Setting Up the WAN Network Resources
Network address of LAN2
System’s firewall IP address. This IP will be 0.0.0.0 if LAN2 network is a public address
IP address of DNS server if it is needed
Query interval timer when WANU didn’t get the IP address of DNS server

## Slide 18
<number>
System Program
Step 9. Setting Up the MFIM Information
IP address of MFIM

## Slide 19
<number>
System Program
Step 10. Applying the Settings
Apply current settings. This button should be clicked after any changes of WANU configurations

## Slide 20
<number>
Installation
1. Switch Configuration with Public IP Address
System
WAN
Other System Devices

## Slide 21
<number>
Installation
2. Switch Configuration Behind NAT Router
Other System Devices
Router

## Slide 22
<number>
Installation
3. Network Configurations #1
 No NAT Router, WANU LAN2 have a Public IP Address
VOIMW
VOIM
MFIM
Router
SIP Server
Network |  | VOIMW |  | VOIM |  | MFIM | 
Address | 20.20.20.0/24 | LAN1 | 10.10.10.10 | LAN1 | 10.10.10.11 | LAN1 | 10.10.10.2
Router | 20.20.20.254 | LAN2 | 20.20.20.253 | LAN2 | Not used | LAN2 | Reserved to Redundancy
system | 10.10.10.0/24 | Router | 10.10.10.10 | Router | 10.10.10.10 | Router | 10.10.10.10
 |  | Firewall | 20.20.20.253 | Firewall | 20.20.20.253 | Firewall | 20.20.20.253
LAN1
LAN1
LAN1
LAN2
10.10.10.0/24
20.20.20.254
20.20.20.253
10.10.10.10

## Slide 23
<number>
Installation
4. Network Configurations #2
 NAT Router
VOIMW
VOIM
MFIM
Router
SIP Server
Network |  | VOIMW |  | VOIM |  | MFIM | 
Address | 192.168.0.0/24 | LAN1 | 10.10.10.10 | LAN1 | 10.10.10.11 | LAN1 | 10.10.10.2
Router | 192.168.0.254 | LAN2 | 192.168.0.253 | LAN2 | Not used | LAN2 | Reserved to Redundancy
public | 30.30.30.10 | Router | 10.10.10.10 | Router | 10.10.10.10 | Router | 10.10.10.10
system | 10.10.10.0/24 | Firewall | 30.30.30.10 | Firewall | 30.30.30.10 | Firewall | 30.30.30.10
Port Fwd. | 192.168.0.253 |  |  |  |  |  | 
LAN1
LAN1
LAN1
LAN2
10.10.10.0/24
192.168.0.254
192.168.0.253
10.10.10.10
30.30.30.10

## Slide 24
<number>
Installation
5. Network Configurations #3-1
 NAT Router, two or more local network with static routing (or VPN)
VOIMW
VOIM
MFIM
Router
Network |  | VOIMW |  | VOIM |  | MFIM | 
Address | 192.168.0.0/24 192.168.1.0/24 | LAN1 | 192.168.0.10 | LAN1 | 192.168.0.11 | LAN1 | 192.168.0.2
Router | 192.168.0.254 192.168.1.254 | LAN2 | 192.168.0.253 | LAN2 | Not used | LAN2 | Reserved to Redundancy
Static Route | Yes | Static Route | Yes | Static Route | Yes | Static Route | Yes
public | 30.30.30.10 | Router | 192.168.0.10 | Router | 192.168.0.10 | Router | 192.168.0.10
system | 192.168.0.0/24 | Firewall | 30.30.30.10 | Firewall | 30.30.30.10 | Firewall | 30.30.30.10
Port Fwd. | 192.168.0.253 |  |  |  |  |  | 
LAN1
LAN1
LAN1
LAN2
192.168.0.0/24
LIP(local remote)
192.168.1.0/24
192.168.0.254 NIC1
192.168.1.254 NIC2
Static Routes at Router Side
1) 192.168.1.0/24  192.168.0.254(NIC1)
2) 192.168.0.0/24  192.168.1.254(NIC2)
30.30.30.10 NIC3
* It needs the program of static routing at VOIM/W and MFIM to communicate with LIP in local remote. Especially if there is no program at VOIMW, the source IP of the packet for 1.x will be changed to LAN2’s by normal routing rule. So the communication can’t be done.
Notes: <number>

## Slide 25
<number>
Installation
6. Network Configurations #3-2
 Static routing at VOIM/W
 Supported revision: E.0Cc or later
or 255.255.255.0
Notes: <number>