## Slide 1
iPECS MFIM Upgrade Process

## Slide 2
[Office version Upgrade procedure]
Set http trace in mon> serial and save trace. (COM1 is recommended to print http trace)
Set maint password. (PGM162 – Flex Btn 3)
Set ‘Web Password Encryption’ to ‘OFF’ in PGM 161-Flex Btn 15
Download DB file.
Delete all file in web admin. (System Management -> File System -> File View & Delete)
Upload GSXXME0Gr_meta_version.rom (Eg, MFIM100 :GS95ME0Gr_meta_version.rom)
Restart MFIM.
Delete all file in web admin. (System Management -> File System -> File View & Delete)
Above process (1~8) are only need once when upgrade from 5.0Gs(or below) to 5.0Ha (or 5.5).
Upload kernel image (eg, GSXXM55Cj_kernel.rom or after version).
GSXXM55Cj_kernel.rom : boot, kernel, resource files
Restart MFIM.
Upload application image (eg, GSXXM55Cj_app.rom or after version)
GSXXM55Cj_app.rom (application , HTML images)
Restart MFIM.

## Slide 3
[Hotel version Upgrade procedure]
Set http trace in mon> serial and save trace. (COM1 is recommended to print http trace)
Set maint password. (PGM162 – Flex Btn 3)
Set ‘Web Password Encryption’ to ‘OFF’ in PGM 161-Flex Btn 15
Download DB file.
Delete all file in web admin. (System Management -> File System -> File View & Delete)
Upload GSXXNE0Ha_meta_version.rom (Eg, MFIM100 :GS95ME0Ha_meta_version.rom)
Restart MFIM.
Delete all file in web admin. (System Management -> File System -> File View & Delete)
Above process (1~8) are only need once when upgrade from 5.0Gs(or below) to 5.0Ha (or 5.5).
Upload kernel image (eg, GSXXM55Cj_kernel.rom or after version).
GSXXM55Cj_kernel.rom : boot, kernel, resource files
Restart MFIM.
Upload application image (eg, GSXXM55Cj_app.rom or after version)
GSXXM55Cj_app.rom (application , HTML images)
Restart MFIM.

## Slide 4
[Upgrade Troubleshooting guideline]
If you have a problem to upgrade MFIM, then please send below information.
-. http trace during MFIM upgrade.
-. Connect to maint> serial with RS232 Serial port.
1. Enter “ver” in maint> serial.
2. Enter “sys sh” to enter system shell.
3. Enter “df” command to view file system.
4. Enter “ls –al /”
5. Enter “ls –al /home”
6. Enter “ls –al /home/http”
7. Enter “cat /etc/autoload”
cf) to quit system shell, enter “exit” command.