## Slide 1
Important Safety Information

## Slide 2
Important Safety Information

## Slide 3
Important Safety Information

## Slide 4
Table of Contents
Putting into operation
LDP-7024LD
ICON description on LCD
Input / Output Devices and Button
Cable Connection
ADP (Additional Device Port)
Placing or answering an outside call
1. Placing an outside call
2. Answering an outside call
3 Soft & Navigation Button
Basic Function
1. Idle
1.1 Pickup
1.2 Conference
1.3 Redial
2. Off Hook
3. Intercom Dialing
4. Intercom Ring Back
5. Intercom Busy
6. Intercom Do Not Disturb
7. Intercom Dialing Error
8. Intercom Receiving
9. Intercom Talk
10. CO Line Busy
11. CO Dialing / CO Talk
12. Checking messages
13. Page
Phone Book
1. New Entry
2. Search by name
3. Search by number
4. Search by group
5. CO access code
6. Delete all entry
6
6
7
8
10
11
13
13
13
14
15
15
15
16
17
18
18
18
18
19
19
19
19
19
20
20
20
21
21
23
24
25
26
26

## Slide 5
Table of Contents
Menu Button Function
1. EZ Menu
1.1 Dialed Calls
1.2 Received Calls
1.3 Speed dial
1.3.1 Dial by STA SPD
1.3.2 Dial by SYS SPD
1.3.3 Dial by ICM Name
1.3.4 Dial by STA SPD Name
1.3.5 Dial by SYS SPD Name
1.4 Call forward
1.5 Absent message
1.6 Paging
1.7 Do not disturb
1.8 Wake up
2. Phone Book
3. Schedule
3.1 Schedule ADD/DEL/EDIT
3.2 Find schedule
3.3 Delete past schedule
3.4 View alarm schedule
3.5 Delete all schedule
4. Customize
4.1 Change language
4.2 Register name
4.3 Ring type
4.4 Speaker / Headset
4.5 E-MIC Headset
4.6 Bright Level
5. Setting
5.1 ENBLOCK MODE
5.2 Station COS
5.3 Password
5.4 Speed PGM
5.5 Answer mode
6. Voice mail
6.1 Internal Voice Mail
6.2 External Voice Mail
Entering Characters
Glossary of Terms
27
27
27
27
28
28
28
29
29
30
31
32
33
34
34
35
36
36
38
39
39
40
41
41
41
42
43
43
43
44
44
45
47
48
49
50
51
51
52
53

## Slide 6
Putting into operation
LDP-7024LD
LDP-7024LD is a user-friendly digital keyset, which offer convenience to user with 3 soft key and navigation key.
Features
-.Trendy and Stylish LDP Family design
-.Multi Level Graphic LCD (9 * 32)
-.Dual LED 24 Flexible buttons
-.Additional Device Port for SLT and FAX
-.Call Log Feature
-.Call Recording Feature (USB Module, Option)
-.Hands-Free Solution (Blue Tooth Module, Option)
-.Wall Mountable(Option)

## Slide 7
Putting into operation
ICON description on LCD
ICON
1. You have received message
2. Call forward
3. DND mode
4. Earphone mode
5. Full Duplex Speaker Phone Mode
6. Mute mode
7. Setting melody
8. Setting alarm
9. Schedule
10. Phone book
11. ON : Already paired but linked-radio with headset
12. STADY ON : Ready to make and answer a call.
BLINK : Ongoing communication via Bluetooth headset.
Description

## Slide 8
Putting into operation
Input / Output Devices and Button
1
2
3
4
5
6
7
8
9
1
Handset
Earphone-Jack Socket
(Ear/Mic Mode)
Speaker
Speed Button
Dnd/Fwd Button
Speaker Button
Hold/Save Button
Phonebook Button
LCD Display
10
11
12
13
14
15
16
17
Message Waiting LED
3 Soft Button
Flexible Button
Trans/Pgm Button
Call back Button
Volume Button
Menu Button
Handsfree Microphone
9
11
12
13
14
15
16
17
3
4
5
6
7
8
2
10

## Slide 9
Putting into operation
Used for handset call.
The optional earphone into the handset to provide a handsfree phone conversation.
Outputs tones and voice at your extension.
Used to access speed dialing, speed programming, save number redial, and last number redial.
The DND (Do Not Disturb) feature lets you activate a ‘do not ring this phone’ mode. When the DND is active, this button is red. It is also used to activate call forwards, to another station or voicemail for example.
Used to forward your calls to another station or voice mail.
Speaker toggles the speakerphone state. The button is red when the speakerphone is active.
This button put a call on hold or save information when programming.
Save the telephone number and make a call use this button.
Displays information about telephone status, dialing directories,and test message information.
Illuminates when the phone is ringing.
Used to work in conjunction with fixed and flexible features.
The remaining Flex buttons can be assigned to a feature.
This button is used to start a transfer (TRS) of a call or enter programming mode (PGM)
A station can initiate a call back request to another busy station. Once that station becomes idle, the station that left the call back request is signaled.
The volume button adjusts the audio levels follows.
Use this menu button to move to the desired option(Dial, MSG, Program) and use for arrows key.
Used to work in conjunction with fixed and flexible features.
Handset
Earphone-Jack Socket
Speaker
Speed Button
Dnd/Fwd Button Speaker Button
Hold/Save Button
Phone Book
LCD Display
Message Waiting LED
3 Soft Button
Flexible Button
Trans/PGM
Call back
Volume
Menu
Handsfree Microphone
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17

## Slide 10
Putting into operation
Cable Connection
①
②
③
④
Cable connection
①, ② Connect the end of the telephone cord to the handset
and the other end to the handset jack at the bottom of the telephone.
③, ④ Connect the end of the cable to the port at the bottom of telephone and the other end to the switch port.
※ Connect the Earphone to the headphone jack at the left side of the telephone.
(In case front view of the base.)

## Slide 11
Putting into operation
ADP (Additional Device Port)

## Slide 12
Putting into operation
ADP (Additional Device Port)

## Slide 13
Placing or answering an outside call
1. Placing an Outside Call
Lift handset
▶
Enter the extension number
Dial 9,0 or select CO line flexible button
talk
▶
2. Answering an Outside Call
or
Lift handset
or
▶
talk
CO Line
ICM Line
Lift handset
▶
Enter the desired phone number
talk
▶
or
▶
CO Line
ICM Line
Lift handset
or
▶
talk
Press flashing CO line button or loop key.
▶

## Slide 14
3 Soft & Navigation Button
“3 Soft Button” is located on the bottom of the LCD display and IP LDK systems provide some fitting message for each operation. It gives easy access to operations with a Navigation Button or volume up/down key. For example, when a user gets busy message of called extension, some operations which becomes available will be displayed “Message Wait”, “Camp-On” and “Flash”. Then by pressing one of 3 soft button, a user can activate the desired feature.
3 Soft Button
Navigation Button
Sometimes a system does show all message for some operation, then the arrow key will be displayed the begin or end line. By pressing a Navigation Button of LDP-7000 series, others will be displayed.
BUSY : STA 100
[CALLBK] CAMP(*) STEP
MSG CAMP-ON FLASH
STATION 100 (T)
FEB 01 04 05:34 pm
FORWARD CONF REDIAL ▶
STATION 100 (T)
FEB 01 04 05:34 pm
◀ ICM BTN

## Slide 15
Basic Function
The 3 soft button enables you to select the various function. For instance, if you want to select the pickup, press the first button on the left as below shown. And if there are more than three functions and displays an arrow on LCD, use Navigation Button to move the next or previous function.
3 Soft Button is located on the bottom of the LCD display and IP LDK systems provide.
1. Idle
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
PICKUP : press the [PICKUP] button to Can pickup
the ring in the same pickup group
CONF : press the [MSG] button to can cancel the unsupervised conference.
REDIAL : press the [REDIAL] button to make a last
number redial.
1.1 Pickup
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
CALL TO STA 104
FROM 100 05:34 pm
TRANS CONF MUTE
A station can pickup a call ringing to an unattended station within the same pickup group by using the pickup procedure.
＊ Refer to IP LDK-100/300/300E programming manual.
Press the [pickup] button.
Talk

## Slide 16
Basic Function
1.2 Conference
CALL TO STA 100
FEB 01 04 05:34 pm
MSG FLASH
CALL TO STA 100
FEB 01 04 05:34 pm
TRANS CONF MUTE
Dial the desired phone number.
e.g.)100
The station 100 answers the call.
Press the [CONF] button.
CONFERENCE
FEB 01 04 05:34 pm
FORWARD CONF REDIAL ▶
Dial the phone number of the desired party
e.g.)104
CALL TO STA 104
FEB 01 04 05:34pm
MSG FLASH
The station 104 answers the call.
CALL TO STA 104
FEB 01 04 05:34 pm
TRANS CONF MUTE
Press the [CONF] button twice.
CONFERENCE
FEB 01 04 05:34 pm
CONF MUTE
For making a 3-party conference, press [CONF] button twice.

## Slide 17
Basic Function
1.3 Redial
STATION 100 (T)
FEB 01 04 05:34 pm
PICKUP CONF REDIAL
Press the [REDIAL] button.
DIALED CALLS
1234
5678
BACK DETAIL SEND
Select the desired one with Navigation Button.
Press [SEND] or button to make the call.
9114
LINE 001 00:01:01
TRANS CONF MUTE ▶
DIALED CALLS-0
07/24 10:56
1234
BACK SEND
Or, [DETAIL] to show the detailed information of DIALED CALLS.
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 01

## Slide 18
Basic Function
2. Off Hook
STATION 100 (T)
FEB 01 04 05:34 pm
FORWARD CONF REDIAL ▶
FWD : press the [FWD] button to forward a call to
another station.
CONF : press the [CONF] button to make a conference.
REDIAL : press the [REDIAL] button to make a last
number redial.
3. Intercom Dialing
STATION 100 (T)
FEB 01 04 05:34 pm
FLASH
FLASH : press the [FLASH] button to disconnect the
line and reseize.
4. Intercom Ring Back
CALL TO STA XXX
FEB 01 04 05:34 pm
MSG FLASH
MSG : press the [MSG] button to leave a message.
FLASH : press the [FLASH] button to disconnect the
line and reseize.
5. Intercom Busy
BUSY : STA 100
[CALLBK] CMAP ( * ) STEP
MSG CAMP-ON FLASH
MSG : press the [MSG] button to leave a message.
CAMP-ON : press the [CAMP-ON] button to allows
you to send a call waiting tone to a busy
station indicating that they have a call
waiting.
FLASH : press the [FLASH] button to disconnect the
line and reseize.
STATION 100 (T)
FEB 01 04 05:34 pm
◀ ICM BTN
ICM : press the [ICM] button to retrieve the ICM [HOLD] button.

## Slide 19
Basic Function
7. Intercom Dialing Error
INVALID
FEB 01 04 05:34 pm
FLASH
FLASH : press the [FLASH] button to disconnect the
line and reseize.
8. Intercom Receiving
CALL FROM STA 101
FEB 01 04 05:34 pm
DND
9. Intercom Talk
CALL FROM STA 101
FEB 01 04 05:34 pm
TRANS CONF MUTE
DND : press the [DND] button to prevent other parties
from disturbing you.
TRANS : press the [TRANS] button to transfer the
incoming call to another station.
CONF : press the [CONF] button to make a conference. MUTE : press the [MUTE] button to mute the handset,
speakerphone, or headset but does not affect
the speech coming over the speaker or
handset. Pressing the [SPEAK] button again
activates the microphone.
10. CO Line Busy
CO LINE 001 BUSY
QUEUING ([CALLBK])
CALLBK
CALLBK : press the [CALLBK] button to reserve CO line.
6. Intercom DND
DO NOT DISTURB STA 100
CALLBK FLASH
CALLBK : press the [CALLBK] button to leave the call
back request or message.
FLASH : press the [FLASH] button to disconnect the
line and reseize.

## Slide 20
Basic Function
11. CO Dialing/CO Talk
123456789
LINE 125 00:00:03
TRANS CONF MUTE ▶
123456789
LINE 125 00:00:03
◀ RECORD FLASH ACNR
TRANS : press the [TRANS] button to transfer the
incoming call to another station.
CONF : press the [CONF] button to make a conference.
MUTE : press the [MUTE] button to mute the handset,
speakerphone, or headset but does not affect
the speech coming over the speaker or
handset. Pressing the [SPEAK] button again
activates the microphone.
RECORD : press the [RECORD] button to record the
current calling.
FLASH : press the [FLASH] button to disconnect the
line and reseize.
ACNR : press the [ACNR] button to set the automatic
call number redial.
12. Checking messages
VMIB MSG FROM : EXTERNAL
NEXT REPEAT DELETE ▶
VMIB MSG FROM : EXTERNAL
◀ ADD REWIND CALL BACK
ADD : press the [ADD] button to leave a message to
the party who leave a message to me.
REWIND : press the [REWIND] button to hear the
message rewinded.
CALLBK : press the [CALLBK] button to reserve CO line.
※ ADD, REWIND,CALL BACK is not available in LDK-20.
13. Page
PAGE FROM STA 103
30 JUL 04 01:28 pm
MEET ME
NEXT : press the [NEXT] button to move to the next
message.
REPEAT : press the [REPEAT] button to hear the
message again.
DELETE : press the [DELETE] button to erase the
message.
MEET : press the [MEET] button to answer the current
paging.

## Slide 21
Enter the name.
To move to the next step, press the button.
※ Use the softkey button to enter the character
such as English, the number and the
symbol and press the softkey button to select
the type : capital English letter>
small English letter>the number>the symbol.
Phone Book
Press the [1] button.
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
PHONE BOOK
6. DELETE ALL ENTRY ▲ ▲
▼
EXIT OK
1. NEW ENTRY
NEW ENTRY
NAME : 
TYPE : MOBILE
CO CODE : NOT USE
NUMBER :
GROUP : NO GR.
BACK ABC SAVE
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
The [PHONE BOOK] is used for registering the new phone number and searching, correcting and deleting the stored phone number.
The number of the phone number registers up to 100.

## Slide 22
Select the CO access code, use the to
select the NOT USE or CODE-1, 2,3,4,5.
※ In case of selecting one of the e-mail or address or memo, NOT USE will be displayed and can’t select the CO access code.
Phone Book
NEW ENTRY
NAME : JANE
TYPE : ◀ MOBILE ▶
CO CODE : NOT USE
NUMBER :
GROUP : NO GR.
BACK SAVE
Enter the type, select the desired one among the
cellular phone number or office number or home
number or fax number or e-mail or address or memo.
NEW ENTRY
NAME : JANE
TYPE : MOBILE
CO CODE : ◀ CODE-1 ▶
NUMBER :
GROUP : NO GR.
BACK SAVE
Enter the phone number. In case of selecting e-mail or address or memo on type, the contents is available.
NEW ENTRY
NAME : JANE
TYPE : MOBILE
CO CODE : CODE-1
NUMBER : 123456789
GROUP : NO GR.
BACK SAVE
Select the group. Use to select NO GR /family / friend /office / school /customer or club. Press [SAVE] to save the new entry.
NEW ENTRY
NAME : JANE
TYPE : MOBILE
CO CODE : CODE-1
NUMBER : 123456789
GROUP : ◀ FAMILY ▶
BACK SAVE

## Slide 23
Phone Book
2. SEARCH BY NAME
Press [FIND] and then the phone book entry will be displayed.
PHONE BOOK
1. NEW ENTRY ▲
2. Search By Name
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
BACK ABC FIND
SEARCH BY NAME
INPUT NAME ?
ABC
When entering the name, enter the full name or
the part of the name(ex:ABC) and press [FIND].
The name will be displayed. Use to select the desired name.
※ Press [EDIT] to correct the phone number.
Press [SEND] to make a call.
※ Use the button to select type.
RESULTS
001 : JONE MARK
003 : ABRAHAM
007 : LUCKY
◀MOBILE▶ 01011111234
BACK EDIT SEND
Press the [2] button.
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
※ For detailed information about entering name, see the page 52.

## Slide 24
Phone Book
3. SEARCH BY NUMBER
Press the [3] button.
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
PHONE BOOK
1. NEW ENTRY ▲
2. Search By Name
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
BACK FIND
SEARCH BY NUMBER
INPUT NUMBER?
123
When entering the phone number, enter the part of the phone number or the full number and press [FIND].
The name will be displayed. Use to select the desired name.
※ Press [EDIT] to correct the phone number.
Press [SEND] to make a call.
RESULTS
001 : JONE MARK
003 : ABRAHAM
007 : LUCKY
◀MOBILE▶ 01011111234
BACK EDIT SEND

## Slide 25
Phone Book
4. SEARCH BY GROUP
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. REG. CO ACCESS CODE ▼
BACK FIND
SEARCH BY GROUP
NO GR. ▲
FAMILY
FRIEND
OFFICE ▼
Press the [4] button.
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
Use to select the group and press [FIND].
The name will be displayed. Use to select the desired name.
※ Press [EDIT] to correct the phone number.
Press [SEND] to make a call.
RESULTS
001 : JONE MARK
003 : ABRAHAM
007 : LUCKY
◀MOBILE▶ 01011111234
BACK EDIT SEND

## Slide 26
Phone Book
5. CO ACCESS CODE
Press the [5] button.
PHONE BOOK
CO ACCESS CODE
CODE-1 : 9
CODE-2 : 8801
CODE-3 :
CODE-4 :
CODE-5 :
BACK SAVE
6. DELETE ALL ENTRY
Press the [6] button.
PHONE BOOK
6. DELETE ALL ENTRY ▲ ▲
▼
Exit OK
PHONE BOOK
6. Delete All Entry ▲
▼
BACK OK
Use to select ‘YES’.
Press [OK] to delete all the phone book.
Use to select the code and enter the
CO ACCESS CODE.
Press [SAVE] to save. The entered CO ACCESS CODE is entered when the phone number registers or corrects.
ARE YOU SURE
TO DELETE DATA?
NO
YES
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK

## Slide 27
Menu Button Function
1. EZ MENU
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.
1.1 DIALED CALLS
DIALED CALLS
1234
5678
BACK DETAIL SEND
1.2 RECEIVED CALL
RECEIVED CALLS
1234
5678
BACK DETAIL SEND
Use to select the list.
Press [SEND] to dial the desired one.
Press [DETAIL] to show the detailed information of DIALED CALLS.
Also press [SEND] to make the call.
Use to select the list.
Press [SEND] to dial the desired one.
Press [DETAIL] to show the detailed information of DIALED CALLS.
Also press [SEND] to make the call.

## Slide 28
Menu Button Function
1.3 SPEED DIAL
1.DIAL BY STA SPD
2.DIAL BY SYS SPD
3.DIAL BY ICM NAME
4.DIAL BY STA SPD NAME
5.DIAL BY SYS SPD NAME
BACK EXIT
Press the [1] button.
Use to select the desired one.
Press [SEND] to make the call.
※ To check the name of the selected number,
press the [NAME/TEL] button.
On the contrary, to check the number of the
selected name, press the [NAME/TEL]
button.
1.DIAL BY STA SPD
2.DIAL BY SYS SPD
3.DIAL BY ICM NAME
4.DIAL BY STA SPD NAME
5.DIAL BY SYS SPD NAME
BACK EXIT
Press the [2] button.
1.3.1 DIAL BY STA SPD
1.3.2 DIAL BY SYS SPD
Use to select the desired one. Also press [SEND] to make the call.
1234 (001)
4567 (002)
5678 (003)
BACK NAME/TEL SEND
9021111111 (001)
9022222222 (002)
9023333333 (003)
BACK NAME/TEL SEND

## Slide 29
Menu Button Function
1.DIAL BY STA SPD
2.DIAL BY SYS SPD
3.DIAL BY ICM NAME
4.DIAL BY STA SPD NAME
5.DIAL BY SYS SPD NAME
BACK EXIT
Press the [3] button.
Use to select the desired one.
Also press [SEND] to make the call.
1.DIAL BY STA SPD
2.DIAL BY SYS SPD
3.DIAL BY ICM NAME
4.DIAL BY STA SPD NAME
5.DIAL BY SYS SPD NAME
BACK SEND
Press the [4] button.
1.3.3 DIAL BY ICM NAME
1.3.4 DIAL BY STA SPD NAME
Use to select the desired one. Also press [SEND] to make the call.
JANE (001)
ROBERT (002)
HEAY (003)
BACK SEND
JANE (001)
ROBERT (002)
HEAY (003)
BACK NAME/TEL SEND

## Slide 30
Menu Button Function
1.DIAL BY STA SPD
2.DIAL BY SYS SPD
3.DIAL BY ICM NAME
4.DIAL BY STA SPD NAME
5.DIAL BY SYS SPD NAME
BACK EXIT
Press the [5] Button.
Use to select the desired one.
Also press [SEND] to make the call.
1.3.5 DIAL BY SYS SPD NAME
JANE (2002)
ROBERT (2004)
HEAY (2001)
BACK NAME/TEL SEND

## Slide 31
Menu Button Function
1.4 CALL FORWARD
when user can’t receive a call because of having a meeting or absence, the call forwarding lets you forward your calls to another number. For detailed information about forward , refer to the programming manual.
Select the desired type of forward from 0 to 7.
※ in case of canceling the forward, press [ # ].
Enter the forwarded station / group/#(VMIB).
FORWARD TO STA 158 (U)
06 SEP 04 11:42am
PICKUP CONF REDIAL
Enter the forwarded station / group/#(VMIB).
2004
07 / 01
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
1.UNCONO.FWD 6.OFFNET-NO ANS
2.BUSY FWD 7.IN-CO OFFNET
3.NO ANS FWD 0.FOLLOW ME
4.BUSY/NO ANS #.CANCEL FWD
5.OFFNET-UNC
ENTER FORWARD TYPE
( 0 – 7 , # )
BACK EXIT
1.UNCONO.FWD 6.OFFNET-NO ANS
2.BUSY FWD 7.IN-CO OFFNET
3.NO ANS FWD 0.FOLLOW ME
4.BUSY/NO ANS #.CANCEL FWD
5.OFFNET-UNC
UNCONDITION FORWARD
ENTER STA/HUNT/# (VNIB)
BACK EXIT

## Slide 32
Menu Button Function
1.5 ABSENT MESSAGE
01.LUNCH RETURN AT HH:MM
02.ON VACATION
03.OUT OF OFFICE HH:MM
04.OUT OF OFFICE MM:DD
05.OUT OF OFFICE
ENTER MESSAGE NO
BACK NEXT CANCEL
01.LUNCH RETURN AT HH:MM
02.ON VACATION
03.OUT OF OFFICE HH:MM
04.OUT OF OFFICE MM:DD
05.OUT OF OFFICE
ENTER TIME
HH : MM
BACK SAVE EXIT
The absent message list will be displayed.
Use [NEXT] button or [BACK] button to enter the number of the desired absent message. ※ To erase the absent message, press [CANCEL].
Press [HOLD] button to save.
Enter the time.
e.g.) am 07:30  enter 0730.
pm 03:30  enter 1530.
01.LUNCH RETURN AT HH:MM
02.ON VACATION
03.OUT OF OFFICE HH:MM
04.OUT OF OFFICE MM:DD
05.OUT OF OFFICE
ENTER TIME
07:30 Press HOLD Key
BACK SAVE EXIT

## Slide 33
Menu Button Function
1.6 PAGING
The paging is very convenient in case of emergency or finding someone.
The external paging requires a external amplifier and speaker.
The paging is available only for approval person.
For detailed information about paging, refer to the programming manual.
1.INTERNAL 6.EXT ALL
2.INT ALL 7.ALL (INT+EXT)
3.EXT ZONE 1
4.EXT ZONE 2
5.EXT ZONE 3
BACK EXIT
Select the paging zone.
Enter the detailed zone.
1.INTERNAL 6.EXT ALL
2.INT ALL 7.ALL (INT+EXT)
3.EXT ZONE 1
4.EXT ZONE 2
5.EXT ZONE 3
ENTER INT PAGE NO (01-35)
BACK EXIT
Start paging by lifting handset.
After finishing paging, put the handset down.
1.INTERNAL
2.INT ALL)
3.EXT ZONE 1
4.ALL (INT+EXT)
BACK EXIT
1.INTERNAL
2.INT ALL
3.EXT ZONE 1
4.ALL (INT+EXT)
ENTER INT PAGE NO (01-10)
BACK EXIT
LDK-100/300/600
LDK-20
LDK-100/300/600
LDK-20

## Slide 34
Menu Button Function
1.7 DO NOT DISTURB
STA IN DO NOT DISTURB
04 JUL 03 06:01 pm
PICKUP CONF REDIAL
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 01
After setting the DND, the DND icon will be displayed on the top of LCD.
1.8 WAKE UP
1.DIALED CALLS 6.PAGING
2.RECEIVED CALLS7.DO NOT DISTURB
3.SPEED DIAL 8.WAKE UP
4.CALL FORWARD
5.ABSENT MESSAGE
ENTER YOUR WAKEUP TIME
HH:MM 04:01 pm
BACK SAVE EXIT
Enter the alarm time.
After setting the alarm time,
press the[SAVE]button.
The alarm icon will be displayed on the top of LCD and [*] is blinking.
1.DIALED CALLS 6.PAGING
2.RECEIVED CALLS7.DO NOT DISTURB
3.SPEED DIAL 8.WAKE UP
4.CALL FORWARD
5.ABSENT MESSAGE
ENTER YOUR WAKEUP TIME
07:30-C 04:01 pm
BACK SAVE EXIT
S:One Day (Default)
C:Every Day ( # )
* Set the time : e.g. (7hour)
am 07:00
pm 19:00

## Slide 35
Menu Button Function
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.
2. PHONE BOOK
PHONE BOOK
1. NEW ENTRY ▲
2. SEARCH BY NAME
3. SEARCH BY NUMBER
4. SEARCH BY GROUP
5. EDIT CO ACCESS CODE ▼
EXIT OK
PHONE BOOK
6. DELETE ALL ENTRY ▲
▼
EXIT OK
For the detailed information about the phone book, see phonebook(p21).

## Slide 36
Menu Button Function
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.
3. SCHEDULE
3.1 SCHEDULE ADD/DEL/EDIT
SCHEDULE
1. SCHEDULE/ADD/DEL/EDIT
2. FIND SCHEDULE
3. DELETE PAST SCHEDULE
4. CHECK ALARM SCHEDULE
5. DELETE ALL SCHEDULE
BACK TODAY OK
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
CALENDAR
07/2004
The number of the schedule is added up to 50.
The calendar of schedule is from 1960 to 2040.
Use to select the date and
press the [OK] button to save it.
※ Press [TODAY] or [5] to move to current date.
Press [1] to move to last year.
Press [3] to move to next year.
Press [7] to move to last month.
Press [9] to next month.
SCHEDULE ADD
Use [ADD] to add the schedule. Use number key to enter the time directly.
※ am 7:00 ▶ 0700
pm 7:00 ▶ 1900
SCHEDULE ADD
DATE : 01/JUL/04 (SAT)
TIME : [PM ] 06 : 59
REPE : ◀ NONE ▶
ALARM : NONE
TEXT :
BACK SAVE
Use to set NONE or everyday or every week or every month.
DATE : 01/JUL/04 (SAT)
TIME : [PM] 06 : 59
REPE : NONE
ALARM : NONE
TEXT :
BACK AM SAVE

## Slide 37
Menu Button Function
SCHEDULE ADD
DATE : 01/JUL/04 (SAT)
TIME : [PM ] 06 : 59
REPE : NONE
ALARM : NONE
TEXT :
BACK SET SAVE
Set the alarm.
Press the [SET] button to inform the schedule and enter the time.
SCHEDULE ADD
Press [SAVE] to save the schedule.
CHECK SCHEDULE
01 JUL 04 06:01 pm
07/2004
The alarm icon will be displayed on the top of LCD and it will ring for the time. After checking the schedule, the icon will be disappeared.
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
DATE : 01/JUL/04 (SAT)
TIME : [PM ] 06 : 59
REPE : NONE
ALARM :00 HOUR 00 MIN BEFORE
TEXT : CONFERENCE
BACK ALL SAVE

## Slide 38
Menu Button Function
3.2 FIND SCHEDULE
FIND SCHEDULE
SEARCH : SCHEDULE
YEAR : ◀ 2004 ▶
MONTH : 02
TEXT :
BACK ALL FIND
FIND SCHEDULE
Use to select the year.
Use to select the month.
RESULTS
SEARCH : SCHEDULE
YEAR : 2004
MONTH : ◀ 06 ▶
TEXT :
BACK ALL FIND
DATA : 01/JUL/04 1/1
[AM] 07:45 CONFERENCE
BACK VIEW
Press the [FIND] button and the result will be displayed.
Use the [VIEW] button to check the contents of schedule.

## Slide 39
Menu Button Function
3.3 DELETE PAST SCHEDULE
PAST SCHEDULE
PAST SCHEDULE : 01
BACK DEL
The number of the past schedule is displayed.
Press the [DEL] button.
PAST SCHEDULE
PAST SCH. : 01
BACK OK
ARE YOU SURE
TO DELETE DATA?
NO
YES
Use to select [YES] or [NO].
Press [DEL] to delete the past schedule.
3.4 VIEW ALARM SCHEDULE
CHECK SCHEDULE
01 JUL 04 *07:45 am
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 03
When the stored schedule comes, the schedule icon will be displayed on the top of LCD. And the alarm ring will ring to inform the time.
ALARM SCHEDULE
Check the schedule.
Press the [DEL] to clear the schedule icon or
Press the [BACK] to leave the schedule icon.
DATE : 01/JUL/04 (SAT)
TIME : [PM ] 06 : 59
REPE : DAY
ALARM : 00 HOUR 01 MIN BEFORE
TEXT : CONFERENCE
BACK

## Slide 40
Menu Button Function
3.5 DELETE ALL SCHEDULE
PAST SCHEDULE
PAST SCH. : 01
BACK OK
ARE YOU SURE
TO DELETE DATA?
NO
YES
Use to select [YES] or [NO].
Press [OK] to delete the all schedule.
If selecting “YES”, delete it. If selecting “no”, don’t delete it.

## Slide 41
Menu Button Function
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.
4. CUSTOMIZE
4.1 CHANGE LANGUAGE
1.CHANGE LANG 6.BRIGHT LEVEL
2.REGISTER NAME
3.RING TYPE
4.SPKR/HEADSET
5.E-MIC MEADSET
BACK EXIT
Press the [1] to change language.
4.2 REGISTER NAME
1.CHANGE LANG 6.BRIGHT LEVEL
2.REGISTER NAME
3.RING TYPE
4.SPKR/HEADSET
5.E-MIC MEADSET
JAN
ENTER NAME ( )
BACK ABC> OK
Press the [2] and enter the name.
Press the [OK] button to save it.
CALL TO JAN
01 JUL 04 07:45 am
MSG FALSH
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 03
When the another station calls, the name on the LCD will be displayed instead of the station number.
※ For detailed information about entering name, see the page 52.

## Slide 42
Menu Button Function
4.3 RING TYPE
1.ICM RING
2.ICM MELODY
3.CO RING
4.CO MELODY
BACK EXIT
1.ICM RING
2.ICM MELODY
3.CO RING
4.CO MELODY
RING TONE
DIAL 01 –15 : 01
BACK SAVE EXIT
Press the [1] button.
Use the dial button to select ring tone.
※ There are 15 types from 01 to 15.
e.g ) 01
※ Setting the CO ring is the same.
1.ICM RING
2.ICM MELODY
3.CO RING
4.CO MELODY
BACK EXIT
◀ Pleasure (10) ▶
[01] Cancan
[02] Trumpet Ensemble
[03] Pathetique
[04] Russian Dance
[05] Bohe Folk Song
EXIT OK
Press the [2] button.
Use to select the desired category.
Press the [OK] or button and then the
melody is changed.
※ Press the [EXIT] button to cancel.
※ Setting the CO melody is the same.
To set the melody, MFU and MU board is required.
Use to select the desired melody.

## Slide 43
Menu Button Function
4.4 SPEAKER/HEADSET
1.CHANGE LANG 6.BRIGHT LEVEL
2.REGISTER NAME
3.RING TYPE
4.SPKR/HEADSET
5.E-MIC HEADSET
SELECT SPEAKER/HEADSET
(1:SPK 0:HEADSET) : 1
BACK SAVE EXIT
Enter [1] to select speaker and [0] to select headset. Press the [SAVE] button to save it.
4.5 E-MIC HEADSET
1.CHANGE LANG 6.BRIGHT LEVEL
2.REGISTER NAME
3.RING TYPE
4.SPKR/HEADSET
5.E-MIC HEADSET
EAR-MIC HEADSET
(1:ON/0:OFF) : OFF
BACK SAVE EXIT
Note
To use an earphone, the speaker mode is required to set in speaker / headset mode.
Press [1] to use an earphone and [0] not to use an earphone. Press [SAVE] to save it.
4.6 BRIGHT LEVEL
1.CHANGE LANG 6.BRIGHT LEVEL
2.REGISTER NAME
3.RING TYPE
4.SPKR/HEADSET
5.E-MIC HEADSET
■ ■ ■ ■ ■ ■ ■ ■ ■ ■ ■□□□□□
SELECT BY UP/DOWN KEY
BACK EXIT
Use or to adjust the bright level.

## Slide 44
Menu Button Function
5. SETTING
5.1 ENBLOCK MODE
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
ENBLOCK MODE
(1:ON/0:OFF) : OFF
BACK SAVE EXIT
Press [1] to set the EN-BLOCK MODE.
Press [SAVE] to save it.
STATION 100 (T)
1234
CLEAR SEND
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 03
In en-block mode, when dialing, press the [CLEAR] button to erase the entered number.
Press [SEND] to make a call.
※ In case of dialing in en-block mode, don’t use [HOLD] to make a call.
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.

## Slide 45
Menu Button Function
5.2 STATION COS
1.TEMPORARY COS
2.WALKING COS
ICM ONLY MODE
PRESS HOLD KEY
BACK SAVE EXIT
SET TEMPORARY COS
The password is needed.
Press the [1] TEMPORARY COS.
Press the [SAVE] button to down the COS.
1.TEMPORARY COS
2.WALKING COS
ENTER CURRENT PASSWORD
BACK SAVE EXIT
CANCEL TEMPORARY COS
Enter the password.
※ If the password is wrong, the warning tone will be heard.
Press the [SAVE] button to down the COS.
1.TEMPORARY COS
2.WALKING COS
BACK EXIT
Select the item.
5.2.1 TEMPORARY COS

## Slide 46
Menu Button Function
1.TEMPORARY COS
2.WALKING COS
ENTER COS OVERRIDE CODE
BACK SAVE EXIT
Enter the COS Override code.
Press the [SAVE] button to use the walking COS
5.2.2 WALKING COS
1.TEMPORARY COS
2.WALKING COS
ENTER COS OVERRIDE CODE
PRESS HOLD KEY
BACK SAVE EXIT

## Slide 47
Menu Button Function
5.3 PASSWORD
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
ENTER PASSWORD :
BACK SAVE EXIT
REGISTER PASSWORD
Press the [3] PASSWORD.
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
ENTER CURRENT PASSWORD
BACK SAVE EXIT
CHANGE PASSWORD
After entering the password(5 digits),
press the [HOLD] button to save it.
Press the [3] PASSWORD.
Enter the current password.
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
ENTER PASSWORD :
BACK SAVE EXIT
After entering the new password,
press the [HOLD] button to save it.

## Slide 48
Menu Button Function
5.4 SPEED PGM
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
BACK EXIT
Press the [4] SPEED PGM.
ENTER SPD BIN NO (000)
PAUSE FLASH D-TONE
Enter speed bin no.
e.g ) 005
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 01
ENTER CO-BTN/DIGIT (005)
PAUSE FLASH D-TONE
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 01
Enter phone number and then press the [HOLD] button.
e.g ) 12345
LORA
ENTER NAME (SPD 005)
ABC> OK
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 01
Enter name and then press the [HOLD] button.

## Slide 49
Menu Button Function
5.5 ANSWER MODE
1.ENBLOCK MODE
2.STATION COS
3.PASSWORD
4.SPEED PGM
5.ANSWER MODE
ENTER ICM ANS MODE
H (1) T (2) P (3)
BACK SAVE EXIT
Press the [5] ANSWER MODE.
There are three modes and select the desired mode. Press the [SAVE] button to save it.
[1] HANDSFREE MODE
[2] TONE MODE
[3] PRIVATE MODE

## Slide 50
Menu Button Function
6. VOICE MAIL
6.1 INTERNAL VOICE MAIL
1.INT VOICE MAIL
2.EXT VOICE MAIL
BACK EXIT
1.Ez MENU 6.VOICE MAIL
2.PHONE BOOK
3.SCHEDULE
4.CUSTOMIZE
5.SETTING
EXIT
Press the [MENU] button.
VMIB MSG FROM : STA 130
NEXT REPEAT DELETE ▶
Press the [1] button.
Press [NEXT] to hear another voice mail, press [REPEAT] to repeat the current message and to erase the message, press [DELETE].
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 03

## Slide 51
Menu Button Function
6.2 EXTERNAL VOICE MAIL
1.INT VOICE MAIL
2.EXT VOICE MAIL
BACK EXIT
> 620
BACK NEXT ANSWER
Use [NEXT] to move to the next voice mail group. To check the external voice mail, press [ANSWER].
Press the [2] button.
SUN MON TUE WED THU FRI SAT
1
2 3 4 5 6 7 8
9 10 11 12 13 14 15
16 17 18 19 20 21 22
23 24 25 26 27 28 29
30 31
2004
07 / 03

## Slide 52
Entering characters
Enter the figure
ABC
abc
NUM
Enter the letters
ABC
abc
▶
▶
Enter the symbol
ABC
abc
NUM
SYMBL
▶
▶
▶
▶
Dial
▶
Dial
▲▼ Norm
1 / 4 ◀▶
① ② ③ ④ ⑤ ⑥ ⑦ ⑧ ⑨ 0
. ( ) - ! ? * _
※ Use the button and then select the symbol.
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 53
Glossary of Terms
Intercom – describes internal calls within the telephone system
Central Office Line – also known as a trunk line or outside line
A commonly used number stored in a speed bin for easy access
Do Not Disturb – a telephone in DND will show as busy to callers
Forward – your calls can be sent to another location such a voicemail or another station
Direct Dial Inwards or Direct Inwards Dialing – ISDN lines can be provided with multiple telephone numbers which are each routed to individual extensions or Hunt Groups
Digital Key Telephone Unit – a LG digital telephone
Single Line Telephone – an analogue telephone
A type of CO line that comes in multiples of 2 or more
Voice Message Interface Board – LG’s integral Voice Processing card
Conference – where you can talk to 2 or more internal or external parties
ICM
CO Line
Speed Dial
DND
FWD
DDI or DID
DKTU
SLT
ISDN
VMIB
CONF
1
2
3
4
5
6
7
8
9
10
11