## Slide 1
Wake-up Call
To register wake-up call,
● Press TRANS/PGM button.
● Dial 4 1 (LDK-300/300E/100/24/20: 0 4 2).
● Dial the station range. In case of one station, dial the station number twice.
● After hearing confirmation tone, enter 4-digit wake-up time (HHmm) in
24-hour mode. (HH= 00~23, mm= 00~59)
● Press HOLD/SAVE button for one-day, or dial # and HOLD/SAVE button for
until canceled.
Button
Procedures
● Press the 5th menu key from the main menu to select PROGRAM.
On the display, you'll see the following.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select the ATD PROGRAM. On the display, you'll see the following.
A>WAKE-UP SET
A>WAKE-UP ERASE
A>PASSWORD ERASE
A>CHG DATE MODE
A>CHG TIME MODE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Press the 5th menu key from the main menu to select PROGRAM.
On the display, you'll see the following.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select the ATD PROGRAM and PAGE down(▼) key 4 times.
On the display, you'll see the following.
A>CHNG DATE/TIME
A>SET WAKE UP
A>DISBL WAKE UP
A>LCD DATE MODE
A>LCD TIME MODE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the SET WAKE-UP key.

## Slide 2
Wake-up Call (Cont’d)
Button
Procedures
● Enter the station range (XXX-YYY) to receive wake-up call.
● Enter 4-digit wake-up time (HHmm) in 24-hour mode.
● Press HOLD/SAVE button for one-day, or dial # and HOLD/SAVE button for
until canceled.
To cancel wake-up call,
● Press TRANS/PGM button.
● Dial 4 2 (LDK-300/300E/100/24/20: 0 4 3).
(Confirmation tone is heard and MON button is lighting.)
● Dial the station range to be canceled.
● Press HOLD/SAVE button. (MON button will be extinguished.)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select the ATD PROGRAM.
● Select the WAKE-UP ERASE key.
● Enter the station range to be canceled (XXX~YYY).
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select the ATD PROGRAM and PAGE down(▼) key 4 times.
● Select the DISBL WAKE UP key.
● Enter the station range to be canceled (XXX~YYY).
● Press HOLD/SAVE button.
Attendant Operation

## Slide 3
System Greetings
● Press # (to record with DKTU) button or * (to record with external MOH)
button after hearing the message.
● Record your greeting and hang up to finish the recording.
● To delete, press DND/FWD button while the message is played.
Button
Procedures
It provides announcements for Hunt service (UCD/Circular/Terminal) or DISA and only the
system attendant can record this message.
In GDK-16/20W,
● Press TRANS/PGM button.
● Dial # 4.
● Select the announcement type.
(1: System Greeting, 2: System Prompt)
● Dial the announcement number.
● Dial the source number (1: external MOH, 2: DKTU)
● Dial # to start recording.
● Press HOLD/SAVE button.
● You have 19 System Greetings and 9 Prompts;
System Greetings (Announcement Type 1)
1: Day Time System Greeting
2 : Night Time System Greeting
3 : Circular & Terminal Hunt Group Greeting
4 : 1st UCD Group Announcement
5 : 2nd UCD Group Announcement
6 : Ring Group Announcement (GDK-16: version 4.0XX, 20W: version 3.0XX)
7 : DVIB MOH
8 : SLT Message Waiting Indication Announcement
(GDK-16: version 4.0XX, 20W: version 3.0XX)
9 : Off-Net Forward Announcement (GDK-16: version 4.0XX, 20W: version 3.0XX)
10 : Group Overflow Announcement (GDK-16: version 4.0XX, 20W: version 3.0XX)
11-19: CCR Announcement (GDK-16: version 4.0XX, 20W: version 3.0XX)
System Prompts (Announcement Type 2)
1: Timeout Prompt 6 : No Answer Prompt
2 : Retry Prompt 7 : Transfer to Attendant Prompt
3 : Busy Prompt 8 : Authorization Code Prompt
4 : DND Prompt 9 : Record Start Prompt
5 : Invalid Prompt
● To delete announcement, dial the announcement number and #.
● Press TRANS/PGM button.
● Dial # 4.
● For DVU, dial 0 1 for announcement 1, dial 0 2 for announcement 2, or 0 3
for announcement 3. (Announcement 3 is played back when the called party
is busy.)
● For EDVU, you have 31 (01~31) system greetings;
1~9 : for Hunt or company information with DISA
10 : for Invalid message
11 : for Time-out message
12 : for Try again message
13 : for Transfer to attendant message
14 : for Leave message
15 : for Record message
16 : for Enter authorization message
17 : for MOH message
18 : for Busy message
20 : for STA off-net announcement message

## Slide 4
System Greetings (LDK-300/300E/100/24/20) (Cont'd)
To record system greetings,
● Press TRANS/PGM button.
● Dial 0 6.
● Dial the announcement number (001~100).
● “Press # button to record” is heard. Then press # button to start recording.
● Record your greeting and press HOLD/SAVE button to finish the recording.
● To delete, press SPEED button while the message is played.
● The System Prompt messages are 071~100 as default;
071: VMIB MOH 086: Reserved
072: Reserved 087: Reserved
073: Invalid Number Prompt 088: Remote VMIB Control Main Menu Prompt
074: Time out Prompt 089: Remote VMIB Sub-menu for digit 1 in
075: Retry Prompt Main Menu Prompt
076: Transfer to Attendant Prompt 090: Reserved
077: Reserved 091: Reserved
078: Leave Message Prompt 092: Reserved
079: Record Start Prompt 093: Remote VMIB Sub-menu for digit 2 in
080: Authorization Code Prompt Main Menu Prompt
081: Busy Prompt 094: Remote VMIB Sub-menu for digit 3 in
082: Reserved Main Menu Prompt
083: Station Off-net Forward Prompt 095: Remote VMIB Sub-menu for digit * in
084: DND Prompt Main Menu Prompt
085: No Answer Prompt 096: Leave Message after Tone Prompt
097~100: Reserved
Button
Procedures
Button
Procedure
This feature allows the attendant to set the Time/Date without entering Admin Programming.
● Press TRANS/PGM button.
● Dial # 1.
● Enter Date + Time. Enter as YYMMDDHHmm.
(YY= Year 00~99, MM= Month 01~12, DD= Date 01~31, HH= Hour 00~23,
mm= minute 00~59)
If there is no need to change date or time, press * key.
(YYMMDD + * or * + HHmm)
● Press HOLD/SAVE button.
In GDK-16/20W , LDK-300/300E/100/24/20,
● Press TRANS/PGM button.
● Dial # 1 (LDK-300/100/24/20 : 0 4 1).
● Enter Date as MMDDYY (6 digits) and press HOLD/SAVE button.
● Enter Time as military format (4 digits) and press HOLD/SAVE button.
If there is no need to change date or time, press HOLD/SAVE button to go to
the next step.
Attendant Clock Set
In LDK-300/300E/100/24/20,
Attendant Operation

## Slide 5
Button
Procedure
To change the date format on the LCD,
● Press TRANS/PGM button.
● Dial * 5 (LDK-300/300E/100/24/20: 0 4 4).
● The format toggles between DDMMYY and MMDDYY.
(YY : year, MM : month, DD : date)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key.
● On the display, you'll see the following.
Changing Time/Date Format
A>WAKE-UP SET
A>WAKE-UP ERASE
A>PASSWORD ERASE
A>CHG DATE MODE
A>CHG TIME MODE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the CHG DATE MODE key.
● The format toggles between DDMMYY and MMDDYY.
(YY : year, MM : month, DD : date)
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select the LCD DATE MODE key.
● The format toggles between DDMMYY and MMDDYY.
(YY : year, MM : month, DD : date)
● Press the 5th menu key from the main menu to select PROGRAM.
On the display, you'll see the following.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the ATD PROGRAM and PAGE down(▼) key 4 times.
On the display, you'll see the following.
A>CHNG DATE/TIME
A>SET WAKE UP
A>DISBL WAKE UP
A>LCD DATE MODE
A>LCD TIME MODE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼

## Slide 6
Button
Procedure
To change the time format on the LCD,
● Press TRANS/PGM button.
● Dial * 6 (LDK-300/300E/100/24/20: 0 4 5).
● The format toggles between 12-hour mode and 24-hour mode.
(YY : year, MM : month, DD : date)
Changing Time/Date Format (Cont’d)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key.
● Select the CHG TIME MODE key.
The format toggles between 12 and 24-hour mode.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key PAGE down(▼) key 4 times.
● Select the LCD TIME MODE key.
The format toggles between 12 and 24-hour mode.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
To Set Current Time 1 Hour Early/Late (Only in GDK-16/20W)
Button
Procedure
To set the current time 1 hour early,
● Press TRANS/PGM button.
● Dial ＊ 1.
To set the current time 1 hour late,
● Press TRANS/PGM button.
● Dial ＊ 2.
Attendant Operation

## Slide 7
Button
Procedure
To store system speed numbers,
● Press TRANS/PGM button.
● Dial SPEED button.
● Dial speed number bin.
● Dial the phone numbers to be stored.
● Dial HOLD/SAVE button.
Or,
● Press TRANS/PGM button.
● Dial SPEED button.
● Dial speed number bin.
● Press desired outside line button.
● Dial the phone numbers to be stored.
● Dial HOLD/SAVE button.
To use system speed numbers,
● Press SPEED button.
● Dial speed number bin.
A group of speed dial numbers can be stored within the system for access by allowed stations.
These numbers provide speedy access to often used outgoing CO dialing numbers.
LDK-300 : 2000~4999
LDK-300E : 2000~6999
LDK-100/24 : 2000~3499
LDK-20:2000~2499
GDK-162 : 200~999
100 : 200~399
FPII : 200~399
16/20W : 21~99
System Speed Dial
Attendant Intrusion
Button
Procedure
To assign a flexible key as the Intrusion button
(Not available in GDK-16/20W),
● Press TRANS/PGM button.
● Press the desired flexible key to be registered.
● Press TRANS/PGM button.
● Dial 8 6.
● Press HOLD/SAVE button.
To activate attendant intrusion (LDK-300/300E/100/24/20,
GDK-162/100/FPII),
● Press DSS button corresponding to the busy station you wish to call.
(Busy tone is heard.)
● Press ATD INTRUSION button.
(Intrusion warning tone is heard in the busy station, then a 3-way
conference is set up.)
To activate attendant intrusion (GDK-16/20W),
● Press CO button you wish to converse.
(If intrusion is allowed by Admin program, then 3 way conversation is set
up. If intrusion is not allowed, busy tone will be heard.)
● System Base Program (Main Menu 5) - System Attribute (Sub Menu 1)
- Privacy (Terminal Menu 2)
Attendant may intrude into any station which is in conversation with a CO line.

## Slide 8
Day/On-demand/Night Mode Service (Manual/Automatic)
To activate/deactivate Day/Night/On-demand mode manually,
● Press DND/FWD button at attendant station.
● Then, DND/FWD button is flashing. (The system is placed into On-demand
mode.)
● If pressing the DND button one more, then the system is placed into Night
service mode.
● On-demand mode is not activated automatically.
Button
Procedures
To change Day/Night mode automatically,
● Press TRANS/PGM button.
● Dial # 9.
● Enter DAY TIME + NIGHT TIME, or DAY TIME + * or * + NIGHT TIME .
(Enter as HHmm (HH= hour 00~23, mm= minute 00~59)
● Press HOLD/SAVE button.
The attendant station can be placed into night service mode allowing ring assignments and
answering privileges to station not having the privileges in the day mode. Or, can be placed
into on-demand service mode allowing ring assignments and answering privileges to station
not having the privileges in the night mode.
(In GDK-16, only Day/Night mode change is available by pressing DND button at attendant
station.)
To activate/deactivate Day/Night/On-demand/Weekend/Auto mode manually,
● Pressing DND/FWD button, the ring mode is changed to
On-demand  Night  Weekend Auto  Day mode in sequence.
● On-demand mode is not activated automatically.
Button
Procedures
To activate Auto ring mode with Attendant PGM mode,
● Press TRANS/PGM button.
● Dial 0 7 4.
● Dial 1 and press HOLD/SAVE button.
(The Weekly Time Table should be entered by Admin Programming.)
The system can be placed in Day/On-demand/Night/Weekend/Auto mode operation manually
by pressing [DND/FWD] button at attendant station. In Auto ring mode, the ring mode will follow
the Weekly Time Table (PGM 233).
Day/On-demand/Night/Weekend Mode Service (LDK-300/300E/100/24/20)
Attendant Operation

## Slide 9
To activate/deactivate Day/Night/Auto Ring mode manually,
● Pressing DND/FWD button, the ring mode is changed to Night  Auto Ring
 Day mode in sequence.
Button
Procedures
To activate Auto ring mode with Attendant PGM mode,
● The Weekly Time Table should be entered by Admin Programming
The system can be placed in Day/Night/Auto Ring mode operation manually by pressing
[DND/FWD] button at attendant station. In Auto ring mode, the ring mode will follow the Weekly
Time Table in Admin Programming(Main 5- Sub21 ).
Auto Ring mode is available for ver 4.0XX(GDK-16) and 3.0XX(GDK-20W)
Day/Night/Auto Ring Mode Service (GDK-16/20W)
● Press the 4th menu key from the main menu to select FEATURE.
On the display, you will see the following.
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Button
Procedures
STA PRT SMDR
ACT GRD PRT SMDR
STA DEL SMDR
ACT GRP DEL SMR
DISP CALL CHARGE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select STA PRT SMDR key.
● Enter the desired station range to be printed.
● Press HOLD/SAVE button.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
For station basis,
● Dial * 0
(LDK-300/300E100/24/20: TRANS/PGM+0111, GDK-16/20W: TRANS/PGM + * 81)
● Enter the desired station range.
● Press HOLD/SAVE button.
Accumulated SMDR records will be printed out through the printer
connected to KSU.
(GDK 16: Above V4.0
20W : Above V3.0)
Station Message Detail Recording(SMDR) can provide details on both incoming and outgoing
calls.
To Print out Accumulated SMDR Records

## Slide 10
Button
Procedures
To Print out Accumulated SMDR Records (Cont'd)
● Press the 5th menu key from the main menu to select PROGRAM.
On the display, you will see the following.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Attendant Operation
● Select ATD PROGRAM key. On the display, you will see the following.
For account group basis,
● Dial * 1 (LDK-300/300E/100/24/20: TRANS/PGM + 0 1 1 3).
● Enter the desired account group to be printed.
● Press HOLD/SAVE button.
(Accumulated SMDR records will be printed out
through the printer connected to KSU.)
LDK-300/300E : 01~99
LDK-100/24/20 : 01~23
GDK-162 : 01~99
100 : 01~24
FPII :01~24
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from the main menu to select FEATURE.
● Press PAGE down(▼) key 4 times.
● Select ACT GRP PRT SMDR key.
● Enter the account group to be printed.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select ATD PROGRAM key.
● Select GRP PRT SMDR key.
● Enter the account group to be printed.
● Press HOLD/SAVE button.
A>STA PRT SMDR
A>STA DEL SMDR
A>GRP PRT SMDR
A>GRP DEL SMDR
A>DISP CALL CHRG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select STA PRT SMDR key.
● Enter the desired station range to be printed.
● Press HOLD/SAVE button.

## Slide 11
Button
Procedure
To Erase SMDR Records
Or using display, (Only in KD-33LD, KD/E-36LD , LKD-30LD)
● Press the 4th menu key from the main menu to select FEATURE.
● Press PAGE down(▼) key 4 times.
● Select STA DEL SMDR key.
● Enter the station range to be erased.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD , LKD-30LD)
● Press the 5th menu key from the main menu to select FEATURE.
● Select ATD PROGRAM key.
● Select STA DEL SMDR key.
● Enter the station range to be erased.
● Press HOLD/SAVE button.
For call account group basis,
● Dial * 3 (LDK-300/300E/100/24/20: TRANS/PGM + 0 1 1 4).
● Enter the desired account group.
(SMDR records will be erased for all stations in the range.)
● Press HOLD/SAVE button.
Or using display, (Only in KD-33LD, KD/E-36LD , LKD-30LD)
● Press the 4th menu key from the main menu to select FEATURE.
● Press PAGE down(▼) key 4 times.
● Select ACT GRP DEL SMDR key.
● Enter the account group to be erased.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD , LKD-30LD)
● Press the 5th menu key from the main menu to select FEATURE.
● Select ATD PROGRAM key.
● Select GRP DEL SMDR key.
● Enter the station range to be erased.
● Press HOLD/SAVE button.
For station basis,
● Dial * 2
(LDK-300/300E/100/24/20: TRANS/PGM+0112, GDK-16/20W: TRANS/PGM *82).
● Enter the desired station range.
(SMDR records will be erased for all stations in the range.)
● Press HOLD/SAVE button.
(GDK 16: Above V4.0
20W : Above V3.0)

## Slide 12
Button
Procedure
To Erase SMDR Records (Cont'd)
To display call charge,
● Dial * 4 (LDK-300/300E/100/24/20: TRANS/PGM + 0 1 1 5).
● Enter the station number.
● Press HOLD/SAVE button.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from the main menu to select FEATURE.
● Press PAGE down(▼) key 4 times.
● Select DISP CALL CHARGE key.
● Enter the desired station number.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD , LKD-30LD)
● Press the 5th menu key from the main menu to select FEATURE.
● Select ATD PROGRAM key.
● Select DISP CALL CHRG key.
● Enter the desired station number.
● Press HOLD/SAVE button.
Button
Procedure
● Press TRANS/PGM button.
● Dial # 8 (LDK-300/300E/100/24/20: 0 7 2).
● Dial the station number and enter the name using the code shown below.
● Press HOLD/SAVE button.
Dial by Name (for ICM) (＊)
Attendant Operation

## Slide 13
Button
Procedure
Dial by Name (for ICM) (＊) (Cont'd)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key.
● Press PAGE down(▼) key 3 times. On the display, you'll see the following.
A>USER DIAL NAME
A>AUTO DAY-NIGHT
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Dial the station number and enter the name using the code.
● Press HOLD/SAVE button.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key.
● Press PAGE down(▼) key 6 times. On the display, you'll see the following.
A>STA CLI AL DEL
A>REC VMIB ANNC
A>CANCEL FEAT
A>REG STA NAME
A>DISABLE CO OUT
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the REG STA NAME key.
● Dial the station number and enter the name using the code.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Customized Message (＊)
Button
Procedure
● Press TRANS/PGM button.
● Dial * 7 (LDK-300/300E/100/24/20: 0 5 3).
● Dial the number of the desired message (11~20).
● Enter the desired message using the code in Dial by Name.
● Press HOLD/SAVE button.

## Slide 14
CO Outgoing Disable (＊)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key.
● Press PAGE down(▼) key once. On the display, you'll see the following.
(In LDK-300/300E/100/24/20, press PAGE down(▼) key 6 times.)
● Select the DISABLE CO OUT key.
● Press the desired outside line button. (Confirmation tone is heard.)
Button
Procedure
To disable outgoing calls a CO line,
● Press TRANS/PGM button.
● Dial * 8 (LDK-300/300E/100/24/20: 0 7 3).
● Press the desired outside line button. (Confirmation tone is heard.)
● After hearing confirmation tone, selected outside line button is disabled.
● Repeat the process to enable the CO line.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
To activate temporary COS change,
● Press TRANS/PGM button.
● Dial # 2 (LDK-300/300E/100/24/20: 0 2 1).
● Enter the station range.
● Press HOLD/SAVE button.
Button
Procedures
A station user can change the class of service to lower class temporarily to prevent unauthorized
use of the station by others.
To remove temporary COS change,
● Press TRANS/PGM button.
● Dial # 3 (LDK-300/300E/100/24/20: 0 2 2).
● Enter the station range.
● Press HOLD/SAVE button.
Temporary COS Change (＊)
A>DISABLE CO OUT
A>STA MSG ERASE
A>SET ICMBOX MSC
A>CLOCK SET
A>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
A>STA CLI AL DEL
A>REC VMIB ANNC
A>CANCEL FEAT
A>REG STA NAME
A>DISABLE CO OUT
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
<LDK-300/300E/100/24/20>
Attendant Operation

## Slide 15
Button
Procedure
To start the traffic analysis at system attendant,
● Press TRANS/PGM button.
● Dial # 7 1.
● Press HOLD/SAVE button.
To stop the traffic analysis at system attendant,
● Press TRANS/PGM button.
● Dial # 7 2.
● Press HOLD/SAVE button.
To print the result of traffic analysis at system attendant,
● Press TRANS/PGM button.
● Dial # 7 3.
● Press HOLD/SAVE button.
To abort printing at system attendant,
● Press TRANS/PGM button.
● Dial # 7 4.
● Press HOLD/SAVE button.
The system will monitor the system and record various traffic data which can be printed upon
request. The information can be used to determine whether the circuits installed in the system
are adequate.
When enabled, it will continue to monitor the traffic until disabled. The traffic data is collected
and sent to the RS232C port upon request. The collected traffic data contains two types of
traffic data.
The first type is peg counts which give an actual count of the number of times a particular
operation has occurred. Peg counts are given in absolute values from 00000 to 99999. The
second type of data is usage times which give the average percent occupancy of a device, i.e.,
stations, CO lines, DTMF receivers, etc. Usage times are given in seconds from 00000 to
99999. Counts and times are cumulative from the time the monitoring is activated, and are
reset by initiating the start up procedure again.
Traffic Analysis (＊)

## Slide 16
Button
Procedure
To print all summary at system attendant,
● Press TRANS/PGM button.
● Dial 0 1 2 1.
● Select Measurement Time type.
● Press HOLD/SAVE button.
To print all summary traffic report periodically at system attendant,
● Press TRANS/PGM button.
● Dial 0 1 2 2.
● Press HOLD/SAVE button.
To cancel periodic printing of all summary traffic reports,
● Press TRANS/PGM button.
● Dial 0 1 2 3.
● Press HOLD/SAVE button.
To print the traffic report,
● Press TRANS/PGM button.
● Dial 0 1 2 4 (Attendant Traffic Report)
0 1 2 5 (Call Summary Report)
0 1 2 6 (Call Hourly Report)
0 1 2 7 (H/W Unit Usage Summary Report)
0 1 2 8 (CO Traffic Report)
0 1 2 9 (CO Traffic Hourly Report)
● Press HOLD/SAVE button.
Traffic Analysis (LDK-300/300E/100/24/20) (Cont'd)
Button
Procedure
The attendant can cancel the features, DND CALL FORWARD and preselected message
activating at other station.
● Press TRANS/PGM button.
● Dial * 9 (LDK-300/300E/100/24/20: 0 7 1).
● Dial the desired station range to be canceled.
● Press HOLD/SAVE button.
Erasing Station Message (＊)
The system can monitor and print various system activate based on the attendant’s request.
The traffic-monitoring program is activated only when enabled and will continue accumulating
statistics until disabled. The traffic data is output to the RS-232C port upon manual request.
The system will support the following traffic reports; Attendant Traffic Report, Call Summary
Report, Call Hourly Report, H/W Unit Usage Summary Report, CO Traffic Report and CO Traffic
Hourly Report.
Attendant Operation

## Slide 17
Type (00~25)
GDK-162 GDK-FPII/100 Language
0 0 0 0 English
0 1 0 1 Korean
0 2 0 2 Italian
0 3 0 3 English for Large LCD
0 4 0 4 Swedish
0 5 0 5 Norwegian
0 6 0 6 Finnish
0 7 0 7 Dutch
0 8 0 8 Spanish
0 9 0 9 Korean for Large LCD
1 0 1 0 Danish
. . 1 1 German
. . 1 2 German for Large LCD
1 3 1 3 Estonia
1 2 1 4 Estonia for Large LCD
1 4 1 5 Swedish for Large LCD
1 5 1 6 Italy for Large LCD
1 6 1 7 Norway for Large LCD
1 7 1 8 Finnish for Large LCD
1 8 1 9 Dutch for Large LCD
2 0 2 0 Russian
9 2 1 Spanish for Large LCD
2 1 2 2 Russian for Large LCD
1 1 2 3 Danish for Large LCD
2 2 2 4 Portuguese
. . 2 5 Portuguese for Large LCD
Button
Procedure
Attendant LCD Language
To change the LCD language at attendant,
● Press TRANS/PGM button.
● Dial 5 1 (LDK-300/300E/100/24/20: 0 7  ).
● Dial the station range to be changed.
● Select the language type with the following codes.
(GDK-16/20W: English / Each Nation’s Language)
● Press HOLD/SAVE button.
LDK-300/300E/100/24/20
:Type (00~14)
LDK-300/300E Language
/100/24/20
0 0 English
0 1 Italian
0 2 Finnish
0 3 Dutch
0 4 Swedish
0 5 Danish
0 6 Norwegian
0 7 Hungarian
0 8 Germany
0 9 French
1 0 Portuguese
1 1 Spanish
1 2 Korean
1 3 Estonia
1 4 Russian
In GDK16 / 20W (16: 4.0XX & 20W: 3.0XX)
To change the LCD language at attendant,
● Press TRANS/PGM button.
● Dial 5 1
● Dial the station range to be changed.
● Select the language ( English / Each Nation’s Language)
● Press HOLD/SAVE button.

## Slide 18
Button
Procedure
To set ICM box music,
● Press TRANS/PGM button.
● Dial * 0 (LDK-300/300E/100/24/20: 0 7 5).
● Dial the music channel (0~9, LDK-300/300E: 01~12, LDK-100:01~11,
LDK-24/20:1~8).
● Press HOLD/SAVE button.
The attendant can select the music channel source to an ICM box.
Intercom Box BGM Selection by Attendant (＊)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key. On the display, you will see the following.
A>WAKE-UP SET
A>WAKE-UP ERASE
A>PASSWORD ERASE
A>CHG DATE MODE
A>CHG TIME MODE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press PAGE down(▼) key once.
You'll see the following.
A>DISABLE CO OUT
A>STA MSG ERASE
A>SET ICMBOX MSC
A>CLOCK SET
A>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the SET ICMBOX MSC.
● Press the Music type;
0 : No music
1~9 : Music from channel 1~9
● Press HOLD/SAVE button.
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key. On the display, you will see the following.
A>STA PRT SMDR
A>STA DEL SMDR
A>GRP PRT SMDR
A>GRP DEL SMDR
A>DISP CALL CHRG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Attendant Operation

## Slide 19
● Select the ICMBX MSC SEL.
● Press the Music type;
00 : No music
LDK-300/300E: 01~12 ( Music from channel 1~12 )
LDK-100: 01~11 ( Music from channel 1~11 )
LDK-24/20: 1~8 ( Music from channel 1~8 )
● Press HOLD/SAVE button.
● Press PAGE down(▼) key 7 times.
You'll see the following.
A>AUTO D/N/W
A>ICMBX BGM SEL
A>BGM TO EXT 1
A>BGM TO EXT 2
A>BGM TO EXT 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Button
Procedure
Intercom Box BGM Selection by Attendant (＊) (Cont'd)
Button
Procedure
To set External Page Port music,
● Press TRANS/PGM button.
● Dial 0 7 6 (External Port 1), 0 7 7 (External Port 2), or 0 7 8 (External Port 3).
● Dial the music channel (LDK-300/300E:01~12, LDK-100:01~11, LDK-24/20:1~8).
● Press HOLD/SAVE button.
External Page Port BGM Selection by Attendant (Only in LDK-300/300E/100/24/20)
● Press the 5th menu key from the main menu to select PROGRAM.
● Select the ATD PROGRAM key and press PAGE down(▼) key 7 times. Then
you will see the following.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
A>AUTO D/N/W
A>ICMBX BGM SEL
A>BGM TO EXT 1
A>BGM TO EXT 2
A>BGM TO EXT 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select the BGM TO EXT 1~3.
● Press the Music type;
00 : No music
LDK-300/300E : 01~12 ( Music from channel 1~12)
LDK-100 : 01~11 ( Music from channel 1~11)
LDK-24/20: 1~8 ( Music from channel 1~8 )
● Press HOLD/SAVE button.

## Slide 20
Button
Procedure
Button
Procedures
● Lift handset or press MON button.
● Press the desired DSS station button.
● Hang up or press RELEASE button to terminate the call.
Making a Page
Button
Procedure
● Lift handset or press MON button.
● Press PAGE button.
● Speak in normal voice tone to announce message.
● Hang up or press RELEASE button.
Transferring an Outside Line to Another Station
● While connecting an outside line, press the desired DSS station button.
● You can wait to announce the transfer or,
● Hang up or press RELEASE button.
Attendant DSS Operation /Placing an Intercom Call from the DSS
Button
Procedure
● Lift handset or press MON button.
● Press the programmed INTERCOM GROUP CALL button.
● The call is connected to an idle station in the group.
Overriding a Key Telephone in Do Not Disturb
Button
Procedure
● Press DSS button of the station to be overridden. (DND tone or busy tone is
heard.)
● Press programmed OVERRIDE button.
Intercom Group Call (＊)
● Press DSS button of the station to be overridden. (DND tone or busy tone is
heard.)
● Dial * to override the station in DND or in busy.
In LDK-300/300E/100/24/20, GDK-16/20W
Attendant Operation

## Slide 21
Attendant Programming Menu Table
The attendant can program some features with this table by pressing TRANS/PGM button
and appropriate codes.
Attendant Main
Menu
Attendant
Sub Menu - I
Attendant
Sub Menu
- II
Selection
Remark
[1] PRINT SMDR
(STA BASE)
STN# (+ END STN#)
MAIN ATD
[2] DELETE (STA BASE)
STN# (+ END STN#)
MAIN ATD
[3] PRINT SMDR
(GRP BASE)
GRP# (+ END GRP#)
MAIN ATD
[4] DELETE (GRP BASE)
GRP# (+ END GRP#)
MAIN ATD
[5] DISPLAY CALL
CHARGE
MAIN ATD
[6] ABORT PRINTING
None
MAIN ATD
[7] PRINT LOST CALL
MAIN ATD
[1] SMDR
[8] DELETE LOST CALL
MAIN ATD
[1] PRINT ALL
SUMMARY
Analysis Time Type
MAIN ATD
[2] PRINT ALL
PERIODIC
Analysis Time Type
, Print Time (Hour)
MAIN ATD
[3] ABORT PERIODIC
PRINT
None
MAIN ATD
[4] PRINT ATD
TRAFFIC
Analysis Time Type
MAIN ATD
[5] PRINT CALL
SUMMARY
None
MAIN ATD
[6] PRINT CALL
HOURLY
None
MAIN ATD
[7] PRINT H/W USAGE
Analysis Time Type
MAIN ATD
[8] PRINT CO
SUMMARY
Analysis Time Type
MAIN ATD
[1]PRINT
[2] TRAFFIC
[9] PRINT CO HOURLY
Enter CO
Grp #
MAIN ATD
[1] SET ICM ONLY
MODE
STN#
(+ END STN#)
[2]COS
[2] RESTORE COS
STN#
(+ END STN#)
[3]AUTHORIZATION
[1] CHANGE
AUTHORIZATION
STN# (+ END STN#)
MAIN or
GROUP ATD
[1] CHANGE
DATE/TIME
MM/DD/YY
MAIN ATD
[2] SET WAKE UP
STN# (+ END STN#)
MAIN or
GROUP ATD
[3] DISABLE WAKE
UP
STN# (+ END STN#)
MAIN or
GROUP ATD
[4] LCD DATE MODE
MMDDYY/DDMMYY
MAIN ATD
[5] LCD TIME MODE
12H/24H
MAIN ATD
[4]TIME
[6] USE PX TIME
/DATE
ON/OFF
MAIN ATD

## Slide 22
Attendant Programming Menu Table (Cont'd)
Attendant Main
MENU
Attendant
Sub Menu - I
Attendant
Sub Menu - II
Selection
Remark
[1] PRESELECT MSG
ACT
STN# (+ END STN#)
+ MSG #(00-10)
MAIN or
GROUP ATD
[2] PRESELECT MSG
DEACT
STN# (+ END STN#)
MAIN or
GROUP ATD
[3] CUSTOM MSG
REG
MSG # (11-20)
+ MSG STREAM
MAIN or
GROUP ATD
[4] ERASE VM MSG
STN# (+ END STN#)
[5] MESSAGE
[5] ATD DEL ALL CLI
MSG
[6] REC. VMIB
ANNOUNCEMENT
VMIB ANNC# (01-70)
SYSTEM ATD
[1] CANCEL
FEATURES
STN# (+ END STN#)
MAIN or
GROUP ATD
[2] RESISTER STA
NAME
STN# + NAME
MAIN ATD
[3] DISABLE
CO OUTGOING
PRESSING CO BTN
MAIN ATD
[4] AUTO RING
MODE
ATD/AUTO
[5] ICM BOX BGM
BGM CHANNEL #
(01-12)
MAIN ATD
[6] EXT PORT#1 BGM
EN/DI
ENABLE / DISABLE
MAIN ATD
[7] EXT PORT#2 BGM
EN/DI
ENABLE / DISABLE
MAIN ATD
[8] EXT PORT#3 BGM
EN/DI
ENABLE / DISABLE
MAIN ATD
[9] PREPAID CALL
[7]
SUPPLEMENTARY
[*] LCD DISPLAY
LANGUAGE
[*] BOARD
SERVICE SWITCH
SLOT NUMBER
(01 – 27)
[#] WHTU
SUBSCRIBE
FLEX 1 – FLEX 9
CH SEL
Attendant Operation