## Slide 1
Placing an Outside Call
● Lift handset or press MON button.
● Press outside line button, pool button or dial CO line access
code.
● Dial desired party.
● When called party answers, lift handset or use speakerphone.
9 (or 0), 8 +
LDK-300:01~72
LDK-300E:01~72
LDK-100:01~24
LDK-24/20 :1~8
162 : 01 ~ 48
100 : 01 ~ 24
FPII : 01 ~ 09
16/20W: 1 ~ 4
Or, 88 +
LDK-300:001~200
LDK-300E:
001~400
LDK-100:01~40
LDK-24 :01~12
LDK-20 :01~08
162 : 01 ~ 96
100 : 01 ~ 48
FPII : 01 ~ 34
16 : 1 ~ 6
20W : 1 ~ 8
Button
Procedures
Range
Call Transfer
Button
Procedures
To transfer an outside call to the other extension,
● Press TRANS/PGM button. (The outside call is put on hold.)
● Dial station number or appropriate DSS button.
● You can make a screened or unscreened transfer.
When the called extension answers, notice the call transfer and
hang up to complete call transfer.
While the station you called rings, hang up to complete call
transfer.
To answer screened transfer,
● When a station rings according to Intercom Answer Mode
selection, answer the intercom call.
● The transferring party hangs up, the call will be connected.
Range
LDK-300:100~399
LDK-300E:
1000~1599
LDK-100:100-227
LDK-24:10-41
LDK-20:10-25
162 : 100 ~ 291
100 : 100 ~ 235
FPII: 100 ~ 177
16 : 100 ~ 115
16E: 100 ~ 121
20W: 100 ~ 133
Screened
Transfer
Unscreened
Transfer
Note : The feature which is marked (＊), is not available in GDK-16/GDK-20W.
CO Line Features
Answering an Outside Call
Button
Procedures
Range
● Lift handset or press MON button to use speakerphone.
● Press flashing CO line button or loop key.
(If the Preferred Line Answer feature is ON for your station,
you may answer just by lifting handset.)

## Slide 2
Last Number Redial
The last dialed number on an outside line is saved.
To redial the last dialed number,
● Press REDIAL button. Or,
● Press SPEED + *.
Save Number Redial (＊)
Button
Procedures
Range
If you want to save a number you dialed,
● After dialing the number of an outside party, keep handset
off-hook state.
● Press SPEED button twice.
● Hang up.
To dial a saved number,
● Press SPEED + #.
Button
Procedures
Range
In LDK-300/300E/100/24/20
Each station with LCD has 10 individual last dialed number
directory.
To use one of dialed numbers in the directory by scrolling,
● Press REDIAL button. Or,
● Press SPEED + *.
● When the last dialed number is displayed. Press VOLUME
(▲/▼) button to find a phone number.
● Press HOLD/SAVE button then, the number is dialed.

## Slide 3
Button
Procedures
Range
● Press the programmed DIAL MEMO button.
To program [DIAL MEMO] button,
[TRANS/PGM] + flexible button + [TRANS/PGM] + 8 0 +
[HOLD/SAVE]
● Dial the desired number.
● Press DIAL MEMO button again to save.
To dial the dial memo number,
● Press SPEED + #.
To check the dial memo number,
● In idle state, press DIAL MEMO button.
● The saved number is displayed on the LCD.
While on an outside line or intercom call, you may enter and save a number in the save number
redial bin for future use. (This feature is not available in LDK-300/300E/100/24/20 system.)
Dial Memo (＊)
Button
Procedures
Range
● Press REDIAL button.
● Hang up.
● A busy or no answer number will be redialed automatically
after pre-programmed time interval while MUTE button is
lighting.
● When called party answers, lift handset to talk.
When the called party is busy or does not answer the call, the system can automatically redial
the number by pre-programmed time interval.
Queuing
Button
Procedures
Range
● Lift handset or press MON button.
● Press busy outside line button or specific line group button.
● Pressing CALLBK button, your CALLBK button is lighting
and confirmation tone is heard.
● Hang up or press MON button.
To answer a queue request,
● When the busy CO line or specific line group returns to idle,
you hear ring and the queued line button is flashing.
● Lift handset and dial a desired phone number.
When a CO line is busy, you can request a call back when the CO line is available. As soon as it
becomes idle, you can be the first extension to get the CO line.
Auto Call Number Redial
16: Above V4.0
20W: Above V3.0
16: Above V4.0
20W: Above V3.0
CO Line Features

## Slide 4
Executive/Secretary Transfer (＊)
Button
Procedures
● When the Executive Station is busy or DND (Do Not Disturb),
all calls will go to the Secretary Station.
● The Secretary Station may signal the Executive Station that is
in DND by using Call Wait feature. (Press * key or dial the last
digit of the number of Executive station or press the DSS
button to operate Call Wait feature.)
Range
Button
Procedures
Range
● Dialing an extension number, and the station is busy.
● After hearing ICM busy tone, dial the last digit of the next
extension number in the same 10’s group.
(ex. If station “112” is busy, dial digit “4” to call station “114”.)
● It can be used for CO line call by pressing SPEED button +
last digit.
When an extension is busy, you can make a call to a different station by dialing only the last digit
of new station number.
Button
Procedures
Range
Station Speed bin
LDK-300 :000~099
LDK-300E:000~099
LDK-100 : 000~099
LDK-24/20 : 000~099
162/100/FPII: 00~19
/16/20W
GDK-16/20W:
Line group button
is not available.
Each extension can program up to 20 individual speed dial numbers in the station. The numbers
are entered and stored by the user and it can be recalled at any time.
Speed Dial Numbers (Station Basis)
Step Call (＊)
To store station speed numbers,
● Press TRANS/PGM button.
● Press SPEED button.
● Dial speed number bin.
● Dial the phone numbers to be stored.
● Press HOLD/SAVE button.
● Enter name for Dial by Name. (optional)
Or,
● Press TRANS/PGM button.
● Press SPEED button.
● Dial speed number bin.
● Press desired outside line or specific line group button.
● Dial the phone number to be stored.
● Press HOLD/SAVE button.
● Enter name for Dial by Name. (optional)
● Press HOLD/SAVE button.
Dial by Name :
16: Above V4.0
20W: Above V3.0

## Slide 5
Button
Procedures
To use station speed numbers,
● Lift handset or press MON button.
● Press SPEED button.
● Dial speed number bin.
To use system speed numbers,
● Lift handset or press MON button.
● Press SPEED button.
● Dial speed number bin.
To erase station speed numbers,
● Press TRANS/PGM button.
● Press SPEED button.
● Dial speed number bin to be erased.
● Press HOLD/SAVE button.
Range
System Speed bin
LDK-300:
2000~4999
LDK-300E:
2000~6999
LDK-100/24:
2000~3499
LDK-20:
2000~2499
162 : 200~999
100 : 200~399
FPII : 200~399
16/20W : 21~99
Speed Dial Numbers (Station Basis) (Cont'd)
Button
Procedures
● Press TRANS/PGM button.
● Press SPEED button and speed number bin.
● Dial the desired phone number.
● Press HOLD/SAVE button.
● Enter the name up to 16 letters using the code below;
Users for digital display phone can enter the called party’s name so they can dial by name
instead of dialing the phone number.
● Press HOLD/SAVE button.
● Pressing [▼] key while entering name, the last character will
be erased.
Storing Dial by Name
In LDK-300/300E/100/24/20, GDK-16/20W
16 : Above V4.0
20W : Above V3.0
CO Line Features
Range

## Slide 6
Call Park
Button
Procedures
While connected to an outside call,
● Press TRANS/PGM button.
● Dial parking location.
Range
LDK-300/300E
:601~619
LDK-100:601~610
LDK-24/20 :601~608
162 : 601~619
100 : 601~610
FPII: 601~605
16/20W: 601~606
(16: Above V4.0,
20W: Above V3.0)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from main menu and you will see
the following on the display.
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
A call can be parked in a parking location and the call will be retrieved by dialing the location
number. (The call can be picked up by other extension with making a page announcement to
inform the parking location.)
● Press PAGE down(▼) key, and you will see the following
on the display.
CALL PARK (01-19)
GROUP PICKUP
DIR PICKUP (STA#)
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select CALL PARK.
To retrieve a parked call,
● Lift handset or press MON button.
● Dial parking location.
Button
Procedures
● Lift handset or press MON button.
● Press flashing CO line button. If a CO line button is not
assigned, dial 6 9. (LDK-300/300E/100/24/20: dial 5 6 9)
● You will be connected to ringing outside line.
Range
Universal Night Answer (＊)
When CO lines are programmed for UNA and the system is placed into night mode, users can
answer incoming CO line calls employing dial code regardless of pick-up group.

## Slide 7
Button
Procedures
Range
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from main menu and you will see
the following on the display.
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Press PAGE down(▼) key twice, and you will see the
following on the display.
Universal Night Answer (Cont'd)
● Select UNIV ANSWER(UNIV NITE ANSWER in LDK-300/
300E/100/24/20) key.
If an outside line is assigned for UNA and the attendant
station is placed into night service mode, you will be
connected to ringing outside line.
ACC CO-GR (01-48)
ACC 1 CO (01-96)
UNIV NITE ANSWER
TIE ROUTE (01-30)
ALARM RESET
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
ACC 1 C0 (1-200)
ACC CO_GR(01~72)
TIE ROUTE(01-30)
CALL PARK(01-19)
UNIV NITE ANSWER
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
● Press TRANS/PGM button.
● Dial 4 9 (LDK-300/300E/100/24/20: 1 2).
● Dial 1 for Handsfree, 2 for Tone ring, or 3 for Privacy
announce.
● Press HOLD/SAVE button.
Button
Procedures
Range
Changing Intercom Answer Mode
CO Line Features

## Slide 8
Button
Procedures
Range
● Dial intercom number or press programmed DSS button.
● You will hear,
- Ring back tone in TN (Tone) mode. Wait for called station
to answer the ringing.
- 3 bursts of tone in HF(Handsfree) or PV(Privacy) mode.
Begin your announcement after the tone.
Answering an Intercom Call
Button
Procedures
● With your intercom answer mode setting,
- in TN mode, intercom ring is heard. Lift handset to talk.
- in PV mode, 3 bursts of tone and one-way announcement is
heard. Lift handset to talk.
- in HF mode, 3 bursts of tone and announcement is heard.
Reply with handsfree mode or lift handset for privacy.
Range
Placing an Intercom Call
● If your phone has ICM button, you may put an intercom call
on hold by pressing HOLD/SAVE button.
● Or, while on an intercom call, press ICM button.
● The ICM button flashes and intercom dial tone will be heard.
To retrieve intercom call on hold,
● Press the flashing ICM button and lift handset.
Button
Procedures
Range
Placing an Intercom on Hold (＊)

## Slide 9
Changing Differential Ring
Button
Procedures
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from main menu to select PROGRAM
and you’ll see the following on the display.
ATD PROGRAM
STATIONPROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select STATION PROGRAM.
On the display, you will see the following.
● Press PAGE down(▼) key twice.
On the display, you will see the following.
● Press TRANS/PGM button.
● Dial 5 0 (LDK-300/300E/100/24/20 : 1 1).
● Select the ring type by dialing 1~4.
● Press HOLD/SAVE button.
Range
● Select DIFFER RING key.
● Select the ring type (1~4) by pressing dial button 1~4.
● Press HOLD/SAVE button.
S>WAKE-UP SET
S>WAKE-UP ERASE
S>REG PASSWORD
S>CHG PASSWORD
S>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
S>RING TYPE
S>ANSWER MODE
S>COS DOWN
S>RESTORE COS
S>WALKING COS
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
S>DIFFER RING
LGE/GS86P-5.5Ca
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
S>RING TYPE
S>ANSWER MODE
S>COS DOWN
S>RESTORE COS
S>WALKING COS
RING TYPE
1~4 : 1
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
Intercom Features

## Slide 10
Button
Procedures
● When a busy keyset engaged in an internal or external call is
called through camp-on by a caller, HOLD/SAVE button of
busy keyset is flashing.
After tone, the busy keyset can be connected to both parties.
● Press HOLD/SAVE button in the busy keyset to converse with
new call.
● Press HOLD/SAVE button again to alternate the call.
This feature provides voice announcement to a busy station without interrupting the existing
conversation. The announcement is received over the existing conversation so that only the
busy station hears both incoming parties.
Voice Over (＊)
Answering a Call Wait with Voice Over
Button
Procedures
● You hear camp-on tone and HOLD/SAVE button is flashing.
● Press HOLD/SAVE button to talk with the second caller.
The first caller is placed on hold. (MOH may be provided)
● You will be connected to the first caller when the second caller
hangs up.
Range
GDK-16/20W:
The previous
internal call will
be disconnected.
The previous
external call will
be on hold.
Range
Button
Procedures
● You hear intercom or transferred outside line ring at a station.
● Lift handset or press MON button.
● Dial 7 and the ringing station number.
● You will be connected to the calling party.
Range
LDK-300:100~399
LDK-300E:
1000~1599
LDK-100:100~227
LDK-24:10~41
LDK-20:10~25
162 : 100~291
100 : 100~235
FPII : 100~177
16 : 100~ 115
16E: 100~ 121
20W : 100~133
(16: Above V4.0
20W: Above V3.0)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from the main menu.
● Select DIR.PICKUP(STA#) and dial the ringing station number.
● You will be connected to calling party automatically.
Directed Call Pick-up

## Slide 11
Call Wait (Camp-on)
Button
Procedures
● After receiving intercom busy tone, dial “*” or last digit of
called station number, or press DSS button.
● Camp-on tone is heard in called station.
● When called party answers, talk or hang up to transfer the call.
Range
If you dial a busy station, you may alert it of your call.
Mute
Button
Procedures
● Press MUTE button to activate.
● Press MUTE button again to deactivate.
It provides privacy during speakerphone or handset operation by disabling the microphone.
Range
Button
Procedures
● After receiving intercom busy tone, press CALLBK button.
● Hang up.
● When the busy station hangs up, you will be signaled.
● Answer the signal by lifting handset or by pressing MON
button, the station you called will be signaled.
Range
If you dial a station that is busy, you can leave a callback indication.
Call Back
Intercom Features

## Slide 12
Message Waiting
Procedures
● If a called party does not answer, press CALLBK button.
● Hang up.
● At that time, the LED of CALLBK button in the called station is
flashing.
Range
On LKD-2N/S, 8D/S,
● If a called party does not answer, press TRANS/PGM button
and dial 5 6 . (LDK-300/300E/100/24/20: 5 5 6)
To answer a message waiting,
● Press flashing CALLBK button.
● Station that left message will be signaled with tone ring.
On LKD-2N/S, 8D/S,
● Dial 5 7 (LDK-300/300E/100/24/20: 5 5 7) to answer a message waiting.
When the called extension does not answer the call, you can leave a message wait to the station.
Button
Procedures
If your phone has been programmed to have Do Not Disturb,
● Press DND/FWD button while on-hook or your phone is
ringing.
● The LED is lighting and your phone is in DND.
To remove Do Not Disturb,
● Press DND/FWD button while on-hook.
● The LED is extinguished and DND at your phone is removed.
Range
On LKD-2N/S, 8D/S,
● Dial 5 3 (LDK-300/300E/100/24/20: 5 5 3) instead of pressing
DND/FWD button (Toggle setting).
Do Not Disturb
Button

## Slide 13
Button
Procedures
● Lift handset or press MON button.
(The MON button is lighting.)
● Press DND/FWD button.
● Press the call forward type;
0 - Follow me (not available in GDK-16/20W)
1 - Unconditional
2 - Busy calls
3 - No answer calls
4 - Busy / no answer calls
5 - Station off-net
6 - Incoming outside line to off-net (system attendant only)
7 - DVU forward - 1 (forwarded after 4sec)
8 - DVU forward - 2 (forwarded after predefined time)
9 - DVU forward for busy
● Dial station number or press DSS button or intercom group.
● GDK-16/20W can be available to the type 1-7 only.
● Confirmation tone is heard and DND/FWD button is flashing
on forwarded station.
● Hang up.
- In case Follow-me, it should be programmed from the station
that you will be forwarded to i.e. if your extension is 102 and
you are forwarding to 104, then you will need to go to 104 to
program the feature. Also, this feature requires authorization
code and requires system programming.
- In case Station Off-net, the number you are forwarding to
should be saved as a speed dial number first. (Please see the
Page 12 to save a Speed Dial Number.)
- In case Incoming outside line to Off-net, it requires system
programming.
- In GDK-16/20W, 1 DVIB Forward(busy/no answer) is available.
(DND/FWD + dial 7; in no answer case, the forwarding time
can be programmed with Admin Programming.)
To cancel call forward,
● Lift handset or press MON button.
● Press DND/FWD button and dial #.
● Hang up.
- To cancel Incoming Outside line to Off-net (at system
attendant), Press MON + DND/FWD + CO line code (CO
group/CO line no./CO BTN) + #
Range
Sta. No.
162 : 100~291
100 : 100~235
FPII :100~177
16 : 100~115
16E: 100~121
20W: 100~133
INT. Group
162 : 620~649
100 : 620~634
FPII : 620~627
16/20W : 61~64
On LKD-2N/S, 8D/S,
● Dial 5 4 instead of pressing DND/FWD button.
Call Forward
A call can be forwarded to the other station or group depending on the call forward type.
It should be programmed in Admin. Programming to use some of the Call Forward types.
Intercom Features

## Slide 14
Button
Procedures
● Lift handset or press MON button.
(The MON button is lighting.)
● Press DND/FWD button.
● Press the call forward type;
0 - Follow me
1 - Unconditional
2 - Busy calls
3 - No answer calls
4 - Busy / no answer calls
5 - Station off-net, Unconditional
6 - Station off-net, No Answer
7 - Incoming outside line to off-net (Attendant only)
● Dial station number or press DSS button or intercom group.
● Confirmation tone is heard and DND/FWD button is flashing
on forwarded station.
● Hang up.
To activate call forward to VMIB,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial desired Call Forward code (1~4).
● Dial VMIB selection code # to receive the call.
● Hang up.
- In case Follow-me, it should be programmed from the station
that you will be forwarded to i.e. if your extension is 102 and
you are forwarding to 104, then you will need to go to 104 to
program the feature. Also, this feature requires authorization
code and requires system programming.
- In case Station Off-net, the number you are forwarding to
should be saved as a speed dial number first. (Please see the
Page 12 to save a Speed Dial Number.)
- In case Incoming outside line to Off-net, it requires system
programming.
To cancel call forward,
● Lift handset or press MON button.
● Press DND/FWD button and dial #.
● Hang up.
- To cancel Incoming Outside line to Off-net (at system
attendant), Press MON + DND/FWD + CO line code (CO
group/CO line no./CO BTN) + #
Range
Sta. No.
LDK-300 :
100~399
LDK-300E:
1000~1599
LDK-100 :
100~227
LDK-24 :
10~41
LDK-20:10~25
INT. Group
LDK-300/300E :
620~667
LDK-100 :
620~634
LDK-24 :
620~629
LDK-20: 620~629
On LKD-2N/S, 8D/S,
● Dial 5 5 4 instead of pressing DND/FWD button.
Call Forward (LDK-300/300E/100/24/20)
A call can be forwarded to the other station, station group or VMIB depending on the call forward type. It should be programmed in Admin. Programming to use some of the Call Forward types.

## Slide 15
Paging
Button
Procedures
To make a page,
● Lift handset.
● Dial page zone. (See below chart.) And you will hear warning
tone.
● After the tone, speak your message.
● Hang up.
162 100 FPII 16/20W LDK-100
Range
All Call 4 9 4 9 4 9 # 0 5 4 9 5 4 9 5 4 9
Internal Zone 1 4 0 1 4 0 1 4 0 1 # 1 5 0 1 5 0 1 5 0 1
Internal Zone 2 4 0 2 4 0 2 4 0 2 # 2 5 0 2 5 0 2 5 0 2
: : : : N.A. : :
Internal Zone 5 4 0 5 4 0 5 4 0 5 5 0 5 5 0 5 5 0 5
: : : : N.A. : :
Internal Zone 10 4 1 0 4 1 0 5 1 0 5 1 0 5 1 0
: : : N.A
Internal Zone 15 4 1 5 4 1 5 5 1 5 5 1 5
: :
Internal Zone 20 4 2 0
Internal Zone 35 5 3 5
Internal All Call 4 3 4 3 4 3 # 4 5 4 3 5 4 3 5 4 3
External Zone 1 4 6 4 6 4 6 N.A 5 4 5 5 4 5 5 4 5
External Zone 2 4 7 4 7 5 4 6 5 4 6 N.A
External Zone 3 5 4 7 5 4 7
External All Call 4 8 4 8 4 8 # 3 5 4 8 5 4 8
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
For internal zone,
● Press the 4th menu key from main menu and you will see
the following on the display.
LDK-300/300E
:01~35
LDK-100:01~15
LDK-24:01~10
LDK-20:01~10
162 : 01~20
100 : 01~15
FPII : 01~05
● Select INT PAGE key.
● Dial the desired zone. (Confirmation tone is heard.)
● After the tone, speak your message.
For internal all call/external all call/all call,
● Press the 4th menu key from main menu and you will see
the following on the display.
LDK-300/300E
:01~35
LDK-100:01~15
LDK-24:01~10
LDK-20:01~10
162 : 01~20
100 : 01~15
FPII : 01~05
A station, which is allowed to access page facilities, can connect and transmit voice announcement to any or all of the system external/internal page zones.
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
INT PAGE (01-35)
INT ALL CALL
EXT PAGE 1
EXT PAGE 2
EXT PAGE 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
INT PAGE (01-35)
INT ALL CALL
EXT PAGE 1
EXT PAGE 2
EXT PAGE 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
Intercom Features
LDK-300/
300E
LDK-24/
20

## Slide 16
To answer paging,
● Go to the nearest key telephone.
● Lift handset and dial 4 4
(GDK-16/20W: # 6, LDK-300/300E/100/24/20:5 4 4)
or HOLD/SAVE button, and you will be connected to the
paging party.
● Press the 4th menu key from main menu and you will see
the following on the display.
● Select the desired page key.
(INT ALL CALL/EXT ALL CALL/INT/EXT ALL CALL)
● You will hear warning tone.
● After the tone, speak your message.
Button
Procedures
Range
Paging (Cont’d)
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
LDK-300/300E
:01~35
LDK-100:01~15
LDK-24:01~10
LDK-20:01~10
162 : 01~20
100 : 01~15
FPII : 01~05
● Select MEET ME and you will be connected to paging party.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Flash
Button
Procedures
● While connected to an outside line, press FLASH button.
Range
Disconnects outside line and reseizes dial tone. It can be used to send a timed break recall when
the system is connected with a PBX.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select MEET ME and you will be connected to paging party.
INT PAGE (01-35)
INT ALL CALL
EXT PAGE 1
EXT PAGE 2
EXT PAGE 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
▼
< LDK-300/300E/100/24/20 >

## Slide 17
To activate speakerphone,
● Press MON button.
● Dial outside line number or intercom number to talk.
Button
Procedures
Range
Pressing an outside line button, a speed button, a station button or dialing a station number will
automatically activate the speakerphone. (LKD-2N/S has no microphone and doesn’t function
as handsfree unit.)
Speakerphone
Button
Procedures
● In speakerphone mode, press VOLUME (▲/▼) button to
control the speakerphone volume.
Range
● Press the 5th menu key from main menu to select
PROGRAM.
● Select SPEAKER VOLUME.
● Press VOLUME (▲/▼) button to control speaker volume.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Speaker Volume Control
Intercom Features
Button
Procedures
Range
To make an intercom group call,
● Lift handset or press MON button.
● Dial the intercom group number.
INT. Group No.
LDK-300/300E:
620~667
LDK-100:620~634
LDK-24/20: 620~629
162 : 620 ~ 649
100 : 620 ~ 634
FPII : 620 ~ 627
16/20W : 61~64
Button
Procedures
● When bell rings, press VOLUME (▲/▼) button to control
ring volume.
Range
● Press the 5th menu key from main menu to select
PROGRAM.
● Select RING VOLUME.
● Press VOLUME (▲/▼) button to control ring volume.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Ring Volume Control
Range
Placing an Intercom Group Call

## Slide 18
Button
Procedures
● Press HOLD/SAVE button.
- Once for system hold
- Twice for exclusive hold
Reverse if hold preference is programmed to system hold.
● Press HOLD/SAVE button (in GDK-16/20W).
CO call will be put on hold according to the Hold Preference.
To retrieve the call,
● Lift handset and press flashing outside line button.
Range
Group Call Pick-up
Button
Procedures
Range
You should be in the same pick-up group as ringing phone.
● You hear an unattended phone ringing.
● Lift handset or press MON button.
● Dial 6 6 (LDK-300/300E/100/24/20 : 5 6 6).
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select the GROUP PICKUP. You will be connected to the
calling party automatically.
● Pressing PAGE down(▼) key, you will see the following.
● Press the 4th menu key from the main menu.
INTERCOM CALL
STATION SPD DIAL
SYSTEM SPD DIAL
FEATURE
PROGRAM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▶
INT PAGE (01-20)
INT ALL CALL
EXT ALL CALL
INT/EXT ALL CALL
MEET ME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
▲
▼
CALL PARK (01-19)
GROUP PICKUP
DIR PICKUP (STA#)
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Placing a CO Call on Hold

## Slide 19
Group Call Pick-up (Cont’d)
Button
Procedures
Range
● Press the 4th menu key from the main menu.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Pressing PAGE down(▼) key 3 times, you will see the
following.
● Select the GROUP PICKUP. You will be connected to the
calling party automatically.
INTERCOM CALL
STATION SPD DIAL
SYSTEM SPD DIAL
FEATURE
PROGRAM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▶
INT PAGE (01-35)
INT ALL CALL
EXT PAGE 1
EXT PAGE 2
EXT PAGE 3
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
▲
▼
GROUP PCIKUP
DIR PICKUP (STA#)
ALARM RESET
DOOR OPEN (1-7)
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Conference
Button
Procedures
Range
To establish a conference,
● Call desired party. (internal or outside)
● Press CONF button. (CONF button is lighting and the called
party is put on exclusive hold.)
● Call the next party.
● Press CONF button twice. (once if adding additional parties)
● Conference is established.
To add another party in the conference,
(not available in GDK-16/20W)
● Press CONF button.
● Call the next party.
● Press CONF button twice.
To exit a conference (unsupervised),
● Press CONF button in the supervisor station and hang up.
Other parties are still connected.
GDK-16/20W:
At most 3 parties
can be active in
a conference.
System Features

## Slide 20
Button
Procedures
Range
Re-entering a conference,
● Lift handset or press MON button.
● Press CONF button.
To drop an outside party, (not available in GDK-16/20W)
(You should be active in the conference.)
● Press outside line of party you wish to drop.
● Hang up or press MON button.
To terminate the conference,
● Hang up or, press CONF button if unsupervised.
On LKD-2N/S, 8D/S,
● Conference feature can be accomplished by programming
a flexible key as CONF button (TRANS + 91).
Conference (Cont'd)
To prevent unauthorized outside calling, DISA access or Trunk access on your station by others,
the system provides a means to lock/unlock a station by access authorization code.
Range
● Press the 5th menu key from the main menu.
● Select the STATION PROGRAM and you will see the
following.
S>WAKE-UP SET
S>WAKE-UP ERASE
S>REG PASSWORD
S>CHG PASSWORD
S>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
INTERCOM CALL
STATION SPD DIAL
SYSTEM SPD DIAL
FEATURE
PROGRAM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▶
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▣
▣
▲
▼
▲
▼
Button
Procedures
To register access authorization code,
● Press TRANS/PGM button and dial 44.
(LDK-300/300E/100/24/20:31)
● Dial your own 5 digits access authorization code.
● Press HOLD/SAVE button.
● Confirmation tone is heard.
Access Authorization Code (＊)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)

## Slide 21
Access Authorization Code (＊) (Cont'd)
Range
Button
Procedures
● Press the 5th menu key from the main menu.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Select the STATION PROGRAM and press PAGE down(▼)
key, you will see the following.
S>AUTHO REGISTER
S>AUTHO CHANGE
S>SET WAKEUP TM
S>WAKEUP DISBL
S>SET PRESEL MSG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
INTERCOM CALL
STATION SPD DIAL
SYSTEM SPD DIAL
FEATURE
PROGRAM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▶
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▣
▣
▲
▼
▲
▼
● Select the AUTHO REGISTER and enter the 5 digits access
authorization code.
● Press HOLD/SAVE button.
To change access authorization code,
● Press TRANS/PGM button and dial 45.
(LDK-300/300E/100/24/20:32).
● Dial your current access authorization code. You will hear
confirmation tone.
● Dial your new 5 digits access authorization code.
● Press HOLD/SAVE button.
● You will hear confirmation tone.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select the STATION PROGRAM.
● Select the CHANGE PASSWORD and enter your current
access authorization code.
● Enter your new 5 digits access authorization code.
● Press HOLD/SAVE button.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select the STATION PROGRAM and press PAGE down(▼)
key.
● Select the AUTHO CHANGE and enter your current access
authorization code.
● Enter your new 5 digits access authorization code.
● Press HOLD/SAVE button.
System Features

## Slide 22
Procedures
● Press TRANS/PGM button and dial 46.
(LDK-300/300E/100/24/20:21).
● Press HOLD/SAVE button. (Confirmation tone is heard.)
● MUTE button will flash until restored to normal.
Range
Note : An access authorization code should be registered.
Blocking Outside Calls (＊)
● Press the 5th menu key from the main menu.
● Press STATION PROGRAM key and you will see the following.
● Select INTERCOM ONLY.
In LDK-300/300E/100/24/20, select TMPRL COS DOWN.
● Press HOLD/SAVE button. (Confirmation tone is heard.)
● MUTE button will flash until restored to normal.
Restoring Outside Calls (＊)
Button
Procedures
● Press TRANS/PGM button and dial 47.
(LDK-300/300E/100/24/20:22).
● Dial your current access authorization code.
(Confirmation tone is heard.)
● MUTE button will be extinguished.
Range
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Press STATION PROGRAM key.
● Press PAGE down(▼) key.
On the display, you will see the following.
● Select RESTORE COS key.
● Enter your current access authorization code.
● Press HOLD/SAVE button.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Button
S>RESTORE COS
S>MSG PROGRAM
S>ICM ANS MODE
S>MUSIC CHANNEL
S>PRESELECT MSG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
S>RING TYPE
S>ANSWER MODE
S>COS DOWN
S>RESTORE COS
S>WALKING COS
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >
S>WAKE-UP SET
S>WAKE-UP ERASE
S>REG PASSWORD
S>CHG PASSWORD
S>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
S>RING TYPE
S>ANSWER MODE
S>TMPRL COS DOWN
S>RESTORE COS
S>WALKING COS
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
< LDK-300/300E/100/24/20 >

## Slide 23
Wake-up Call
Button
Procedures
To register wake-up time,
● Press TRANS/PGM button.
● Dial 4 1 and 4-digit wake-up time (HHMM) in 24-hour mode.
(HH = 00~23, MM = 00~59)
● Press HOLD/SAVE button for “one-day” or dial # and
HOLD/SAVE button for “until canceled”.
(Confirmation tone is heard.)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select the STATION PROGRAM and you will see the
following.
Range
The system automatically sends ring signal to a station which registers a wake-up time. There are
two kinds of wake-up call, one is effective for one-day, the other is effective until canceled.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
S>WAKE-UP SET
S>WAKE-UP ERASE
S>REG PASSWORD
S>CHG PASSWORD
S>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select WAKE-UP SET key.
● Press the 5th menu key from the main menu.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
INTERCOM CALL
STATION SPD DIAL
SYSTEM SPD DIAL
FEATURE
PROGRAM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▶
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▣
▣
▲
▼
▲
▼
● Select the STATION PROGRAM and press PAGE down(▼)
key, you will see the following.
S>AUTHO REGISTER
S>AUTHO CHANGE
S>SET WAKEUP TM
S>WAKEUP DISBL
S>SET PRESEL MSG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select SET WAKEUP TM key.
System Features

## Slide 24
Wake-up Call (Cont’d)
Button
Procedures
Range
To cancel wake-up call,
● Press TRANS/PGM button and dial 4 2.
● Press HOLD/SAVE button. (Confirmation tone is heard.)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select STATION PROGRAM key.
● Select WAKE-UP ERASE key.
● Press HOLD/SAVE button. (Confirmation tone is heard.)
● Enter 4-digit wake-up time (HHMM) in 24-hour mode.
(HH = 00~23, MM = 00~59)
● Press HOLD/SAVE button for “one-day” or dial # and
HOLD/SAVE button for “until canceled”.
(Confirmation tone is heard.)
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from the main menu.
● Select STATION PROGRAM key and press PAGE down(▼)
key.
● Select WAKE-UP DISBL key.
● Press HOLD/SAVE button. (Confirmation tone is heard.)
Procedures
● Press SPEED button twice.
● On the display, you will see the following.
Range
DIAL BY NAME
ICM : 1 U_SPD : 2 S_SPD : 3
● Select desired type.
1 : Intercom
2 : User (Station Speed Dial)
3 : System (System Speed Dial)
● Confirmation tone is heard and you will see the following.
1 : XXXX XXXX XXXXXX
2 : YYYY YYYY YYYYYY
Each station and speed dial number can be assigned to a name. When names are programmed,
you may select a speed dial number by the stored name.
Button
Using Dial By Name

## Slide 25
Procedures
Range
● Press the VOLUME button to see the next two names.
● You may enter characters using the code in “Storing Dial by
Name”. The LCD will display the first two names which match
your input.
● To select the name in line 1, press HOLD/SAVE button.
● To select the name in line 2, dial 2 and press HOLD/SAVE
button.
● The call is placed automatically.
Using Dial By Name (Cont’d)
Each station and speed dial number can be assigned to a name. When names are programmed,
you may select a speed dial number by the stored name.
Button
● Pressing VOLUME button, the cursor will be moved to the
next name. When the cursor points a name or a dial number
to call, press HOLD/SAVE button. Then, the stored number
is dialed.
● You may enter characters using the code in “Storing Dial by
Name”. The LCD will display the first two names which match
your input. (You may delete the last letter of your input by
pressing CALLBK button. And then, the previous matched
name is displayed.)
● You can see the matched phone number by pressing FLASH
button while the name is displayed (toggle).
● Press SPEED button twice.
● On the display, you will see the following.
DIAL BY NAME
ICM : 1 U_SPD : 2 S_SPD : 3
● Select desired type.
1 : Intercom
2 : User (Station Speed Dial)
3 : System (System Speed Dial)
● Confirmation tone is heard and you will see the following.
1 : XXXX XXXX XXXXXX
2 : YYYY YYYY YYYYYY
In LDK-300/300E/100/24/20, GDK-16/20W
System Features

## Slide 26
Procedures
Range
Button
Using Dial By Name (＊) (Cont’d)
Intercom Call
(Intercom name should be programmed by attendant.)
● Press the 1st menu key from the main menu.
If it is programmed, you will see the following on the display.
● Select the key according to the first letter of the desired party’s
name. (Ex. Selecting the first letter with HI, you will see the
sorted subscriber’s name as follows.)
HONG H.S.
JANG W.H.
KIM Y.J.
LEE M.S.
LEE S.H.
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
AB LMN
CD OPQ
EFG RST
HI UVW
JK XYZ
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press PAGE (▲/▼) button until you find the desired name.
LEE Y.U.
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
Station Speed Dial
(Station Speed Dial should be programmed at a station.)
● Press the 2nd menu key from the main menu.
You will see the following on the display.
AB LMN
CD OPQ
EFG RST
HI UVW
JK XYZ
● Follow the procedure as described in Intercom Call.
System Speed Dial
(System Speed Dial should be programmed by attendant.)
● Press the 3rd menu key from the main menu.
● Follow the procedure as described in Station Speed Dial.

## Slide 27
Programming Your Name into Display
Button
Procedures
● Press TRANS/PGM button.
● Press SPEED button and dial 0 0.
● Press SPEED button.
● Enter your name. (up to 7 letters using the code in “Storing
Dial by name.)
● Press HOLD/SAVE button.
Range
You can program your name and people using display phones will see your name instead of your
station number.
Button
Procedures
● Press TRANS/PGM button and dial 77.
(LDK-300/300E/100/24/20:51).
● Dial the number of desired message. Date, Time or Station
Number if required.
● Press HOLD/SAVE button. (DND/FWD button is flashing.)
0 1 LUNCH, RETURN HH:MM
0 2 ON VACATION / RETURN AT MM:DD
0 3 OUT OF OFFICE/ RERURN TIME HH:MM
0 4 OUT OF OFFICE/ RETURN AT MM:DD
0 5 OUT OF OFFICE/ RETURN UNKNOWN
0 6 CALL : XX.... (Telephone number: Max. 17 digits)
0 7 IN OFFICE/STA XXXX
0 8 IN A MEETING / RETURN TIME (HH:MM)
0 9 AT HOME
1 0 AT BRANCH OFFICE
# to cancel
1 1 ~ 2 0 are used for customized messages which are
programmed by attendant. (See “Creating Customized Message”)
Range
You can select a pre-assigned message to be displayed on the LCD of the phone calling the station.
Pre-selected Message (＊)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Press the 5th menu key from main menu and you will see
the following on the display.
16: Above V4.0
20W: Above V3.0)
In LDK-300/300E/100/24/20
● Press TRANS/PGM button.
● Dial 7 4.
● Enter your name. (up to 7 letters using the code in “Storing
Dial by name.)
● Press HOLD/SAVE button.
System Features

## Slide 28
Button
Procedures
Range
You can select a pre-assigned message to be displayed on the LCD of the phone calling the
station.
Pre-selected Message (＊) (Cont'd)
S>WAKE-UP SET
S>WAKE-UP ERASE
S>REG PASSWORD
S>CHG PASSWORD
S>INTERCOM ONLY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Press PAGE down(▼) key and you will see the following
on the display.
S>RESTORE COS
S>MSG PROGRAM
S>ICM INS MODE
S>MUSIC CHANNEL
S>PRESELECT MSG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select STATION PROGRAM key.
On the display, you will see the following.
● Select PRESELECT MSG.
● On the display, you will see the following.
LUNCH (TIME)
VACATION (DATE)
OUT (TIME)
OUT (DATE)
OUT ( ? )
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select desired message key, date, time or station number, if
required.
● Press HOLD/SAVE button. (DND/FWD button is flashing.)
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from main menu and you will see
the following on the display.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▣
▲
▼

## Slide 29
Pre-selected Message (Cont’d)
Button
Procedures
Range
● Select the STATION PROGRAM and press PAGE down(▼)
key, you will see the following.
S>AUTHO REGISTER
S>AUTHO CHANGE
S>SET WAKEUP TM
S>WAKEUP DISBL
S>SET PRESEL MSG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select SET PRESEL MSG.
● On the display, you will see the following.
● Select desired message key, date, time or station number, if
required.
● Press HOLD/SAVE button. (DND/FWD button is flashing.)
To turn off message display,
● Press flashing DND/FWD button.
LUNCH (TIME)
VACATION (DATE)
OUT (TIME)
OUT (DATE)
OUT ( ? )
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
CALL XXXX (TEL)
STA XXXX (STA#)
MEETING (TIME)
AT HOME
AT BRANCH OFFICE
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
User Custom Message Programming (＊)
Button
Procedures
● Press TRANS/PGM button and dial 48.
(LDK-300/300E/100/24/20:52)
at the station. (Confirmation tone is heard.)
● Enter the message. (up to 24 letters using the code in “Storing
Dial by Name”)
● Press HOLD/SAVE button.
Range
You may program a custom message 00 to be displayed on the LCD of the phone calling your
station.
System Features

## Slide 30
● Press TRANS/PGM button.
● Dial 7 3 .
● Internal BGM is heard.
● Pressing TRANS/PGM + 7 3, the selected music is changed
by turns. (Channel 0 (00): BGM is not heard.)
Button
Procedures
Range
LDK-300/300E
:00~12
LDK-100:00~11
LDK-24/20 :0~8
162 : 0~9
100 : 0~9
FPII : 0~9
16/20W : 1~3
A station can receive audio, generally music from an internal or external source while idle.
Background Music
Time Prompt :
● Dial 6 7 1.
● You will hear the time prompt, “Time is XX : XX PM.”
Date Prompt :
● Dial 6 7 2.
● You will hear the date prompt, “Date is December, 20th.”
Station Number Prompt :
● Dial 6 7 3.
● You will hear the station number prompt, “This is station
XXXX.”
Record your greeting,
● Dial 6 7 4 (The message is heard after 4sec) or 6 7 0 (The
message is heard after predefined time) .
● To stop recording, press MON button or HOLD/SAVE button.
( MON button: erased automatically after 48 hours,
HOLD/SAVE button: remained until canceled)
● After recording your greeting message, a caller will hear your
greeting message when you do not answer the call within a
predefined time (PGM 43-BTN 24).
Delete your greeting,
● Dial 6 7 5.
Playback your greeting,
● Dial 6 7 6. (You will hear the recorded greeting message.)
Station status prompt ;
● Dial 6 7 7. (You will hear below list (a-h). c-g items will be
omitted if not active.)
a) Station number XXXX b) Intercom Answer mode
c) Listed message X d) Wake-up time XXXX AM or PM
e) Do not disturb f) Forwarded to station XXXX
g) Forwarded to speed bin XXX h) Locked(temporary COS change)
i) COS X
Button
Procedures
Range
This feature provides the station an audible system prompt and you can record your greeting to
provide the caller when the call is not answered within the predefined time.
Voice Announcement
In LDK-300/300E/100/24/20,
● Press TRANS/PGM button.
● Dial 7 3 and select BGM channel (00~12).
● Press HOLD/SAVE button.

## Slide 31
Button
Procedures
Range
Record paging message;
● Dial 6 7 8.
● Lift handset to record your paging message.
● Press HOLD/SAVE button after recording.
Confirm paging message;
● Dial 6 7 9.
● The paging message is heard.
Activate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial 7 or 8 (Select DVU forward type 1 or 2).
● Go on-hook.
Deactivate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial #.
● Go on-hook.
Listen to the recorded message,
● Press the flashing CALLBK button.
● The recorded message is heard with the time and date.
● Pressing HOLD/SAVE button, the current message is saved
and the next message is heard.
● Pressing CALLBK button, the recorded message is heard
from the first.
● Pressing CONF button, the current message is deleted.
※ The recorded caller’s message will not be erased without pressing
CONF button. But, the system power is off or system is reset, it will be
erased.
※ The max. user recording time is about 250sec. (Default: 20sec: it can
be programmable with admin programming - PGM 44-BTN 16.)
Voice Announcement (Cont'd)
On LKD-2N/S, 8D/S,
● If a DVU message is left, the MSG lamp is flashing.
● Dial 5 7 or programmed CALLBK button to listen to the
recorded message.
● The recorded message is heard and then the message is
automatically deleted.
● Pressing HOLD/SAVE button while a message is played, the
next message is heard. (The current message is placed to
the last.)
● Pressing programmed CALLBK button, the recorded
message is heard from the first.
● If you don’t press HOLD/SAVE button any more, the current
message is deleted and other messages are remained.
● If you program a flex. button as a CONF button, the message
will be saved and you should press the programmed CONF
button to delete the message (only in GDK-16).
System Features

## Slide 32
Button
Procedures
Range
Voice Announcement (Cont’d)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
Time Prompt;
● Dial 6 7 1.
● You will hear the time prompt, “Time is XX : XX PM.”
Date Prompt :
● Dial 6 7 2.
● You will hear the date prompt, “Date is December, 20th.”
Station Number Prompt :
● Dial 6 7 3.
● You will hear the station number prompt, “This is station
XXXX.”
Record paging message;
● Dial 6 7 8.
● Lift handset to record your paging message.
● Press HOLD/SAVE button after recording.
DVU station status;
● Press the 4th key from the main menu.
● Press PAGE down(▼) key 4 times.
● Select DVU STA STATUS.
You will hear below lists (a - i).
a) Station number XXXX
b) Ring assignment
c) Listed message X
d) Wake-up time XXXX AM or PM
e) Do Not disturb
f) Forwarded to station XXXX
g) Forwarded to speed bin XXX
h) Locked (temporary COS change)
i) COS X
Record your greeting;
● Press the 4th key from the main menu.
● Press PAGE down(▼) key 3 times.
● Select DVU RECORD key.
● Lift handset to record your greeting message.
● Press HOLD/SAVE button.
Delete your recording;
● Press the 4th key from the main menu.
● Press PAGE down(▼) key 3 times.
● Select DVU DELETE key.
Playback your greeting ;
● Press the 4th key from the main menu.
● Press PAGE down(▼) key 3 times.
● Select DVU PLAY key.
Paging your greeting ;
● Lift handset and dial the desired page zone.
● After hearing confirmation tone, your recorded paging
message is sent to the page zone automatically.

## Slide 33
Button
Procedures
Range
Voice Announcement (in GDK-16/20W) (Cont'd)
In GDK-16/20W,
Record your greeting,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial 7 #.
Delete your greeting,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial 7 ＊.
Activate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial 7 .
● Go on-hook.
Deactivate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial #.
● Go on-hook.
To listen to the recorded message,
● Press the flashing CALLBK button.
● The recorded message is heard with the time and date.
● Pressing HOLD/SAVE button, the current message is saved
and the next message is heard.
● Pressing CALLBK button, the recorded message is heard
from the first.
● Pressing CONF button, the current message is deleted.
* The operation of 2/8 BTN keyset is the same with other GDK
systems. (Refer to p.41)
※ The max. user recording time is about 250sec. (Default: 20sec: it can
be programmable with admin programming - Main Menu 6-1-24)
System Features

## Slide 34
Date & Time Prompt ;
● Press TRANS/PGM button and dial 6 2.
● You will hear the time prompt,
“Date is December, 20th, Time is XX : XX PM.”
Station Number Prompt ;
● Press TRANS/PGM button and dial 6 3.
● You will hear the station number prompt, “This is station
XXXX.”
Station Status Prompt ;
● Press TRANS/PGM button and dial 6 4. (You will hear below
list (a-j). c-i items will be omitted if not active.)
a) Station number XXXX b) Intercom Answer Mode
c) Listed message X d) Wake-up time XX:XX AM or PM
e) Do not disturb f) Forwarded to station XXXX
g) Forwarded to speed bin XXX h) Queued CO XXX
i) Locked (temporary COS change) j) COS X
Record your greeting,
● Press TRANS/PGM button and dial 6 1.
● “Press # button to record” is heard and if there is a recorded
greeting, the greeting will be played.
● Press # button and record your greeting after hearing
confirmation tone.
● Press HOLD/SAVE button or MON button to finish recording,
then you will hear confirmation tone.
● Pressing SPEED button while playing, the greeting is deleted
and confirmation tone is heard.
Delete your greeting,
● Press TRANS/PGM button and dial 6 6.
Activate Call Forward to VMIB,
● Lift handset or press MON button.
● Press DND/FWD button.
● Dial Call Forward type code (1~4).
● Dial # key. (Confirmation tone is heard.)
● Go on-hook.
Deactivate Call Forward to VMIB,
● Lift handset or press MON button.
● Press DND/FWD button.
Leave voice message wait,
● After user greeting is played. “Record your message” prompt
is heard.
● After beep tone, record your message with normal voice.
● Hang up.
Button
Procedures
Range
Voice Announcement (in LDK-300/300E/100/24/20) (Cont'd)
In LDK-300/300E/100/24/20,

## Slide 35
Listen to the recorded message,
● Press the flashing CALLBK button.
● The recorded message is heard with the time and date.
● Pressing HOLD/SAVE button, the current message is saved
and the next message is heard.
● Pressing CALLBK button, the current message is played
again.
● Pressing CONF button, the current message is deleted and
the next message is heard.
* The operation of 2/8 BTN keyset is the same with other GDK
systems.
Record VMIB Paging Message,
● Press TRANS/PGM button and dial 6 5.
● “Press # button to record” is heard and if there is a recorded
paging message, it will be played.
● Press # button and record paging message after hearing
confirmation tone.
● Press HOLD/SAVE button or MON button to finish recording,
then you will hear confirmation tone.
● Pressing SPEED button while playing, the greeting is deleted
and confirmation tone is heard.
Activate VMIB Message Paging,
● Dial the desired page zone (5XX) and lift handset.
● The recorded VMIB message is paged.
Delete VMIB Paging Message,
● Press TRANS/PGM button and dial 6 7.
● The recorded message is deleted.
● Or, press SPEED button while playing, then the message is
deleted and confirmation tone is heard.
Button
Procedures
Range
Voice Announcement (in LDK-300/300E/100/24/20) (Cont'd)
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 5th menu key from main menu and you will see
the following on the display.
ATD PROGRAM
STATION PROGRAM
LCD BRIGHTNESS
RING VOLUME
SPEAKER VOLUME
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▣
▲
▼
System Features

## Slide 36
Button
Procedures
Range
Voice Announcement (in LDK-300/300E/100/24/20) (Cont'd)
Date & Time Prompt;
● Select LISTEN TM / DT key in the above display.
● You will hear the time prompt,
“Date is December, 20th, Time is XX : XX PM.”
Station Number Prompt :
● Select LISTEN STA NUM key in the above display.
● You will hear the station number prompt, “This is station
XXXX.”
Station Status Prompt :
● Press PAGE down(▼) key again in the above display, you will
see the following.
S>LISTEN STA STAT
S>RECORD PG MSG
S>ERASE USER GRT
S>ERASE PAGE MSG
S>LCD DISP LANG
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼
● Select LISTEN STA STAT key. Then you will hear station
status.
Record VMIB Paging Message :
● Select RECORD PG MSG key in the above display.
Erase your User Greeting :
● Select ERASE USET GRT key in the above display.
ERASE VMIB Paging Message :
● Select ERASE PAGE MSG key in the above display.
● Select the STATION PROGRAM and press PAGE down(▼)
key twice, you will see the following.
S>SET CUSTOM MSG
S>2WAY REC SMDI
S>REC USER GREET
S>LISTEN TM / DT
S>LISTEN STA NUM
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
▣
■
■
■
■
■
▲
▼

## Slide 37
CO Message Wait
Button
Procedures
Range
When a call is received with DISA/DID, the Calling Line Identification (CLI) of the incoming call is
displayed on the LCD of the station. If the DISA/DID external party hangs up the call before
answered, the CLI will be stored in the CO message wait queue in the called party.
To retrieve CLI Message,
● Press CALLBK button.
● The stored message will be shown on the LCD.
To delete the current CLI message and see the next one,
● Press CONF button.
To make a callback,
● Press HOLD/SAVE button.
● The stored number is dialed as speed dialing.
To see the next/previous CLI message,
● Press VOLUME button.
To delete all CLI messages, (Not available in GDK-16/20W)
● Press SPEED button twice.
● If DVU message is stored with CLI message, the CLI
message will not be deleted by pressing SPEED button.
DISA (Direct Inward System Access)
● Dial the CO access code after hearing dial tone or voice guide
from DVU.
● Or, dial the CO access code after dialing the programmed
authorization code (when needed) for outgoing call.
Button
Procedures
Outside caller can access a CO line which is programmed as DISA line.
Range
LCD Language Change
Button
Procedures
Range
● Press TRANS/PGM button and dial 51.
(LDK-300/300E/100/24/20:71).
● The language in LCD is changed into default value.
● If pressing TRANS/PGM + 5 1 (LDK-300/300E/100/24/20: 71),
the language in the LCD is changed to the nation’s language.
16: Above V4.0
20W: Above V3.0
System Features

## Slide 38
Button
Procedures
● Press the 4th menu key from main menu to select FEATURE.
● Press PAGE down(▼) key twice.
On the display, you will see the following.
ACC CO-GR(01-48)
ACC 1 CO(01-96)
UNIV NITE ANSWER
TIE ROUTE (01-30)
ALARM RESET
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select ALARM RESET key.
● Ring is stopped.
Alarm Reset
Range
To terminate alarm signal while idle state,
● Dial 6 5 (LDK-300/300E/100/24/20: 5 6 5).
● Confirmation tone is heard and the alarm signal is terminated
at all assigned stations.
Or using display, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
● Press the 4th menu key from main menu to select FEATURE.
● Press PAGE down(▼) key 3 times.
On the display, you will see the following.
GROUP PICKUP
DIR PICKUP (STA#)
ALARM RESET
DOOR OPEN
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select ALARM RESET key.
● Ring is stopped.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)

## Slide 39
Two-way Recording (Only in LDK-300/300E/100/24/20, GDK-16/20W)
To record the conversation,
● Press the programmed {RECORD} button.
To program the {RECORD} button,
[TRANS/PGM] + Flex. BTN + [TRANS/PGM]
+ # 4 (LDK-300/300E/100/24/20: 5 4) + [HOLD/SAVE]
To finish the recording,
● Press the programmed {RECORD} button again. Or, replace
the handset.
Button
Procedures
While a CO line call, you can record the conversation and it will be saved in its own mailbox.
Range
The following features are operated only KD-33LD, KD/E-36LD and LKD-30LD.
(Large LCD Digital Keyset)
● Press the 5th menu key from main menu.
● Select LCD BRIGHTNESS.
● Press VOLUME button (▲/▼) to control the brightness.
Button
Procedures
LCD Brightness Control (＊)
Range
Large LCD Keyset Features
Large LCD
Button
Procedures
Range
● Press MENU key to display Calendar.
On the display, you will see calendar as follows;
MAR 2001
S M T W T F S
1 2 3
4 5 6 7 8 9 10
11 12 13 14 15 16 17
18 19 20 21 22 23 24
25 26 27 28 29 30 31
STA 102 (T)
MAR 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● While the calendar is displayed, the main menu key and other
menu keys will not work.
● To display the main menu instead of calendar, press MENU
key.
Calendar Display

## Slide 40
Button
Procedures
Range
● Press the 4th menu key from main menu to select FEATURE.
● Press PAGE down(▼) key 3 times.
On the display, you will see the following.
DOOR OPEN (1-4)
DVU RECORD
DVU DELETE
DVU STA STATUS
DVU PLAY
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select DOOR OPEN(1-4) key.
● Select the door open type by pressing dial button 1~4.
Door Open
● Press the 4th menu key from main menu to select FEATURE.
● Press PAGE down(▼) key 3 times.
On the display, you will see the following.
GROUP PICKUP
DIR PICKUP (STA#)
ALARM RESET
DOOR OPEN
STA 102 (T)
NOV 02 01:40pm
■
■
■
■
■
■
■
■
■
■
▲
▼
▣
● Select DOOR OPEN (1-7) key.
● Select the door open type by pressing dial button 1~7.
In LDK-300/300E/100/24/20, (Only in KD-33LD, KD/E-36LD, LKD-30LD)
LDK-100 : 1-6
LDK-24/20 : 1-2

## Slide 41
Station Programming Menu Table (LDK-300/300E/100/24/20)
The LDK-300/300E/100/24/20 system supports multiple hierarchical menus based on station
programming. User can make station programming by selecting desired menu. By pressing
[TRANS/PGM] button in a keyset with LCD, user can see the menu.

## Slide 42
Direct Station Select station number
162 : 100~291
100 : 100~235
FPII :100~177
16 : 100~115
20W: 100~133
Call Park parking location
162 : 601~619
100 : 601~610
FPII: 601~605
Hunt Group internal hunt group
162 : 620~649
100 : 620~634
FPII : 620~627
16/20W: 61~64
Group Call Pick-up 6 6
Dial Memo TRANS/PGM + 8 0
Call Wait (Camp-on) TRANS/PGM + 8 5
Wake-up
To register (continued) TRANS/PGM + 4 1
To cancel TRANS/PGM + 4 2
Paging Refer to p. 25
Access Authorization
code
Blocking outside call TRANS/PGM + 4 6
Restoring outside call TRANS/PGM + 4 7
Pre-selected Message TRANS/PGM + 7 7
Background Music TRANS/PGM + 7 3
LCD Display Change TRANS/PGM + 5 1
Intercom Hold TRANS/PGM + 8 3
Universal Night Answer 6 9
Loop button TRANS/PGM + 8 4
Speed Dial
Station speed dial SPEED + bin no
162/FPII/100: 00~19
/16/20W
* 01~20:GDK-16(V1.0~V3.0),GDK-20W(V1.0~V2.0)
Flexible Button Programming
To program flexible buttons,
● Press TRANS/PGM button.
● Press a flexible button to program.
● See the below table and enter the desired code.
● Press HOLD/SAVE button.
To erase a flexible button,
● Press TRANS/PGM button.
● Press the flexible button to be erased.
● Press HOLD/SAVE button.
Button
Procedures
Range
Code for Flexible Button Programming
System speed dial SPEED + bin no.
162 : 200~999
100 : 200~399
FPII :200~399
16/20W :21~99
Intercom Answer Mode TRANS/PGM + 4 9
Stop Watch Event Timer TRANS/PGM + 8 9
Alarm Reset 6 5
Station DVU Access 6 7
Account Code TRANS/PGM + 8 1
Camp-on TRANS/PGM + 8 5
Outside Line Access
Group access 9
Group #1 8 0 1 162: Grp#01~48
Group #2 8 0 2 100: Grp#01~24
: : FPII: Grp#01~09
16/20W: Grp#01~04
Group #48 8 4 8
Individual Line Access 8 8 + line no.
162 : 01~96
100 : 01~48
FPII :01~34
16 :01~06
20W:01~08
Button Assignment for LKD-2/8 button
REDIAL button TRANS + 8 8
SPEED button TRANS + 9 0
CONF button TRANS + 9 1
CALLBK button TRANS + 9 2
DND button TRANS + 9 3
FLASH button TRANS + 9 4 (＊)
MUTE button TRANS + 9 5
MON button TRANS + 9 6 (＊)

## Slide 43
Direct Station Select station number
LDK-300: 100~399
LDK-300E: 1000~1599
LDK-100: 100~227
LDK-24 : 10~41
LDK-20 : 10~25
Call Park parking location
LDK-300/300E: 601~619
LDK-100: 601~610
LDK-24/20: 601~608
Hunt Group internal hunt group
LDK-300/300E: 620~667
LDK-100: 620~634
LDK-24/20: 620~629
Alarm Reset 5 6 5
Group Call Pick-up 5 6 6
Universal Night Answer 5 6 9
Speed Dial
Station speed dial SPEED+000~099
System speed dial LDK-300:
SPEED+2000~4999
LDK-300E:
SPEED+2000~6999
LDK-100/24:
SPEED+2000~3499
LDK-20: SPEED + 2000~2499
Outside Line Access
Group access 9
Group #1~72 LDK-300/300E: 801~872
LDK-100: 8 0 1~8 2 4
LDK-24 : 8 0 1~8 0 8
Individual Line Access LDK-300: 8 8+001~200
LDK-100: 8 8+01~40
LDK-24: 8 8+01~12
LDK-20: 88+01~08
Alarm Reset 5 6 5
Code for Flexible Button Programming (LDK-300/300E/100/24/20)
Ring Type
Ring Answer Mode
COS Down
COS Restore
Walking COS
Auth. Code Register
Auth. Code Change
Set Wake-up Time
Wake-up Disable
Set Preselected MSG
Set Customer MSG
Record User Greeting
Listen Time & Date
Listen Station Number
Listen Station Status
Record Page MSG
Erase User Greeting
Erase Page MSG
LCD Display Language
MPB Version Display
Background Music
Register Station Name
Speakerphone/Headset
Headset Ring Mode
Account Code
ICM Hold
LOOP button
Camp-on
TRANS/PGM + 11
TRANS/PGM + 12
TRANS/PGM + 21
TRANS/PGM + 22
TRANS/PGM + 23
TRANS/PGM + 31
TRANS/PGM + 32
TRANS/PGM + 41
TRANS/PGM + 42
TRANS/PGM + 51
TRANS/PGM + 52
TRANS/PGM + 61
TRANS/PGM + 62
TRANS/PGM + 63
TRANS/PGM + 64
TRANS/PGM + 65
TRANS/PGM + 66
TRANS/PGM + 67
TRANS/PGM + 71
TRANS/PGM + 72
TRANS/PGM + 73
TRANS/PGM + 74
TRANS/PGM + 75
TRANS/PGM + 76
TRANS/PGM + 80
TRANS/PGM + 83
TRANS/PGM + 84
TRANS/PGM + 85
. You cannot use large LCD digital keyset in GDK-16/20W.
. Programming flexible buttons for the following features are not supported in GDK-16/20W
(marked (＊)).
- Dial Memo
- Access Authorization Code
- Pre-selected Message
- Stop Watch Event Timer
- Account Code
Information
Button Assignment for LKD-2/8 button
CONF button TRANS + 9 1
CALLBK button TRANS + 9 2
DND button TRANS + 9 3
FLASH button TRANS + 9 4
MUTE button TRANS + 9 5
MON button TRANS + 9 6
REDIAL button TRANS + 9 7