## Slide 1
Introduction
To register hotel name,
● Press TRANS/PGM button.
● Dial 2 1.
● Enter the hotel name (up to 24 digits) with the code as below.
Button
Procedures
● Press HOLD/SAVE button.
The GDK hotel S/W has a number of features that have been designed specifically for hotel and
other hospitality applications. The additional features that are available, add value to the service
offered to guests and increase the efficiency of staff.
This section is aimed at the system manager and anyone else that requires a detailed
description of the hotel facilities and their operation. These features are additional to the normal
office features and refer to the other sections in this user guide. It is available for GDK-162/100/
FPII Hotel S/W.
Register Hotel Name
This feature allows registering or changing the name of hotel. In check-out or displaying room
charge, the registered hotel name is printed out in the headings.
Check-In
This feature allows the System Attendant to view the status of a room and check-in a guest.
When checking in a guest without changing the Room Status, the following default values will
be applied to the room;
Guest Name - Not assigned
Room Day & Night COS - 22
Alarm Calls - Not assigned
Intercom Enable/Disable - Internal call is not allowed
Room to Room Call Groups - System Attendant assigned no.
Authorization Codes - Not assigned
Pre-paid Calls - 0
Call Charge Rate - System Attendant assigned no.

## Slide 2
Check-In (Cont'd)
To check in a guest with Standard Room Status,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial the Room Number.
● Press SPEED button.
● Press HOLD/SAVE button.
Button
Procedures
Check-In / Change a Guest's Room Status
Button
Procedure
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number.
● Press SPEED button.
● Dial Room Status Type (1~8).
1: Register/Change Guest Name (up to 12 digits)
2: Change Room Day and Night Class of Service
3: Register/Change Alarm Call (wake-up) Time
4: Set Intercom Enable/Disable
5: Set Room to Room Call Group
6: Register/Change Authorization Code
7: Register/Change Pre-paid Call Charge
8: Register/Change Call Charge Rate
● Press SPEED button (for only Room Status Type 1).
● Press HOLD/SAVE button.
To check in the guest and change the Room Status from the default values, you should enter
the following information.
To register/change a guest's name,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 1 to register/change guest name.
● Enter the guest's name with the character code.
● Press SPEED button.
● Press HOLD/SAVE button.
Button
Procedures
This feature allows the System Attendant to register/change a guest's name which will be
printed out on the guest's bill when checking out.
Register & Change a Guest Name (Room Status Type 1)
Hotel Operation(GDK)

## Slide 3
Class of Service (Outside Call Restriction) (Room Status Type 2)
When a guest is checked into a room, the system will automatically remove any call barring
restrictions that are set when the room is vacant. The Class of Service is entered into the Room
Status information as 2-digit, the first digit represents the COS for day mode and the second
digit the COS when the system is in night mode.
To change the Class of Service,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 2 to change the Class of Service.
● Dial rooms Day and Night COS (1~7: 2 digits).
● Press HOLD/SAVE button.
Button
Procedures
Guest Alarm Call (Room Status Type 3)
You can set an alarm call for a guest from the Front Desk extension. The alarm call will ring on
the guest's phone and when the call is answered they will receive the system music on hold.
The alarm will ring for 30 seconds and if there is no reply then it will wait for 90sec and try
again. If there is no reply after the third attempt then a "WAKE UP FAIL' alarm will ring on the
attendant and the display will show the extension that the alarm call has failed on.
To set an alarm call from the attendant,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Enter Alarm Call time (HH:MM in 24-hour mode).
● Press SPEED button (for one-time) or # button (for continuous).
● Press HOLD/SAVE button.
Button
Procedures
To change the Intercom Restriction,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 4, the status is changed (toggle setting).
● Press HOLD/SAVE button.
Button
Procedures
It is possible to allow or restrict internal calls from a guest's extension.
Intercom Enable/ Disable (Room Status Type 4)

## Slide 4
Room to Room Call Group (Room Status Type 5)
If a large party of guests are checking into the hotel as a group then it is possible to allow calls
between these guests internally but not allow them to call any other guests in the hotel.
The system will provide up to 100 groups, each of which can have any number of rooms included.
To register/change room to room call group,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 5.
● Enter Room to Room Call Group Number (00~99).
● Press HOLD/SAVE button.
● To remove, press SPEED button.
Button
Procedures
Authorization Code (Room Status Type 6)
The authorization codes can be used for 3 types of operation:
1. If restrictions have been set on the outside lines, then staff and guest will have to dial 9
followed by a valid authorization code before they dial out.
2. If you have Direct Inward System Access(DISA) configured on the system then outside
callers into the switch could be allowed access to other outside lines for dialing out.
3. It is possible to restrict outside calls from Service Stations unless an authorization code has
been entered. It will prevent unauthorized calls being made from unattended Service Stations.
To register/change authorization code,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number or Staff Station Number.
● Press SPEED button.
● Dial 6.
● Enter Authorization Code that you want to use (5 digits).
● Press HOLD/SAVE button.
Button
Procedures
To enter a pre-paid call charge against a guest's room,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 7.
● Dial Pre-paid Call Charge (6 digits).
● Press HOLD/SAVE button.
Button
Procedures
When the guest checks in, a pre-paid call charge can be registered against that room and the
system will keep a check on how much the guest has spent on outside calls. The pre-paid limit
has been reached then a warning tone will be sent to the guest and the call will be disconnected.
Pre-paid Call Charge (Room Status Type 7)
Hotel Operation(GDK)

## Slide 5
Call Charge Rate (Room Status Type 8)
This feature allows system attendant to register Call Charge rate to rooms while check-in.
To assign Call Charge Rate,
● Press TRANS/PGM button.
● Dial 1 0.
● Dial Room Number and press SPEED button.
● Dial 8.
● Dial Call Charge Rate (0~5).
● Press HOLD/SAVE button.
Note: If call charge rate is not assigned, SMDR call charge is applied and after
check-out, the assigned call charge is expired and changed to default value.
Button
Procedures
Baby Listening
A guest can monitor his room at the other place in the hotel. Setting baby listening feature, you
can monitor the room but, the inside of the room cannot hear of you.
To set baby listening at a guest's room,
● Off-hook and dial the guest's room number.
(To cancel, on-hook.)
To operate baby listening at the other places,
● Off-hook and dial the guest's room number twice.
Button
Procedures
To check out a guest,
● Press TRANS/PGM button.
● Dial 1 1.
● Enter the room number.
(To check out a guest with method of payment, press SPEED button and dial
bin no.(credit card no.))
● Press HOLD/SAVE button.
● If you wish to check out more than one guest, dial the next room number.
● Press MON button or hang up.
Button
Procedures
When the guests leave the hotel, it is an easy operation to check them out. The system will
automatically calculate their bill and print it out on the printer. Also, any room status settings
that are applied to the room will be reset to the default values. The system attendant can select
the method of payment among registered ones according to the guest's payment methods.
Check Out

## Slide 6
Room Charge Display & Printing
When a guest checks out or asks for the status of their bill, then it is possible to either display
the current bill on the LCD of the phone or print it out.
To show the current total bill for the guest in the attendant display,
● Press TRANS/PGM button.
● Dial 1 2.
● Dial Room Number.
● The display will show the following information:
Button
Procedures
TOTAL ROOM CHARGE
115 (01) 60.00
Total room charge
● To print out the total charges without any details, press HOLD/SAVE button.
● To print out the total bill for a room, press # button and HOLD/SAVE button.
To print out the Room Status,
● Press TRANS/PGM button.
● Dial 1 3.
● Dial the range of Room Numbers to be printed.
● Press HOLD/SAVE button.
Button
Procedures
Printing a Guest's Room Status
If you do not want guests to be able to dial each other unless they are transferred by the
attendant then, it is possible to block single or multiple rooms.
To enable intercom calls,
● Press TRANS/PGM button.
● Dial 1 4.
● Dial the range of Room Number.
● Press HOLD/SAVE button.
To disable intercom calls,
● Press TRANS/PGM button.
● Dial 1 5.
● Dial the range of Room Number.
● Press HOLD/SAVE button.
Button
Procedures
Intercom Call Enable/Disable
Hotel Operation(GDK)

## Slide 7
By guest's request, system attendant can enable one-time CO call to intercom only station. In
this time, calling station's COS is temporally changed to charged station's COS. The guest can
make only one external call for request.
To enable one-time outside call,
● Press TRANS/PGM button.
● Dial 1 8.
● Dial the room number that the call will be made from.
● Dial the room number that the call will be charged to.
● Press HOLD/SAVE button.
Button
Procedures
To set the LCD language type,
● Press TRANS/PGM button.
● Dial 5 1.
● Dial the range of room number to be changed.
● Dial the language code (0~22/24).
● Press HOLD/SAVE button.
Button
Procedures
The default language is English and if the language is changed then, it will be reset to default
when the guest checks out.
Change LCD Display Language
One-Time CO Call Enable
Language Codes
00: English 01: Korean 02: Italian
04: Swedish 05: Norwegian 06: Finnish
07: Dutch 08: Spanish 10: Danish
11: German 13: Estonia 20: Russian
22 (GDK-162) / 24 (GDK-100/FPII): Portuguese
(In Hotel S/W Version 5.5 or later,)
0: For National Language
1: For English
2: For the second National Language

## Slide 8
Bath Alarm
The system has a facility which can be used to ensure that the front desk is notified when the
guest is in trouble. If the handset is left off-hook for a period of time then, an alarm will ring at
reception and the Front Desk staff can take appropriate action.
To set bath alarm device from System Attendant,
● Press TRANS/PGM button.
● Dial 2 7.
● Dial the station range to be set the bath alarm device.
● Press HOLD/SAVE button.
To release bath alarm device from System Attendant,
● Press TRANS/PGM button.
● Dial 2 8.
● Dial the station range to be set the bath alarm device.
● Press HOLD/SAVE button.
Button
Procedures
To register 'Clean' at a guest station by maid,
● Press TRANS/PGM button.
● Dial 7 8.
To register 'Dirty' at a guest station by maid,
● Press TRANS/PGM button.
● Dial 7 9.
Button
Procedures
Once a guest has checked out of a room, the maid status is automatically changed to 'Dirty'.
Therefore, when the maid has finished cleaning the room, he/she can change the maid status
to 'Clean' from the guest's extension.
Maid Status
To register 'Clean' by system attendant,
● Press TRANS/PGM button.
● Dial 7 8.
● Enter the room range.
● Press HOLD/SAVE button.
To register 'Dirty' by system attendant,
● Press TRANS/PGM button.
● Dial 7 9.
● Enter the room range.
● Press HOLD/SAVE button.
Hotel Operation(GDK)

## Slide 9
Register Bar & Mini-Bar Charge
To register bar charge at Service Station or mini-bar charge at
System Attendant,
● Press TRANS/PGM button.
● Dial 7 1.
● Dial room number of guests to be charged.
● Dial Product Code (2 digits).
● Dial Product Cost (up to 6 digits).
● Press SPEED button.
● Dial HOLD/SAVE button.
Button
Procedures
Guest may pay for charge at service station or mini-bar in time of check-out. Bar terminal
operator registers guest's charge using the following procedure. Mini-bar charge of each room
is registered by only system attendant (Front Desk service station).
To set Room to Room Call Group,
● Press TRANS/PGM button.
● Dial 1 6.
● Dial Group Number (00~99).
● Dial the room range.
● Press HOLD/SAVE button.
● To remove from group as above, dial 1 7 after TRANS/PGM button.
Button
Procedures
If you wish to split the hotel rooms into groups for internal calls, this can be done from system
attendant. Once the groups have been set up then only guests in the same group can call each
other internally.
Room to Room Call Group
To assign room rate at the system attendant,
● Press TRANS/PGM button.
● Dial 1 9.
● Enter the room rate bin no.
● Enter room cost and name.
● Dial HOLD/SAVE button.
Button
Procedures
This feature allows the system attendant to assign room rate among 20 different ones to
individual rooms. This information is included in the Total Room Charge Bill which is printed out
on the SMDR and on check-out.
Room Rate Assign

## Slide 10
Room Rate Assign (Cont’d)
To assign a range of rooms the same room rate,,
● Press TRANS/PGM button.
● Dial 2 0.
● Enter the room range.
● Enter the room rate bin no.
● Dial HOLD/SAVE button.
Button
Procedures
This feature allows the system attendant to assign room rate among 20 different ones to
individual rooms. This information is included in the Total Room Charge Bill which is printed out
on the SMDR and on check-out.
In case a guest checks in and checks out in the same day, part time fee may be charged
according to the room type or hotel policy. Each room type may have up to 6 fields for the
different part time range and fee.
Fee for Part Time
To register/change fee for part time table at system attendant,
● Press TRANS/PGM button.
● Dial 2 4.
● Dial fee for part time (00~31).
● Enter time range. (Press Flex. BTN 1 and dial the time with 4 digits.)
● Enter change rate for the part time. (Press Flex. BTN 2 and dial fixed 3 digits
from 000 to 100.)
● Press HOLD/SAVE button.
● To erase, press SPEED button instead of dialing.
Button
Procedures
To insert Internal Speed Directory at Front Desk,
● Press TRANS/PGM button.
● Dial # 8.
● Enter the station number.
● Enter the name.
● Press HOLD/SAVE button.
● To delete a name in the internal speed directory, press HOLD/SAVE button
after entering station number.
Button
Procedures
This feature will automatically build an internal directory of registered service stations and guests
staying at the hotel from the name information that is entered when they check-in. Once the
name has been added to the list, it is possible to choose a name from the list for dialing and
transferring of calls.
Auto Internal Speed Directory
Hotel Operation(GDK)

## Slide 11
Auto Internal Speed Directory (Cont’d)
To dial by name with Internal Speed Directory,
● Press SPEED button twice.
● Dial 1 for internal speed dial directory.
● Press VOLUME button or dial digits to find a name, then the LCD displays 2
names one on each LCD line.
Or, dialing a character, the first matched name is displayed.
● Press HOLD/SAVE button for dial the name on line 1 or dial 2 and press
HOLD/SAVE button on line 2.
Button
Procedures
This feature will automatically build an internal directory of registered service stations and guests
staying at the hotel from the name information that is entered when they check-in. Once the
name has been added to the list, it is possible to choose a name from the list for dialing and
transferring of calls.
Main Attendant can manipulate Hotel programming. If one multiple station enters hotel feature
programming (except PGM 71,78,79), the others cannot enter the programming mode. Only
error tone is heard with ‘Invalid” message.
Multiple Front Desk (Hotel S/W version 5.5 or later)
Button
Procedures
This feature allows to temporarily override toll restriction and makes a toll call from toll restricted
phone. It is activated by entering feature code and the password before accessing a CO line.
To activate, (It is available on a guest station or service station)
● Press TRANS/PGM button.
● Dial 1 8.
● Enter the password.
● Press HOLD/SAVE button.
● Access a CO line and dial tone will be heard.
New Cabina Call (Hotel S/W version 5.5 or later)
Brief SMDR Print (Hotel S/W version 5.5 or later)
Button
Procedures
The brief SMDR for room or service station can be printed by Front-desk station.
To print SMDR,
● Press TRANS/PGM button.
● Dial 2 6.
● Enter the station range.
● Press HOLD/SAVE button.