## Slide 1
Fixed Feature Buttons
● FLASH button is used to terminate an outside call
and re-seize dial tone without having to hang up
the handset.
● SPEED button provides you with access to speed
dialing, save number redial and last number redial.
● TRANS (TRANSFER) button is used to transfer an
outside call from a station to another.
● CALLBK (CALLBACK) button allows you to leave
a callback indication at a station that is busy,
unattended, or in Do Not Disturb.
● CONF button is used to establish conference calls.
● DND/FWD (Do Not Disturb/Forward) button
allows you to forward your calls to another
destination, or make DND mode.
Quick Reference Guide for Digital Key Telephone
● MUTE button allows you to switch the built in
microphone on or off when using the speakerphone
or the handset microphone when using the handset.
● MON button enables you to make a phone call with
-out lifting handset. It turns the telephone on and off
when using the speakerphone.
● HOLD button enables you to place an outside caller
on hold.
● REDIAL allows you to make last number redial and
auto call number redial.
● ▼ VOLUME ▲ bar allows you to adjust speakerphone
and handset volume.
Call Forward
● Press MON button.
● Press DND/FWD button and dial the desired Call
Forward type.
- 0 : Follow me (not available in GDK-16/20W)
- 1 : Unconditional
- 2 : Busy calls
- 3 : No answer calls
- 4 : Busy/no answer calls
- 5 : Station off-net
- 6 : Incoming outside line to off-net (ATD only)
- 7 : DVU forward for no answer-1(after 4sec)
- 8 : DVU forward for no answer-2
(after predefined time)
- 9 : DVU forward for busy
- # : Cancel previous call forward
● Dial the station number or press DSS button or
intercom group where calls are forwarded.
(Confirmation tone is heard.)
● In GDK-16/20W, only 1 DVIB forward is available.
(DND/FOR + ‘7’: DVU forward for no answer/busy)
● In LDK-300/300E/100/24/20, Forward type 0~7 are
available.
(5 : Station off-net, unconditional
6 : Station off-net, no answer
7 : Incoming outside line to off-net (Sys. ATD only))
To make Call forward to VMIB, press # key after
dialing call forward type (1~4).
Call Wait (Camp-on)
If you dial a busy station, you may alert it to your call.
● After receiving intercom busy tone, dial * or the last
digit of called station number or press DSS button.
● When the called party answers, consult with them
or hang up to transfer the call, if any.
Conference
● Call the desired party (internal or outside). When
called party answers, press CONF button.
● Add next conference party by selecting another
outside line or intercom station.
● When the party answers, press CONF button twice.
All parties are connected.
To terminate a conference,
The conference initiator should be actively in the
conference.
● Hang up, or press CONF button to finish the
conference (only for conference initiator).
Leaving a Message Waiting Indication
If you dial a station that is unattended or in Do
Not Disturb, you can leave a message waiting
indication.
● Dial the desired intercom station. Busy tone or
DND tone is heard.
● Press CALLBK button. The called party’s CALLBK
button LED will flash.
To answer a Message Waiting Indication,
● Press flashing CALLBK button and the station that
left message will be signaled with tone ringing.
● If called station does not answer, press the CALLBK
button once to leave a message.
Placing an Outside Call on Hold
While connected to an outside line,
● Press HOLD/SAVE button.
- Once for system hold
- Twice for exclusive hold
● Reverse if hold preference is programmed to
system hold.
● Press HOLD/SAVE button. (in GDK-16/20W)
CO line call will be put on hold according to the
Hold Preference.
Last Number Redial
The last dialed number on an outside line is saved.
● Press REDIAL button. Or,
● Press SPEED button and dial *.
● In LDK-300/300E/100/24/20, each station with LCD has 10 last dialed number directory.You may find a dialed number by pressing VOLUME key. And press HOLD/SAVE button to dial the number.
Note: The feature which is marked (＊),
is not available in GDK-16/20W.
Quick Ref. Guide

## Slide 2
Save Number Redial (＊)
If you wish to save a number you dialed,
● After dialing the number of an outside party, keep
the handset off-hook.
● Press SPEED button twice.
To dial a saved number,
● Press SPEED button and dial #.
Call Transfer
While connected to an outside call,
● Press TRANS/PGM button.
● Dial station number or DSS button.
(You can select a screened or unscreened transfer.)
Screened Transfer
When that extension answers, announce the transfer
and hang up to complete call transfer.
Unscreened Transfer
When the called extension begins to signal, hang up
to complete call transfer.
Storing Speed Dial Numbers
● Press TRANS/PGM button and then SPEED button.
● Dial the speed number bin.
- Station Speed Number bin:00~19
00~099 (LDK-300/300E/100/24/20)
* 01~20 :GDK-16(ver.1.0~3.0),GDK-20W(ver.1.0~2.0)
* 01~19 :GDK-16(ver. 4.0),GDK-20W(ver.3.0)
- System Speed Number bin :200~999 (GDK-162)
(Attendant programmed) 200~399 (GDK-FPII/100)
21~99 (GDK-16/20W)
2000~4999 (LDK-300)
2000~6999 (LDK-300E)
2000~3499 (LDK-100/24)
2000~2499 (LDK-20)
● Dial the phone numbers to be stored.
● Press HOLD/SAVE button to save the number.
To erase an exiting speed bin,
● Press TRANS/PGM button and then SPEED button.
● Dial speed number bin to be erased.
● Press HOLD/SAVE button.
Dialing a Speed Number
● Press SPEED button and dial the speed number bin.
● When the called party answers, pick up the handset
or use speakerphone.
Voice Over (＊)
It is available when the station has been programmed
with voice over.
● When a busy keyset engaged in an internal or
external call is called through camp-on by a caller,
HOLD/SAVE button of busy keyset is flashing.
● After tone, the busy keyset will be connected to
both parties.
Queuing (＊)
You see that a particular line is busy and want to be
placed on a list waiting for the first line in the group
or station to become available.
● Lift handset or press MON button.
● Press the busy outside line button, specific line
group button or DSS button.
● Pressing CALLBK button, your CALLBK button
is lighting and confirmation tone is heard.
● Hang up or press MON button.
Quick Reference Guide for Digital Key Telephone
Direct Station Select 100~399 (LDK-300)
1000~1599 (LDK-300E)
100~227 (LDK-100)
10~41 (LDK-24)
10~25 (LDK-20)
100~291 (GDK-162)
100~235 (GDK-100)
100~177 (GDK-FPII)
100~115 (GDK-16/20W)
Call Park (＊) 601~619
(GDK-162/LDK-300/300E)
601~610 (GDK-100/LDK-100)
601~608 (LDK-24/20)
601~605 (GDK-FPII)
Call Wait (Camp-on) TRANS/PGM + 8 5
Station Speed Dial SPEED + bin no. (00~19)
000~099 (LDK-300/300E/100/24/20)
* 01~20 :GDK-16(ver. 1.0~3.0),
GDK-20W(ver: 1.0~2.0)
System Speed Dial SPEED + bin no.
2000~4999 (LDK-300)
2000~6999 (LDK-300E)
2000~3499 (LDK-100/24)
2000~2499 (LDK-20)
200~999 (GDK-162)
200~399 (GDK-100/FPII)
21~99 (GDK-16/20W)
All Call Page 4 9 (# 0 in GDK-16/20W
5 4 9 in LDK-300/300E/100/24/20)
Universal Night Answer 6 9
(569 in LDK-300/300E/100/24/20)
Last Number Redial SPEED + *
Save Number Redial(＊) SPEED + #
To erase a flexible button,
● Press TRANS/PGM button.
● Press the flexible button to be erased.
● Press HOLD/SAVE button.
To answer a queue request,
● When the busy outside line button, specific line
group button or DSS button returns to idle, you
hear ringing and the queued line button flashes.
● Lift handset and dial outside line.
Attendant Clock Set
The attendant can set the Time/Date without entering
Admin. Programming.
● Press TRANS/PGM button.
● Dial # 1.
● Enter Date/Time. (YYMMDDHHmm)
If there is no need to change date or time, press *
key.
● Press HOLD/SAVE button.
In GDK-16/20W & LDK-300/300E/100/24/20,
● Press TRANS/PGM button.
● Dial # 1 (0 4 1 in LDK-300/300E/100/24/20).
● Enter Date (YYMMDDHH) and press HOLD/SAVE
button.
● Enter Time (HHmm) and press HOLD/SAVE button.
If there is no need to change date or time, do not dial
current date/time and press HOLD/SAVE button.
Flexible Buttons Programming
● Press TRANS/PGM button.
● Press a flexible button to be programmed.
● See the below chart and dial the desired code.
● Press HOLD/SAVE button.