## Slide 1
KD Series
● KD-36D ● KD-24N
KD-36D : LCD Display, 24 Flexible Buttons
KD-36N : No LCD Display, 24 Flexible Buttons
KD-24D : LCD Display, 12 Flexible Buttons
KD-24N : No LCD Display, 24 Flexible Buttons
Large Digital Key Telephone (You cannot use Large LCD keyset with GDK-16/20W system.)
● KD-33LD ● KD/E-36LD
KD/E Series
● KD/E-36EXE ● KD/E-24ENH ● KD/E-8BTN
KD/E-36EXE : LCD Display, 24 Flexible Buttons
KD/E-36ENH : No LCD Display, 24 Flexible Buttons
KD/E-24EXE : LCD Display, 12 Flexible Buttons
KD/E-24ENH : No LCD Display, 24 Flexible Buttons
KD/E-8 BTN : No LCD Display, 8 Flexible Buttons
Digital Key Telephone Family

## Slide 2
LKD Series (You cannot use LKD-30LD with GDK-16/20W system.)
● LKD-2N/S ● LKD-8D/S ● LKD-30LD
LKD-2N/S: No LCD Display, 2 Flexible Buttons
LKD-8D/S: LCD Display, 8 Flexible Buttons
LKD-30D: LCD Display, 30 Flexible Buttons (Dual LED with Flex. BTN 01~24 & Single LED with 25~30)
LKD-30LD: Large LCD Display, 30 Flexible Buttons (Dual LED with Flex. BTN 01~24 & Single LED with 25~30)
LKD-DSS: 48 Flexible Buttons
※ The LKD series keysets can be normally operated in the following S/W version or later.
GDK-FPII: GS40P-1.2A // GDK-100: GS00P-3.2A // GDK-162: GS86P-5.1A
GDK-FPII: GS40P-1.1Cd // GDK-100: GS00P-3.1Df // GDK-162: GS86P-4.0Ee
KE/C, KD/C Series (CTI is not available with GDK-16/20W system.)
KE/C, KD/C Series keysets have normal functions as KD, KD/E keysets and CTI (Computer
Telephony Integration) function to connect PC (RS-232C Interface Function). Connecting CTI
Module, the KE/C, KD/C keyset operates to transmit/receive data to communicate with PC.
Installation Guide for Connection CTI Module to KE/C, KD/C keyset
1. Connect KE/C, KD/C keyset to KTU port of CTI module with 6-pin line cord.
2. Connect KSU to KSU port of CTI module with 4-pin line cord.
3. Connect the serial port of PC to the serial port of CTI module with 9-pin RS-232C cable.
Digital Key Telephone Family

## Slide 3
Button Arrangement for Digital Key Telephone Family
Large Digital Key Telephone (You cannot use large LCD keyset with GDK-16/20W system.)
● KD-33LD ● KD/E-36LD
KD Series
● KD-36D ● KD-36N ● KD-24D ● KD-24N

## Slide 4
Button Arrangement for Digital Key Telephone Family
KD/E Series
● KD/E-36EXE ● KD/E-24ENH ● KD/E-8BTN
LKD Series
● LKD-8D/S ● LKD-30D