## Slide 1
● Lift handset or press MON button.
● Press outside line button, pool button or dial CO line access
code.
● Dial the desired party.
● When the called party answers, lift handset or use
speakerphone.
Placing an Outside Call
9, 8 +
308A : 1~3
616/36/46 :1~7
Or, 88 +
individual CO line button.
308A : 01~03
36 : 01~12
46 : 01~14
616: 01-06
Answering an Outside Call
Button
Procedures
Range
● Lift handset or press MON button to use speakerphone.
● Press flashing outside line button or loop key.
(If your phone is programmed with Preferred Line Answer,
you may answer by just lifting handset.)
Placing an Intercom Call
Button
Procedures
Range
Button
Procedures
Range
● Dial intercom number or press programmed DSS button.
● You will hear,
- Ring back tone in TN (Tone) mode. Wait for called station
to answer the ringing call.
- 3 bursts of tone in HF(Handsfree) or PV(Privacy) mode.
Begin your announcement after the tone.
Answering an Intercom Call
Button
Procedures
● With your intercom mode setting,
- in TN mode, hear intercom ring. Lift handset.
- in PV mode, hear 3 bursts of tone and one-way announce-
ment. Lift handset to talk.
- in HF mode, hear 3 bursts of tone and announcement. Reply
in handsfree or lift handset for privacy.
Range

## Slide 2
Placing a CO Call on Hold
Button
Procedures
● Press HOLD button.
- Twice for exclusive hold
- Once for system hold
Reverse if hold preference is programmed to system hold.
To retrieve the call on system hold,
● Press the flashing button on system hold to converse.
Range
On GSX/E 8 BTN, GK-8S,
● Press 8 # and two-digit line number on hold.
(Only the station that placed the call on hold can retrieve the
call by dialing 8 *.)
308A : 01~03
36 : 01~12
46 : 01~14
616: 01~06
Button
Procedures
Range
Answering an Intercom Call (Cont’d)
On GSX/E 8 BTN, GK-8S,
● Upon hearing intercom ringing, lift handset to answer.
● You can select either TN or HF mode by dialing 7 6 9 which
makes to toggle in TN and PV mode.
● The 3 bursts of tone is heard in PV mode and confirmation tone
is heard in TN mode.
On GSX/E 8 BTN, GK-8S,
● Only the station that placed the call on hold can retrieve the
call by pressing the flashing line button (if provided), or press
8 9 or 8 # and two-digit line number on hold.
308A : 01~03
36 : 01~12
46 : 01~14
616:01-06
To retrieve the call on exclusive hold,
● Press the flashing button on exclusive hold to converse.

## Slide 3
Call Transfer
Button
Procedures
While connected to an outside call,
● Press TRANS button. (The outside call is put on hold.)
● Dial station number or appropriate DSS button.
● At this point, you can make a screened or unscreened transfer.
When the called extension answers, announce transfer and
hang up to complete call transfer.
While the station you called rings, hang up to complete call
transfer.
To answer screened transfer,
● Your station is signaled according to Intercom Answer Mode
selection.
● Answer the intercom call.
● The transferring party hangs up, the call will be connected.
Range
Screened
Transfer
Unscreened
Transfer
The last dialed number on an outside line is saved.
To redial the number,
● Press REDIAL button. (in GK-24/36)
Or,
● Press SPEED + *. (if it is not programmed)
Save Number Redial
Button
Procedures
Range
If you wish to save a number you dialed,
● After dialing the number of an outside party, keep the handset
off-hook.
● Press SPEED button twice.
● Hang up.
To dial a saved number,
● Press SPEED + #.
Button
Procedures
Range
Last Number Redial

## Slide 4
● Press REDIAL button. (in GK-24/36)
Or, press programmed AUTO REDIAL button in GSX/E keyset.
To program AUTO REDIAL button,
SPEED + SPEED + Flex. button + 7 6 7
On GSX/E 8 BTN, GK-8S,
7 6 * + Flex. button + 7 6 7
● Hang up.
● A busy or no answer number will be redialed automatically
after pre-programmed time interval. (The MON button lights.)
● When called party answers, lift handset and converse.
To program MUTE button,
7 6 * + Flex. button + 7 6 5
● Press the programmed DIAL MEMO button in flex. button.
To program DIAL MEMO button,
SPEED + SPEED + Flex. button + 7 7 4
● Dial the desired number.
● Press DIAL MEMO button again to save.
To dial the dial memo number,
● Press SPEED + #.
To check the dial memo number,
● In idle state, press DIAL MEMO button.
● The saved number is displayed. (only in display phone)
Dial Memo
Button
Procedures
Range
While on an outside line or intercom call, you may enter and save a number in the save number
redial bin for future use.
Button
Procedures
Range
When a user calls a busy or no answer number on an outside line, the system can automatically
redial the number.
Auto Call Number Redial
Mute
Button
Procedures
Range
● Press MUTE button to activate.
● Press MUTE button again to deactivate.
It provides privacy during speakerphone or handset operation by disabling the microphone.
● Press programmed MUTE button to activate.
On GSX/E 8 BTN, GK-8S,

## Slide 5
Queuing
Button
Procedures
Range
● Press a busy outside line button or specific line group button.
● Pressing CALLBK button, your CALLBK button lights and
confirmation tone is heard.
● Hang up or press MON button.
● Press a busy outside line button.
● If you have a programmed CALLBK button in 8-button keyset,
press CALLBK button or, press 7 5 6.
● Hang up or press MON button.
You see that a particular line is busy and want to be placed on a list waiting for the first line in the
group to become available.
On GSX/E 8 BTN, GK-8S,
Button
Procedures
Range
When the busy outside line button or specific line group button
returns to idle,
● You hear ringing and the queued line button flashes.
● Lift handset and press flashing outside line in 15 seconds.
Answering a Queue Request
Button
Procedures
Range
While connected to an outside call,
● Press TRANS button.
● Dial parking location. (700~705)
To retrieve a parked call,
● Lift handset or press MON button.
● Dial * and parking location. (700~705)
Call Park

## Slide 6
● While connected to an outside line, press programmed
FLASH button.
To program FLASH button,
7 6 * + Flex. button + 7 6 4
Flash
Button
Procedures
● While connected to an outside line, press FLASH button.
Range
Disconnects outside line and reseizes dial tone. It can be used to send a timed break recall when
the system is connected with a PBX.
On GSX/E 8 BTN, GK-8S,
To activate speakerphone,
● Press MON button.
● Dial outside line number or intercom number to converse.
Button
Procedures
Range
Pressing an outside line button, a speed button, a station button or dialing a station number will
automatically activate the speakerphone.
Speakerphone
To change access authorization code,
● Dial 7 4 5. (Confirmation tone is heard.)
● Dial your current access authorization code. (Confirmation
tone is heard.)
● Dial your new 4 digits access authorization code.
● Press MON button.
Access Authorization Code
Button
Procedures
To register access authorization code,
● Dial 7 4 4. (Confirmation tone is heard.)
● Dial your own 4 digits access authorization code. (Confirmation
tone is heard.)
● Press MON button. (Confirmation tone is heard.)
Range
To prevent unauthorized outside calling, DISA access or Trunk access on your station by others,
the system provides a means to lock/unlock a station by an access authorization code.

## Slide 7
● Lift handset or press MON button.
● Press DND/FOR button.
● Press the call forward type ;
0 - Unconditional
1 - No answer calls
2 - Busy calls
3 - Busy / no answer calls
4 - Follow me
5 - Off-net (Forward to CO line)
(In GHX-308A, only Unconditional type is available. You
don’t have to select call forward type.)
● Dial station number. (100~699)
( If you select type 5,
Press SPEED button and speed bin number.
Press HOLD button
Or, Press CO button and dial telephone number.
Press HOLD button )
● Hang up.
Button
Procedures
● Dial 7 4 7. (Confirmation tone is heard.)
● MUTE button will flash until restored to normal.
● Press MON button. (You can’t use outside call, just use
intercom call.)
Range
Note : An access authorization code should be registered.
Blocking Outside Calls
Restoring Outside Calls
Button
Procedures
● Dial 7 4 8. (Confirmation tone is heard.)
● Dial your current access authorization code.
(Confirmation tone is heard.)
● MUTE button will extinguish.
Range
Button
Procedures
Range
Call Forward

## Slide 8
● Lift handset or press MON button.
● Dial 7 5 4 or press the programmed DND/FOR button.
To program DND/FOR button,
7 6 * + Flex. button + 7 6 3
● Press the call forward type. (0~5)
(In GHX-308A, just Unconditional type is available. You
don’t have to select call forward type.)
● Dial the station number (100~699) or press the DSS button.
(If you select type 5,
Press SPEED button and speed bin number number.
Or, press CO button and dial telephone number.
● Press HOLD button.
● Hang up.
On GSX/E 8 BTN, GK-8S,
Button
Procedures
Range
To cancel call forward,
● Lift handset or press MON button.
● Press DND/FOR button.
● Hang up or press MON button.
● Lift handset or press MON button.
● Dial 7 5 4 or press the programmed DND/FOR button while
on-hook. (Confirmation tone is heard.)
● Hang up or press MON button.
On GSX/E 8 BTN, GK-8S,
Call Forward (Cont’d)
Button
Procedures
If your phone has been programmed to have Do Not Disturb,
● Press DND/FOR button while on-hook or your phone is ringing.
● The LED lights and your phone is in DND.
● Lift handset or press MON button.
● Dial 7 5 3 or the programmed DND/FOR button.
(Confirmation tone is heard.)
● Hang up.
To remove Do Not Disturb,
● Press DND/FOR button while on-hook.
● The LED extinguishes and DND at your phone is removed.
● Lift handset or press MON button.
● Dial 7 5 3 or the programmed DND/FOR button.
Range
Do Not Disturb
On GSX/E 8 BTN, GK-8S,
On GSX/E 8 BTN, GK-8S,

## Slide 9
Button
● If you are designated as the Executive Station and your
phone is busy or DND (Do Not Disturb), all calls will go to
your Secretary Station.
● If your are designated as the Secretary Station, you may
signal the Executive Station that is in DND by using Call Wait
(Camp-on) feature.
Range
Group Call Pick-up
Button
Procedures
Range
You should be in the same pick-up group as ringing phone and
you have the outside line button or loop button.
● You hear an unattended phone ringing.
● Lift handset or press MON button.
● Dial * * .
Procedures
Executive/Secretary Transfer
Button
Procedures
● You hear intercom or transferred outside line ring at a station
in other pick up group.
● Lift handset or press MON button.
● Dial * and the ringing station number.
● You will be connected to calling party.
Range
Directed Call Pick-up
It is available that you pick up a call on a station in other pick up group.

## Slide 10
● To use Conference feature, you should have the
programmed CONF button in the flexible button.
To program CONF button,
7 6 * + Flex. button + 7 6 1
Conference
Button
Procedures
Range
There are 2 types of conferences;
Add on = 3 internal parties or 1 outside and 2 internal
Multi-line = 1 internal parties and 2 outside parties (Available when multi-line conference is
enabled by admin. programming.)
To establish a conference,
● Call the desired party. (internal or outside)
● Press CONF button. (The called party is put on exclusive hold.)
● Call the next party.
● Press CONF button.
● Conference is established.
To exit a conference (unsupervised),
● Press CONF button in the supervisor station and hang up.
Other parties are still connected.
Re-entering a conference,
● Lift handset or press MON button.
● Press CONF button. When the initiator reenter the
conference, confirmation tone is heard to all the stations in
the conference.
To terminate the conference,
● Hang up or, press CONF button if unsupervised.
On GSX/E 8 BTN, GK-8S,
Button
Procedures
● After receiving intercom busy tone, dial 3.
● Camp-on tone is heard in the called station.
● When called party answers by pressing HOLD button, talk or
hang up to transfer the call.
Range
If you dial a busy station, you may alert or transfer it.
Call Wait (Camp-on)

## Slide 11
Answering a Call Wait
Button
Procedures
● You hear camp-on tone and HOLD button flashes.
● Press HOLD button to talk with the second caller.
The internal line is cut and the CO line is placed on hold.
Range
Call Back
Button
Procedures
● After receiving intercom busy tone, press CALLBK button.
● Hang up.
● When the busy station hangs up, you will be signaled.
● Answer by lifting handset or pressing MON button. The station
you called will be signaled.
● After receiving intercom busy tone, press 7 5 6 or the
programmed CALLBK button.
To program CALLBK button,
7 6 * + Flex. button + 7 6 2
● Hang up or press MON button.
● When the busy station hangs up, you will be signaled.
● Answer the signal by lifting handset or pressing MON button,
and the station you called will be signaled.
Range
If you dial a station that is busy, you can leave a callback indication.
On GSX/E 8 BTN, GK-8S,
Button
Procedures
● After receiving DND tone or no answer, press CALLBK button.
(Confirmation tone is heard.)
● Hang up or press MON button.
● The message indication is left at the called party.
● After receiving DND tone or intercom, press 7 5 6 or, the
programmed CALLBK button.
● Hang up or press MON button.
● The message indication is left at the called party.
Range
Message Waiting
If you dial a station that is unattended or in DND, you can leave a message waiting indication.
Up to 5 messages can be left at a phone.
On GSX/E 8 BTN, GK-8S,

## Slide 12
Button
Procedures
Range
Message Waiting
On GSX/E 8 BTN, GK-8S
Button
Procedures
To store station speed numbers,
● Press SPEED button twice. (Or, SPEED button and desired
CO line button.)
● Dial speed number bin.
● Dial the phone numbers to be stored.
● Press SPEED button. (Confirmation tone is heard.)
In GHX-36/46, by programming 10 station speed numbers
can be added to any station instead of deleting speed number
of the other station. In this case, the speed bin number of the
station is 20 (00~19).
Or,
● Press SPEED button.
● Dial the desired outside line or specific line group button.
● Dial speed number bin (00~19)
● Dial the phone number to be stored.
● Press SPEED button.
● Press MON button.
To use station speed numbers,
● Press SPEED button.
● Dial speed number bin.
To erase station speed numbers,
● Press SPEED button twice.
● Dial speed number bin to be erased.
● Press SPEED button twice.
To program SPEED button,
7 6 * + Flex. button + 7 6 0
Range
Station Speed Bin
308A : 00~19
36 : 00~09
46 : 00~09
616 : 00-19
Station Speed Dial
(Cont’d)
On GSX/E 8 BTN, GK-8S
To answer a message waiting indication,
● Press flashing CALLBK button.
● Station that left message will be signaled with tone ring.
● The MSG lamp and/or the programmed CALLBK button will
flash when a message wait indication has been left for you.
● Lift handset.
● Dial 7 5 6 or press the programmed CALLBK button.
● Station that left message will be signaled with tone ring.
To program CALLBK button,
7 6 * + Flex. button + 762

## Slide 13
Button
Procedures
To register wake-up time,
● Dial 7 4 1 (effective until cancelled) or 7 4 2 (for one-day).
● Dial 4-digit wake-up time (HHMM) in 24-hour mode.
(HH = 00~23, MM = 0~59) (Confirmation tone is heard.)
● Press MON button.
● At wake-up time to be registered, you can hear the wake-up
call.
Range
The system automatically sends ring signal to a station which registers an wake-up time. There are
two kinds of wake-up calls, one is effective for one-day, the other is effective until cancelled.
To cancel wake-up call,
● Dial 7 4 3.
● Confirmation tone is heard and press MON button.
Wake-up
Button
Procedures
● Press SPEED button twice.
● Dial 0 0 and press SPEED button.
● Enter the name up to 7 letters using the codes below.
Range
You can program your phone so people using display phone will see your name instead of your
station number.
● Press SPEED button.
● Hang up or press MON button.
To erase your name,
● Press SPEED button twice.
● Dial 0 0 .
● Press SPEED button twice.
Programming Your Name into Display

## Slide 14
Message Type - II
(It is available for only GHX-36/46/616. You can select
Message Type I or II by programming.)
0 0 : cancel the message
0 1: LUNCH RETURN AT xx:xx (xx:xx : time (4 digits))
0 2 : VACATION RETURN ON xx:xx
(xx:xx : time or date (4 digits)
0 3 : ABSENT, RETURN AT CLK xx:xx (xx:xx : time (4 digits))
0 4 : ABSENT, RETURN AT DATE xx:xx (xx:xx : date (4 digits))
0 5 : OUT OF OFFICE - BACK TOM
0 6 : CALL TO xxxx (max. 12 digits)
0 7 : IN OFFICE xxx (3 digits internal station number)
0 8 : MEETING CLK xx:xx (xx:xx : time (4 digits))
0 9 : AT HOME
1 0 : AT BRANCH OFFICE
1 1~2 0 : Customized messages
● Hang up.
To turn off message display,
● Dial 7 2 + 0 0 .
● Lift handset or press MON button.
● Dial 7 2 .
● Dial the number of desired message. (00~20)
Message Type - I
0 0 Cancel Message
0 1 OUT TO LUNCH
0 2 ON VACATION
0 3 OUT OF OFFICE-BACK AM
0 4 OUT OF OFFICE-BACK PM
0 5 OUT OF OFFICE-BACK TOM
0 6 OUT OF OFFICE-BACK UNKN
0 7 OUT OF TOWN
0 8 IN A MEETING
0 9 AT HOME
1 0 AT BRANCH OFFICE
1 1 ~ 2 0 are used for customized messages which are
programmed by attendant. (See “Creating Customized Message”)
Pre-selected Message
Button
Procedures
Range
You can select a pre-assigned message to be displayed on the LCD of the phone calling the
station.

## Slide 15
In GSX/E-21/33,
There are 2 volume control slide switches located at the front of
the phone. Sliding the switch to the right will increase the volume.
● Right Switch - controls tone ringing volume
● Left Switch - controls voice, speakerphone volume while idle.
In GK-24/36/8S,
● Press Volume button (▼/▲) to adjust ring volume while the
phone is ringing.
● Press Volume button (▼/▲) to adjust speakerphone volume
while speakerphone is working.
● Press Volume button (▼/▲) to adjust handset volume while
you are connected to a CO line.
Volume Control
Button
Procedures
Range
Button
Procedures
● Pressing an outside line button, Loop or Pool button, a station
button, or dialing a number in the Numbering Plan will
automatically active speakerphone and light MON button.
Range
Hot Line
Button
Procedures
● Lift handset or press MON button.
● If you do not dial in preprogrammed interval, hot line feature
is operated automatically.
(Intercom call, CO line selection, CO line group selection,
programmed features in flexible button and Speed dial
features can be programmed as Hot Line Feature.)
● To use this feature, it should be preprogrammed in Admin
programming.
Range
Automatic Selection

## Slide 16
Button
Procedures
● During a CO line conversation, you can be given a periodic
warning signal in every 3 minute.
● To use this function, it should be preprogrammed.
Range
● While on-hook,
● Dial 7 7 3 ( in 36/46/616)/ * 7 3 (in 308A) or press
programmed button.
● Dial 7 7 3 ( in 36/46/616)/ * 7 3 (in 308A) again or press
programmed button to remove music.
Button
Procedures
Range
Background Music
To activate background music, the station should have this privilege by admin. programming.
3-minute Warning

## Slide 17
Changing Intercom Signaling
Button
Procedures
● While calling internal key station, dial * .
● If the called station is in TN mode, the calling signal is
changed from TN mode to HF mode.
● If the called station is in HF or PV mode, the calling signal is
changed to TN mode.
Range
The following functions can be used only in GHX-36/46.
Intercom Transfer
Button
Procedures
While conversing with internal party, (available when intercom
transfer is enabled by programming.)
● Press TRANS button.
● Dial 3-digit station number or press appropriate DSS button.
● At this point, you can make a screened or unscreened transfer.
● If the called station is busy or does not answer, you can
converse with the transferred party again by pressing TRANS
button.
Range
Button
Procedures
If you have been given the ability to make pages,
● Lift handset or press MON button.
● Dial page zone. (See below chart.) And you will hear warning
tone.
● When the tone ends, speak in normal tone.
● Hang up.
Range
All Call : # 0 (Not allowed in GHX-308A)
Internal Zone 1 : # 1 (Not allowed in GHX-308A)
Internal Zone 2 : # 2 (Not allowed in GHX-308A)
Internal All Call : # 5 (Not allowed in GHX-308A)
External Page : # 6
To answer paging,
● Go to the nearest key telephone.
● Dial # 7 (‘# #’ in GHX-308A), and you will be connected to
paging party.
Paging

## Slide 18
● To place an intercom call on hold, the keyset should have
ICM button programmed in a flexible button.
To program ICM button,
SPEED + SPEED + Flex. button + 7 7 6
● While conversing with internal party, press HOLD button.
Button
Procedures
Range
● It is available if ICM button is assigned in a flexible button.
To program ICM button,
7 6 * + Flex. button + 7 7 6
To retrieve an intercom call on hold,
● Press ICM button programmed in flexible button.
You can place an intercom call in hold state using HOLD button.
On GSX/E 8 BTN, GK-8S,
Placing an Intercom Call on Hold

## Slide 19
Direct Station Select station number
Call Park 700~705
Hunt Group 710~717
Dial Memo 7 7 4
Access Authorization
Code
To register 7 4 4
To change 7 4 5
Blocking outside call 7 4 7
Restoring outside call 7 4 8
Account Code Entry 7 5 9
Auto Redial 7 6 7
Preselected Message 7200 ~7220
Universal Night Answer 7 7 7
Loop Key 7 9
ICM Key 7 7 6
Speed Dial
Station Speed Dial SPEED + bin no. (00~19)
System Speed Dial SPEED + bin no. (20~99)
Redial
Last Number Redial SPEED + *
(in GK-24/36) REDIAL
Save Number Redial SPEED + #
Flexible Button Programming
To program flexible buttons,
● Press SPEED button twice.
● Press a flexible button to program.
● See the below table and enter the desired code.
To erase a flexible button,
● Press SPEED button twice.
● Press the flexible button to be erased.
● Press FLASH button.
● Press MON button.
● Lift handset and dial 7 6 * .
● Press a flexible button to program.
● See the below table and enter the desired code.
● Go on-hook.
Button
Procedures
Range
Code for Flexible Button Programming
On GSX/E 8 BTN, GK-8S,
Background Music 7 7 3 (in GHX-36/46/616)
* 7 3 (in GHX-308A)
Alarm Reset 7 7 5 (in GHX-36/46/616)
Outside Line Access
Group Access 9
Group # 1 8 1
Group # 2 8 2
Group # 3 8 3
Group # 4 8 4
Group # 5 8 5
Group # 6 8 6
Group # 7 8 7
(Group #4~#7 are available in only GHX-36/46/616)
Individual Line
Button Assignment for GSX(E), GK-8 button
SPEED 7 6 0
CONF 7 6 1
CALLBK 7 6 2
DND/FOR 7 6 3
FLASH 7 6 4
MUTE 7 6 5
MON 7 6 6