## Slide 1
Fixed Feature Buttons
● FLASH button is used to terminate an outside call
and reseize dial tone without having to hang up
the handset.
● SPEED button provides you with access to speed
dialing, save number redial and last number redial.
● TRANS (TRANSFER) button is used to transfer an
outside call from a station to another.
● CALLBK (CALLBACK) button allows you to leave
a callback indication at a station that is busy,
unattended, or in Do Not Disturb.
● CONF button is used to establish conference calls.
● DND/FOR (FORWARD) button allows you to
forward your calls to another station.
Quick Reference Guide for Analog Key Telephone
● MUTE button allows you to switch the built in
microphone on or off when using the speakerphone
or the handset microphone when using the handset.
● MON button enables you to make a phone call
without lifting handset. It turns the telephone on and
off when using the speakerphone.
● HOLD button enables you to place an outside caller
on hold.
● REDIAL button enables you to redial the last dialed
number.
● HF-P-T allows you to select the Intercom Signaling
Mode. HandsFree, Privacy, or Tone.
● ▼ VOLUME ▲ bar allows you adjust speakerphone
and handset volume.
Call Forward
● Press DND/FOR button and dial the desired Call
Forward type.
- 0 : Unconditional
- 1 : No answer calls
- 2 : Busy calls
- 3 : Busy/no answer calls
- 4 : Follow me
- 5 : Off-net
(In GHX-308A, only Unconditional is available. You
don’t have to select call forward type.)
● Dial the station number.(Confirmation tone is heard.)
(If you select type 5,
Press SPEED button and speed bin number.
Press HOLD button
Or, Press CO button and dial telephone number.
Press HOLD button )
Call Wait (Camp-on)
If you dial a busy station, you may alert it to your call.
● After receiving intercom busy tone, dial 3.
(Camp-on tone is heard in the called station.)
● When the called party answers, converse or hang
up to transfer the call.
Conference
● Call the desired party (internal or outside). When
called party answers, press CONF button.
● Add next conference party by selecting another
outside line or intercom station.
● When the party answers, press CONF button twice.
All parties are connected.
(To make conference with outside parties, multi-line
conference should be enabled.)
To terminate a conference,
The conference initiator should be actively in the
conference.
● Replace the handset or press MON button to off.
Message Waiting Indication
If you dial a station that is busy, unattended, or in Do
Not Disturb, you can leave a message waiting
indication.
● Dial the desired intercom station. Busy tone or
DND tone is heard.
● Press CALLBK button. The called party’s CALLBK
button LED will flash.
To answer a Message Waiting Indication,
● Press flashing CALLBK button. The station that left
message will be signaled with tone ringing.
● If called station does not answer, press the CALLBK
button once to leave a message.
Placing an Outside Call on Hold
While connected to an outside line,
● Press HOLD button.
- Twice for exclusive hold
- Once for system hold
● Reverse if hold preference is programmed to
system hold.
Last Number Redial
The last dialed number on an outside line is saved.
● Press REDIAL button. (GK-24/36) Or,
● Press SPEED button and dial *.
Save Number Redial
If you wish to save a number you dialed,
● After dialing the number of an outside party, keep
the handset off-hook.
● Press SPEED button twice.
To dial a saved number,
● Press SPEED button and dial #.

## Slide 2
Call Transfer
While connected to an outside call,
● Press TRANS button.
● Dial station number or appropriate DSS button.
(You can select a screened or unscreened transfer.)
Screened Transfer
When that extension answers, announce the transfer
and hang up to complete call transfer.
Unscreened Transfer
When the called extension begins to signal, hang up
to complete call transfer.
Storing Speed Dial Numbers
● Press SPEED button twice.
● Dial the speed number bin.
- 00~19 Station Speed Numbers (GHX-308A/616)
00~09 Station Speed Numbers (GHX-36/46)
- 20~99 System Speed Numbers
(Attendant programmed)
● Dial the phone numbers to be stored.
● Press SPEED button.
To erase an exiting speed bin,
● Press SPEED button twice.
● Dial speed number bin to be erased.
● Press SPEED button twice.
Dialing a Speed Number
● Press SPEED button and dial the speed number
bin.
● When the called party answers, pick up the handset
or use speakerphone.
Call Back
If you dial a station that is busy, you can leave a
callback indication.
● After receiving intercom busy tone, press CALLBK
button and hang up.
● When the busy station hangs up, you will be
signaled.
● Answer by lifting handset or pressing MON button.
The station you called will be signaled.
Quick Reference Guide for Analog Key Telephone
Flexible Buttons Programming
● Press SPEED button twice.
● Press a flexible button to be programmed.
● See the below chart and dial the desired code.
● Press HOLD button.
Direct Station Select 100~107 (GHX-308A)
100~127 (GHX-36)
100~139 (GHX-46)
Call Park 700~705
Hunt Group 710~717
Station Speed Dial SPEED + 00~19
(00~09 in GHX-36/46)
System Speed Dial SPEED + 20~99
Universal Night 7 7 7
Answer
Last Number Redial SPEED + *
Save Number Redial SPEED + #
All Call # 0 (Not allowed in GHX-308A)
Internal Zone 1 # 1 (Not allowed in GHX-308A)
Internal Zone 2 # 2 (Not allowed in GHX-308A)
Internal All Call # 5 (Not allowed in GHX-308A)
External Page # 6
Meet Me Page # 7 (## in GHX-308A)
To erase a flexible button,
● Press SPEED button twice.
● Press the flexible button to be erased.
● Press FLASH button.
● Press MON button.
Queuing
You see that a particular line is busy and want to be placed on a list waiting for the first line in the group
to become available.
● Press the busy outside line button or specific line
group button.
● Pressing CALLBK button, your CALLBK button
lights and confirmation tone is heard.
● Hang up or press MON button.
To answer a queue request,
● When the busy outside line button or specific line
group button returns to idle, you hear ringing and
the queued line button flashes.
● Lift handset and press flashing outside line.