## Slide 1
Wake-up Call
To register wake-up call,
● Press TRANS button.
● Dial 4 1. (MON button lights.)
● Dial the station range (6 digits). In case of one station, dial the station number
twice.
● After hearing confirmation tone, enter 4-digit wake-up time (HHmm) in
24-hour mode. (HH= 00~23, mm= 00~59)
● Press HOLD button for ‘one-day’ or dial # and HOLD button for ‘until canceled’.
Button
Procedures
To cancel wake-up call,
● Press TRANS button.
● Dial 4 2. (Confirmation tone is heard and MON button lights.)
● Dial the station range to be cancelled.
● Press HOLD button. (MON button will be extinguished.)
Attendant Intrusion
Button
Procedures
To assign a flexible as an Intrusion button,
● Press TRANS button.
● Press the desired button to be registered.
● Press TRANS button.
● Dial 8 6.
● Press HOLD button.
To activate attendant intrusion,
● Press DSS button corresponding to the busy station you wish to call.
(Busy tone is heard.)
● Press ATD INTRUSION button.
(Intrusion warning tone is heard in the busy station, then a 3-way
conference is set up.)
Attendant may intrude into any station which is in conversation with CO line.

## Slide 2
CO Outgoing Disable
Button
Procedures
To disable outgoing calls a CO line,
● Press TRANS button.
● Dial * 8.
● Press the desired outside line button. (Confirmation tone is heard.)
● After hearing confirmation tone, selected outside line button is disabled.
● Repeat the process to enable the CO line.
Changing Time/Date Format
Button
Procedures
To change the date format on the LCD,
● Press TRANS button.
● Dial * 5.
● The format toggles between DDMMYY and MMDDYY.
(YY : year, MM : month, DD : date)
To change the time format on the LCD,
● Press TRANS button.
● Dial * 6.
● The format toggles between 12-hour mode and 24-hour mode.
(YY : year, MM : month, DD : date)
Button
Procedure
This feature allows the attendant to set the Time/Date without entering Admin Programming.
● Press TRANS button.
● Dial # 1.
● Enter Date + Time. Enter as YYMMDDHHmm.
(YY= Year 00~99, MM= Month 01~12, DD= Date 01~31, HH= Hour 00~23,
mm= minute 00~59)
If there is no need to change date or time, press * key.
(YYMMDD + * or * + HHmm)
● Press HOLD button.
Attendant Clock Set

## Slide 3
Button
Procedures
For station basis,
● Dial * 0.
● Enter the desired station range.
● Press HOLD button.
Accumulated SMDR records will be printed out through the printer connected
to KSU.
For account group basis,
● Dial * 1.
● Enter the desired account group to be printed.
● Press HOLD button.
(Accumulated SMDR records will be printed out through the printer connected
to the KSU.)
To Erase SMDR Records
Button
Procedures
For station basis,
● Dial * 2.
● Enter the desired station range.
(SMDR records will be erased for all stations in the range.)
● Press HOLD button.
For call account group,
● Dial * 3.
● Enter the desired account group.
(SMDR records will be erased for all stations in the range.)
● Press HOLD button.
To display call charge,
● Dial * 4.
● Enter the station number.
● Press HOLD button.
To Print out Accumulated SMDR Records
Customized Message
Button
Procedures
● Press TRANS button.
● Dial * 7.
● Dial the number of the desired message (11~20).
● Enter the desired message using the codes.
(Refer to P.43 English Character Set)
● Press HOLD button.

## Slide 4
Temporary COS Change
To activate temporary COS change,
● Press TRANS button.
● Dial # 2.
● Enter the station range.
● Press HOLD button.
Button
Procedures
A station user can change the class of service to lower class temporarily to prevent unauthorized
use of the station by others. (5-digit authorization code must be set at the station to be locked first.)
To remove temporary COS change,
● Press TRANS button.
● Dial # 3.
● Enter the station range.
● Press HOLD button.
● Press TRANS button.
● Dial # 4.
● For DVU, dial 0 1 for announcement 1, dial 0 2 for announcement 2, or 0 3
for announcement 3. (Announcement 3 is played back when the called party
is busy.)
● For EDVU, you have 31 (01~31) system greetings.
1~9 : for Hunt or company information with DISA
10 : for Invalid message
11 : for Timeout message
12 : for Try again message
13 : for Transfer to attendant message
14 : for Leave message
15 : for Record message
16 : for Enter authorization message
17 : for MOH message
18 : for Busy message
20 : Station Off-net Call Forward message
● Press # key (to record with DKTU) or ＊ key (to record with external MOH)
after hearing the message.
● Record your greeting and press HOLD button to finish the recording.
To delete,
● Press TRANS button.
● Dial # 4.
● Dial the system greeting number (01~31) and the message is heard.
● While the message is heard, press DND/FOR button.
● Confirmation tone is heard and the message is deleted.
Button
Procedures
It provides announcements for Hunt service (UCD/Circular/Terminal) or DISA and only the
system attendant can record this message.
System Greetings

## Slide 5
Traffic Analysis
Button
Procedures
To start the traffic analysis at system attendant,
● Press TRANS button.
● Dial # 7 1.
● Press HOLD button.
To stop the traffic analysis at system attendant,
● Press TRANS button.
● Dial # 7 2.
● Press HOLD button.
To print the result of traffic analysis at system attendant,
● Press TRANS button.
● Dial # 7 3.
● Press HOLD button.
To abort printing at system attendant,
● Press TRANS button.
● Dial # 7 4.
● Press HOLD button.
The system will monitor the system and record various traffic data which can be printed upon
request. The information can be used to determine whether the circuits installed in the system are adequate.
When enabled, it will continue to monitor the traffic until disabled. The traffic data is collected and sent to the RS-232C port upon request. The collected traffic data contains two types of traffic data. The first type is peg counts which give an actual count of the number of times a particular operation has occurred. Peg counts are given in absolute values from 00000 to 99999. The second type of data is usage times which give the average percent occupancy of a device, I.e., stations, CO lines, DTMF receivers, etc. Usage times are given in seconds from 00000 to 99999.
Counts and times are cumulative from the time the monitoring is activated, and are reset by initiating the start up procedure again.
To activate/deactivate Day/On-demand/Night mode manually,
● Press DND/FOR button at attendant station.
● Then, DND/FOR button is flashing. (The system is placed in On-demand mode.)
● Pressing DND/FOR button once more, the system is placed in Night mode.
● On-demand mode is not activated automatically.
Button
Procedures
The attendant station can be placed into night service mode allowing ring assignments and
answering privileges to stations not having the privileges in the day mode. Or, can be placed into
On-demand service mode allowing ring assignments and answering privileges to station not
having the privileges in the night mode.
Day/On-demand/Night Mode Service (Manual/Automatic)

## Slide 6
Button
Procedures
● Press SPEED button.
● Dial speed number bin.
A group of speed dial numbers can be stored within the system for access by allowed stations.
These numbers provide speedy access to often used outgoing CO dialing numbers.
GDK-162 : 200~999
100 : 200~399
FPII: 200~299
Intercom Box BGM Selection by Attendant
Button
Procedures
To set ICM box music,
● Press TRANS button.
● Dial * 0.
● Dial the music channel (0,1,2).
● Press HOLD button.
The attendant can select the music channel source to an ICM box.
Erasing Station Message
Button
Procedures
The attendant can cancel the features , DND CALL FORWARD and preselected message active
at other station.
● Press TRANS button.
(TRANS button flashes and the MON button lights steadily.)
● Dial * 9.
● Dial the desired station range to be canceled.
● Press HOLD button.
(Confirmation tone is heard and the station goes to idle status automatically.)
System Speed Dial
Day/On-demand/Night Mode Service (Manual/Automatic) (Cont’d)
To change Day/Night mode automatically,
● Press TRANS button.
● Dial # 9.
● Enter DAY TIME + NIGHT TIME, or DAY TIME + * or NIGHT TIME + * .
(Enter as HHmm (HH= hour 00~23, mm= minute 00~59)
● Press HOLD button.
Button
Procedures

## Slide 7
Attendant DSS Operation /Placing an Intercom Call from the DSS
Button
Procedures
● Lift handset or press MON button. (MON button lights.)
● Press the desired DSS station button.
● Hang up or press RELEASE key to terminate the call.
Making a Page
Button
Procedures
● Lift handset or press MON button.
● Press PAGE button.
● Speak in normal voice tone to deliver message.
● Hang up or press RELEASE button.
Transferring an Outside Line to Another Station
Button
Procedures
● While connecting an outside line, press the desired DSS station button.
● You can wait to announce the transfer or,
● Hang up or press RELEASE button.
Intercom Group Call
Button
Procedures
● Lift handset or press MON button.
● Press the programmed INTERCOM GROUP CALL button.
● The call is connected to an idle station in the group.
Overriding a Key Telephone in Do Not Disturb
Button
Procedures
● Press DSS button of the station to be overridden. (DND tone or busy tone is
heard.)
● Press programmed OVERRIDE button.

## Slide 8
Index
A
Access Authorization Code..................................... 41
Answering a Call Wait with Voice Over ................. 38
Answering an Intercom Call ................................... 32
Answering an Outside Call .................................... 31
Answering a Queue Request ................................. 36
Auto Call Number Redial ....................................... 35
B
Background Music ................................................. 45
Blocking Outside Calls ........................................... 42
C
Call Back ...........................................................… 38
Call Forward ......................................................… 39
Call Park ............................................................... 44
Call Transfer ......................................................... 33
Call Wait ............................................................... 38
Changing Intercom Answer Mode ......................… 31
Conference ........................................................… 37
D
Dial Memo .........................................................… 34
Directed Call Pick-up .........................................… 37
Do Not Disturb ...................................................… 40
E
Executive/Secretary Transfer .............................…36
F
Flash ..................................................................… 45
G
Group Call Pick-up ............................................… 36
L
Last Number Redial ............................................... 34
M
Message Waiting ................................................... 38
Mute ................................................................….. 35
P
Paging .............................................................….. 44
Placing a CO Call on Hold ...............................….. 32
Placing an Intercom Call ..................................….. 32
Placing an Intercom Group Call ............................. 31
Placing an Intercom on Hold .............................…. 33
Placing an Outside Call .....................................…. 31
Pre-selected Message .......................................... 43
Programming Your Name into Display ...............… 43
Q
Queuing .......................................................….. 35
R
Restoring Outside Calls .................................... 42
S
Save Number Redial ......................................... 34
Speakerphone ................................................... 45
Station Speed Dial ............................................. 41
Step Call ............................................................ 36
U
Universal Night Answer ..................................… 45
V
Voice Announcement …………………………….. 52
Voice Over ....................................................…. 33
W
Wake-up Call ..................................................... 42
Attendant Operation
Attendant Clock Set ……………………………… 50
Attendant DSS Operation .............................…. 55
Attendant Intrusion ............................................ 49
Changing Time/Date Format .............................. 50
CO Outgoing Disable ......................................... 50
Customized Message ....................................…. 51
Day/On-demand/Night Mode Service ................. 53
Erasing Station Message ..............................…. 54
Intercom Box BGM Selection by Attendant ........ 54
System Greetings ..............................................52
System Speed Dial ............................................ 54
Temporary COS Change ................................... 52
To Erase SMDR Record .................................... 51
To Print out Accumulated SMDR Records ......... 51
Traffic Analysis ..............................................…. 53
Wake-up Call .................................................… 49