## Slide 1
● Lift handset or press MON button.
● Press outside line button, pool button or dial CO line access
code.
● Dial desired party.
● When called party answers, lift handset or use speakerphone.
● When the line is busy or no answer, press SPEED button and
dial 1 digit to be replaced with the last digit for step call.
Placing an Outside Call
9, 8 +
162 : 01~48
100 : 01~24
FPII: 01~09
Or, 88 +
162 : 01~96
100 : 01~48
FPII: 01~34
Answering an Outside Call
Button
Procedures
Range
● Lift handset or press MON button to use speakerphone.
● Press flashing outside line button or loop key.
(If your phone is programmed with Preferred Line Answer,
you may answer by just lifting handset.)
Placing an Intercom Group Call
Button
Procedures
Range
To make an intercom group call,
● Lift handset or press MON button.
● Dial the intercom group number.
162 : 620~649
100 : 620~634
FPII: 620~627
Button
Procedures
Range
● Press TRANS button.
● Dial 4 9.
● Dial 1 for Handsfree, 2 for Tone ring, or 3 for Privacy announce.
● Press HOLD button.
Button
Procedures
Range
Changing Intercom Answer Mode

## Slide 2
Button
Procedures
Range
● Dial intercom number or press programmed DSS button.
● You will hear,
- Ring back tone in TN (Tone) mode. Wait for called station
to answer the ringing.
- 3 bursts of tone in HF(Handsfree) or PV(Privacy) mode.
Begin your announcement after the tone.
Answering an Intercom Call
Button
Procedures
● With your intercom answer mode setting,
- in TN mode, hear intercom ring. Lift handset.
- in PV mode, hear 3 bursts of tone and one-way announce-
ment. Lift handset to talk.
- in HF mode, hear 3 bursts of tone and announcement. Reply
handsfree or lift handset for privacy.
Range
Placing a CO Call on Hold
Button
Procedures
● Press HOLD button.
- Twice for exclusive hold
- Once for system hold
Reverse if hold preference is programmed to system hold.
To retrieve the call,
● Lift handset and press flashing outside line button.
Range
Placing an Intercom Call
On GSX/E 8 BTN, GK-8S,
To retrieve the call,
● Press 8 # # or press 8 # + line no.
162 : 01 ~ 96
100 : 01 ~ 48
FPII : 01 ~34

## Slide 3
Placing an Intercom on Hold
● The GSX/E keyset should be programmed a flex. button
as an ICM button.
To program an ICM button,
TRANS + Flex. button + TRANS + 8 3 + HOLD
● While on an intercom call, press programmed ICM button
or HOLD button.
● The ICM button flashes and you will hear intercom dial tone.
To retrieve intercom call on hold,
● Press the flashing ICM button and lift handset.
Call Transfer
Button
Procedures
While connected to an outside call,
● Press TRANS button. (The outside call is put on hold.)
● Dial station number or appropriate DSS button.
● At this point, you can make a screened or unscreened transfer.
When the called extension answers, announce transfer and
hang up to complete call transfer.
While the station you called rings, hang up to complete call
transfer.
To answer screened transfer,
● Your station is signaled according to Intercom Answer Mode
selection.
● Answer the intercom call.
● The transferring party hangs up, the call will be connected.
Range
STA No.
162 : 100~291
100 : 100~235
FPII: 100~177
Screened
Transfer
Unscreened
Transfer
Voice Over
Button
Procedures
● When a busy keyset engaged in an internal or external call is
called through camp-on by a caller, HOLD button of busy
keyset is flashing.
After tone, the busy keyset will be connected to both parties.
● Press HOLD button in busy keyset to converse with new caller.
● Press HOLD button in busy keyset again to alternate the call.
Range
This feature provides voice announcement to a busy station without interrupting the existing
conversation. The announcement is received over the existing conversation so that only the
busy station hears both incoming parties.
Button
Procedures
Range

## Slide 4
Last Number Redial
The last dialed number on an outside line is saved.
To redial the number,
● Press REDIAL button. (in GK-24/36 or if it is programmed in
GSX/E)
To program a REDIAL button,
TRANS + Flex. button + TRANS + 8 8 + HOLD
Or,
● Press SPEED + *.
Save Number Redial
Button
Procedures
Range
If you wish to save a number you dialed,
● After dialing the number of an outside party, keep handset
off-hook.
● Press SPEED button twice.
● Hang up.
To dial a saved number,
● Press SPEED + #.
Button
Procedures
Range
Dial Memo
Button
Procedures
Range
● Press the programmed DIAL MEMO button.
To program a DIAL MEMO button,
TRANS + Flex. button + TRANS + 8 0 + HOLD
● Dial the desired number.
● Press DIAL MEMO button again to save.
To dial the dial memo number,
● Press SPEED + #.
To check the dial memo number,
● In idle state, press DIAL MEMO button.
● The saved number is displayed. (in only display phone)
While on an outside line or intercom call, you may enter and save a number in the save number
redial bin for future use.

## Slide 5
Button
Procedures
Range
● Press REDIAL button.
The GSX/E keyset should be programmed a flexible button
as a REDIAL button.
● Hang up.
● A busy or no answer number will be redialed automatically
after pre-programmed time interval. MUTE button and MON
button light.
● When called party answers, press MUTE button to converse.
When a user calls a busy or no answer number on an outside line, the system can
automatically redial the number.
Mute
Button
Procedures
Range
● Press MUTE button to activate.
● Press MUTE button again to deactivate.
It provides privacy during speakerphone or handset operation by disabling the microphone.
Auto Call Number Redial
Queuing
Button
Procedures
Range
● Lift handset or press MON button.
● Press busy outside line button or specific line group button.
● Pressing CALLBK button, your CALLBK button lights and
confirmation tone is heard.
● Hang up or press MON button.
● If you have a programmed CALLBK button in 8 button, press
CALLBK button, or press 5 6.
● Hang up.
You see that a particular line is busy and want to be placed on a list waiting for the first line in the
group to become available.
● Press programmed MUTE button to activate.
On GSX/E 8 BTN, GK-8S,
On GSX/E 8 BTN, GK-8S,

## Slide 6
Answering a Queue Request
Button
Procedures
● If you are designated as the Executive Station and your phone
is busy or DND (Do Not Disturb), all calls will go to your
Secretary Station.
● If your are designated as the Secretary Station, you may signal
the Executive Station that is in DND by using Call Wait (Camp
-on) feature.
Range
Step Call
Button
Procedures
Range
● Call desired internal party.
● After hearing ICM busy tone, dial the last digit of desired
intercom party in the same 10’s group.
(ex. If station “112” is busy, dial digit “4” to call station “114”.)
● It can be used to external call by pressing SPEED button
and the last digit.
Group Call Pick-up
Button
Procedures
Range
You should be in the same pick-up group as ringing phone.
● You hear an unattended phone ringing.
● Lift handset or press MON button.
● Dial 6 6.
Executive/Secretary Transfer
Button
Procedures
Range
When the busy outside line button or specific line group button
returns to idle,
● You hear ringing and the queued line button flashes.
● Lift handset and dial the number.
When an extension is busy, you can make a call to a different station by dialing only the last
digit of the new extension number.

## Slide 7
Directed Call Pick-up
Button
Procedures
● You hear intercom or transferred outside line ring at a station.
● Lift handset or press MON button.
● Dial 7 and the ringing station number.
● You will be connected to the calling party.
Range
162 : 100~291
100 : 100~235
FPII: 100~177
Conference
Button
Procedures
Range
To establish a conference,
● Call desired party (internal or outside).
● Press CONF button. (CONF button lights and the called party
is put on exclusive hold.)
● Call the next party.
● Press CONF button twice. (once if adding additional parties)
● Conference is established.
To add on another party,
● Press CONF button.
● Call the next party.
● Press CONF button twice.
To exit a conference (unsupervised),
● Press CONF button in the supervisor station and hang up.
Other parties are still connected.
Re-entering a conference,
● Lift handset or press MON button.
● Press CONF button.
To drop an outside party,
(You should be actively in the conference.)
● Press outside line of party you wish to drop.
● Hang up or press MON button.
To terminate the conference,
● Hang up or, press CONF button if unsupervised.
● To use Conference Feature, you should have the
programmed CONF button in the flexible button.
On GSX/E 8 BTN, GK-8S,

## Slide 8
Call Wait (Camp-on)
Button
Procedures
● After receiving intercom busy tone, dial “*” , last digit of called
station number, or press DSS button.
● Camp-on tone is heard in called station.
● When called party answers, talk or hang up to transfer the call.
Range
If you dial a busy station, you may alert it of your call.
Answering a Call Wait with Voice Over
Button
Procedures
● You hear camp-on tone and HOLD button is flashing.
● Press HOLD button to talk with the second caller.
The first caller is placed on hold.
● You will be connected to the first caller when the second caller
hangs up.
Range
Call Back
Button
Procedures
● After receiving intercom busy tone, press CALLBK button.
● After receiving intercom busy tone, press TRANS + 5 6 or,
the programmed CALLBK button.
● Hang up.
● When the busy station hangs up, you will be signaled.
● Answer the signal by lifting handset or pressing MON button,
the station you called will be signaled.
Range
If you dial a station that is busy, you can leave a callback indication.
On GSX/E 8 BTN, GK-8S,
Button
Procedures
● If the called party does not answer, press CALLBK button.
● At that time, CALLBK LED of the called station flashes.
● After receiving intercom busy tone, press TRANS + 5 6 or,
the programmed CALLBK button.
● Hang up.
Range
On GSX/E 8 BTN, GK-8S,
Message Waiting

## Slide 9
Button
Procedures
● Lift handset or press MON button.
(The MON button lights.)
● Press DND/FOR button.
● Press the call forward type;
0 - Follow me
1 - Unconditional
2 - Busy calls
3 - No answer calls
4 - Busy / no answer calls
5 - Station off-net
6 - Incoming outside line to off-net (system attendant only)
7 - DVU forward - 1 (forwarded after 4 sec)
8 - DVU forward - 2 (forwarded after predefined time)
● Dial station number or press DSS button or intercom group
where calls are to be received.
(In case of Follow-me, dial authorization code after station
number.)
● Confirmation tone is heard and DND/FOR button is flashing
on forwarded station.
● Hang up.
- In case Follow-me, it should be programmed from the station
that you will be forwarded to i.e. if your extension is 102 and you
are forwarding to 104, then you will need to go to 104 to
program the feature. Also, this feature requires authorization
code and requires system programming.
- In case Station Off-net, the number you are forwarding to
should be saved as a speed dial number first.
If EDVU/DVIB is installed, System Greeting 20 will be heard and
Station off-net call forward will be activated.
- In case Incoming outside line to Off-net, it requires system
programming.
Range
Button
Procedures
To answer a message waiting indication,
● Press flashing CALLBK button.
● Station that left message will be signaled with tone ring.
● The MSG lamp and/or the programmed CALLBK button will
flash when a message wait indication has been left for you.
● Lift handset.
● Dial 5 7 or press the programmed CALLBK button.
● Station that left message will be signaled with tone ring.
Range
Message Waiting (Cont’d)
Call Forward
Sta. No.
162 : 100~291
100 : 100~235
FPII: 100~177
INT. Group
162 : 620~649
100 : 620~634
FPII : 620~627
On GSX/E 8 BTN, GK-8S,

## Slide 10
If your phone has been programmed to have Do Not Disturb,
● Press DND/FOR button while on-hook or your phone is ringing.
● The LED lights and your phone is in DND.
● Lift handset or press MON button.
● Dial 5 3 or the programmed DND/FOR button.
(You will hear confirmation tone.)
● Hang up.
To remove Do Not Disturb,
● Press DND/FOR button while on-hook.
● The LED extinguishes and DND at your phone is removed.
● Lift handset or press MON button.
● Dial 5 3 or the programmed DND/FOR button while on-hook.
To cancel call forward,
● Lift handset or press MON button.
● Press DND/FOR button and dial #.
● Hang up.
- To cancel incoming outside line to off-net (at system attendant),
Press MON + DND/FOR + Line Group No. + #
Call Forward (Cont’d)
Button
Procedures
Range
● Lift handset or press MON button.
● Dial 5 4 or press the programmed DND/FOR button.
● Press the call forward type.
● Dial the station number or press the DSS button.
● Hang up.
● Lift handset or press MON button.
● Dial 5 4 # or press the programmed DND/FOR button while
on-hook.
● Hang up.
Button
Procedures
Range
Do Not Disturb
On GSX/E 8 BTN, GK-8S,
On GSX/E 8 BTN, GK-8S,
On GSX/E 8 BTN, GK-8S,
On GSX/E 8 BTN, GK-8S,

## Slide 11
Button
Procedures
To store station speed numbers,
● Press TRANS button.
● Press SPEED button.
● Dial speed number bin. (00~19)
● Dial the phone numbers to be stored.
● Press HOLD button.
● Enter name for Dial by Name. (optional)
Or,
● Press SPEED button.
● Dial speed number bin. (00~19)
● Press desired outside line or specific line group button.
● Dial the phone number to be stored.
● Press HOLD button.
To use station speed numbers,
● Lift handset or press MON button.
● Press SPEED button.
● Dial speed number bin. (00~19)
To use system speed numbers,
● Lift handset or press MON button.
● Press SPEED button.
● Dial speed number bin.
To erase station speed numbers,
● Press TRANS button.
● Press SPEED button.
● Dial speed number bin to be erased.
● Press HOLD button.
Range
System Speed
bin
162 : 200~999
100 : 200~399
FPII: 200~399
Station Speed Dial
To change access authorization code,
● Press TRANS button and dial 4 5.
● Dial your current access authorization code. You will hear
confirmation tone.
● Dial your new 5 digits access authorization code.
● Press HOLD button. (Confirmation tone is heard.)
Access Authorization Code
Button
Procedures
To register access authorization code,
● Press TRANS button and dial 4 4. (MON button lights.)
● Dial your own 5 digits access authorization code.
● Press HOLD button. (Confirmation tone is heard.)
Range
To prevent unauthorized outside calling, DISA access or Trunk access on your station by others,
the system provides a means to lock/unlock a station by an access authorization code.

## Slide 12
Button
Procedures
● Press TRANS button and dial 4 6. (MON button lights.)
● Press HOLD button. (Confirmation tone is heard.)
● MUTE button will flash until restored to normal.
Range
Note : An access authorization code should be registered.
Blocking Outside Calls
Restoring Outside Calls
Button
Procedures
● Press TRANS button and dial 4 7.
● Dial your current access authorization code.
(Confirmation tone is heard.)
● MUTE button will be extinguished.
Range
Button
Procedures
To register wake-up time,
● Press TRANS button.
● Dial 4 1 and 4-digit wake-up time (HHMM) in 24-hour mode.
(HH = 00~23, MM = 00~59)
● Press HOLD button for “one-day” or dial # and HOLD button
for “until cancelled”. (Confirmation tone is heard.)
Range
The system automatically sends ring signal to a station which register a wake-up time. There are
two kinds of wake-up call, one is effective for one-day, the other is effective until cancelled.
To cancel wake-up call,
● Press TRANS button and dial 4 2.
● Press HOLD button. (Confirmation tone is heard.)
Wake-up Call

## Slide 13
Button
Procedures
● Press TRANS button.
● Press SPEED button and dial 0 0.
● Dial the desired phone number.
● Press SPEED button.
● Enter the name up to 7 letters using the codes below.
Range
You can program your phone so people using display phone will see your name instead of your
station number.
● Press HOLD button.
Programming Your Name into Display
Pre-selected Message
Button
Procedures
● Press TRANS button and dial 7 7.
● Dial the number of desired message. Date, Time or Station
Number, if required.
● Press HOLD button.
0 1 LUNCH, RTN HH:MM
0 2 ON VACATION/RTN DATE (MM:DD)
0 3 OUT OF OFFICE/RTN TIME (HH:MM)
0 4 OUT OF OFFICE/RTN DATE (MM:DD)
0 5 OUT OF OFFICE/RTN UNKNOWN
0 6 CALL : XXXXX
0 7 IN OFFICE/STA XXXX
0 8 IN A MEETING/RTN TIME (HH:MM)
0 9 AT HOME
1 0 AT BRANCH OFFICE
# to cancel
1 1 ~ 2 0 are used for customized messages which are
programmed by attendant. (See “Creating Customized Message”)
Range
You can select a pre-assigned message to be displayed on the LCD of the phone calling
the station.
To turn off message display,
● Press flashing DND/FOR button.

## Slide 14
Button
Procedures
If you have been given the ability to make pages,
● Lift handset.
● Dial page zone. (See below chart.) And you will hear warning
tone.
● When the tone ends, speak in normal tone.
● Hang up.
GDK-162 GDK-100 GDK-FPII
Range
All Call 4 9 4 9 4 9
Internal Zone 1 4 0 1 4 0 1 4 0 1
: : :
Internal Zone 05 4 0 5 4 0 5 4 0 5
: :
Internal Zone 15 4 1 5 4 1 5
: :
Internal Zone 20 4 2 0
Internal All Call 4 3 4 3 4 3
External Zone 1 4 6 4 6 4 6
External Zone 2 4 7 4 7 -
External All Call 4 8 4 8 4 8
To answer paging,
● Go to the nearest key telephone.
● Lift handset and dial 4 4, and you will be connected to paging
party.
Paging
Button
Procedures
Range
While connected to an outside call,
● Press TRANS button.
● Dial parking location.
To retrieve a parked call,
● Lift handset or press MON button.
● Dial parking location.
162 : 601~619
100 : 601~610
FPII : 601~605
Call Park

## Slide 15
Button
Procedures
● Lift handset or press MON button.
● Press flashing outside line button. If an outside line button is
not assigned, dial 6 9.
● You will be connected to ringing outside line.
Range
● Press TRANS button.
● Dial 7 3.
Button
Procedures
Range
Background Music
Flash
Button
Procedures
● While connected to an outside line, press FLASH button.
Range
Disconnects outside line and reseizes dial tone. It can be used to send a timed break recall when
the system is connected with a PBX.
Universal Night Answer
Speakerphone
To activate speakerphone,
● Press MON button.
● Dial outside line number or intercom number to converse.
Button
Procedures
Range
Pressing an outside line button, a speed button, a station button or dialing a station number will
automatically activate the speakerphone.

## Slide 16
Voice Announcement
Time Prompt;
● Dial 6 7 1.
● You will hear the time prompt, “Time is XX : XX PM.”
Date Prompt;
● Dial 6 7 2.
● You will hear the time prompt, “Date is December, 20th.”
Station Number Prompt;
● Dial 6 7 3.
● You will hear the station number prompt, “This is station XXXX.”
Button
Procedures
Range
Record your greeting,
● Dial 6 7 4 (The message is heard after 4sec) or 6 7 0 (The
message is heard after predefined time).
● To stop recording, press MON button or HOLD button.
(MON button: erased automatically after 48 hours
HOLD button: remained until canceled)
● After recording your greeting message, a caller will hear your
greeting message when you do not answer the call within a
predetermined time (PGM 43-BTN 24).
Delete your greeting,
● Dial 6 7 5.
Playback your greeting,
● Dial 6 7 6. (You will hear our greeting message.)
Station status prompt;
● Dial 6 7 7. (You will hear below list (a-h). c-g items will be
omitted if not active.)
a) Station number XXXX
b) Listed message X
c) Wake-up time XXXX AM or PM
d) Do not disturb
e) Forwarded to station XXXX
f) Forwarded to speed bin XXX
g) Locked (temporary COS change)
h) COS X
Record your paging message,
● Dial 6 7 8.
● Lift handset to record your paging message.
● Press HOLD button.
Confirm your paging message,
● Dial 6 7 9.
● The paging message is heard.
Activate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FOR button.
● Dial 7 or 8 (Select DVU Forward type 1 or 2).
● Go on-hook.
Deactivate Call Forward to DVU,
● Lift handset or press MON button.
● Press DND/FOR button.
● Dial # .
● Go on-hook.

## Slide 17
Voice Announcement (Cont’d)
Button
Procedures
Range
Listen to the recorded message,
● Press the flashing CALLBK button.
● The recorded message is heard with the time and date.
● Pressing HOLD button, the current message is saved and the
next message is heard.
● Pressing CALLBK button, the recorded message is heard from
the first.
● Pressing CONF button, the current message is deleted.
On GSX/E 8 BTN, GK-8S,
● If a DVU message is left, the MSG lamp is flashing.
● Dial 5 7 or press programmed CALLBK button to listen to the
recorded message.
● The recorded message is heard and then the message is
automatically deleted.
● Pressing HOLD button while the message is played, the next
message is heard. (The current message is placed to the last.)
● Pressing programmed CALLBK button, the recorded message
is heard from the first.
● If you don’t press HOLD button any more, the current message
is deleted and other messages are remained.

## Slide 18
Flexible Button Programming
To program flexible buttons,
● Press TRANS button.
● Press a flexible button to program.
● See the below table and enter the desired code.
● Press HOLD button.
To erase a flexible button,
● Press TRANS button.
● Press the flexible button to be erased.
● Press HOLD button.
Button
Procedures
Range
Code for Flexible Button Programming
Direct Station Select station number
162 :100~291
100 :100~235
FPII:100~177
Call Park parking location
162 :601~619
100 :601~610
FPII:601~605
Hunt Group internal hunt group
162 :620~649
100 :620~634
FPII:620~627
Dial Memo TRANS + 8 0
Call Wait (Camp-on) TRANS + 8 5
Wake-up
To register TRANS + 4 1
To cancel TRANS + 4 2
Paging Refer to p. 44
Access Authorization Code
To register TRANS + 4 4
To change TRANS + 4 5
Blocking outside call TRANS + 4 6
Restoring outside call TRANS + 4 7
Pre-selected Message TRANS + 7 7
Background Music TRANS + 7 3
Intercom Hold TRANS + 8 3
Universal Night Answer 6 9
Loop button TRANS/PGM + 8 4
Speed Dial
Outside Line Access
Group access 9
Group #1 8 0 1
Group #2 8 0 2
: :
Group #48 8 4 8
(Available up to Group #24 for GDK-100)
Individual Line Access 8 8 + Line No.
162 : 01~96
100 : 01~48
FPII: 01~34
Button Assignment for GSX/E, GK-8 button
SPEED TRANS + 9 0
CONF TRANS + 9 1
CALLBK TRANS + 9 2
DND/FOR TRANS + 9 3
FLASH TRANS + 9 4
MUTE TRANS + 9 5
MON TRANS + 9 6