## Slide 1
SCM Compact V2.4.0 Configuration Guide
Distribution
English
Ver.1.0

## Slide 2: History
Version | Date | Changes
1.0 | 2019.01 | Initial version for V2.4.0.x
Notes: Note

## Slide 3
| [Intercom2] One Way Mode
| [Intercom2] Forced Disconnect
※ This function was tested in SMT-I 5343 T04.10
| ACD Call Pickup
| SBC] Request URI Change
Notes: 3

## Slide 4
[Intercom2] One Way Mode

## Slide 5: [Intercom2] One Way Mode
The One Way Mode for Intercom (receiver) is set to ‘One Way Mode’ in the [CONFIGURATION > Service > User Service > Intercom] menu.
※ The callee of intercom answer the call automatically and can only hear as the MUTE key turns on.
Notes: Note

## Slide 6
[Intercom2] Forced Disconnect

## Slide 7: [Intercom2] Forced Disconnect
The ‘Forced Disconnect’ mode for Intercom Extension Number is set to ‘Forced Disconnect’ in the [CONFIGURATION > Service > User Service > Intercom] menu.
This feature applies only to the using for intercom KEY of Phone Key Programming.
If there is an intercom call in the conversation state when new intercom KEY is pressed, the existing intercom call ends and new intercom call proceeds.
※ This is valid only when the existing intercom call generated through KEY and is not applicable to manual operation.
Notes: Note

## Slide 8: [Intercom2] Forced Disconnect
Your can not set different ‘Forced Disconnect’ value on one Extension Number.
If you try to set different value on same Extension Number, It will be failed with pop-up information in Admin.
Notes: Note

## Slide 9
ACD Call Pickup

## Slide 10: ACD Call Pickup
To pickup ACD Group Call, ‘ACD Group Call Picku’ is set to ‘Enable’ in the [CONFIGURATION > User Group > Change User Group > Options] menu.
Notes: Note

## Slide 11
[SBC] Request URI Change

## Slide 12: [SBC] Request URI 변경
The Request URI Change function is set to ‘Request URI’ and ‘Request URI String’ in the [CONFIGURATION > Network > SBC > Policy] menu.
Notes: Note

## Slide 13: [SBC] Request URI 변경
The Operator can change Request URI information for Host or User Info.
in the [CONFIGURATION > Network > SBC > Policy] menu.
Notes: Note

## Slide 14: End of document